## Slide 1: Time Freq. Measurement Mechanism & Procedure
Date: 2012-07-16
Authors:

## Slide 2: Abstract
Enhanced Power Saving (PS) mechanisms are supposed to be included, as per FRD.
An accurate Time-Frequency Measurement Mechanism & Procedure (TFM2P) for improving the effectiveness of existing PS features is proposed.
TFM2P can be especially useful in case of lower traffic but numerous sensors or meters (use case 1) requiring battery conservation.

## Slide 3: Principle of PS feature
Synchronize peer nodes to TSF
Schedule or Trigger for STA wake-up
Doze as long as possible for peer nodes to queue
Awake as short as possible to communicate quickly
Accuracy of TSF sync does set the duty ratio ,
; for small
c.f. Peer to peer clock frequency accuracy=40ppm,
(1) = (36ms / 15min) + 40 = 40 + 40 ppm
(2) = (360us / hour) + 40 = 0.1 + 40 ppm
or = (3.6ms / 10 hour) +40 = 0.1 +40 ppm

## Slide 4: Potential of PS improvement by TFM2P
Wake-up Scheduling;
(1) △=40ppm, = 80ppm, means PS loss of half.
(2) △=40ppm, = 40.1ppm, means PS loss of ten times.
Wake-up margin
for accuracy tolerance
Sender
(e.g. TSF master)
Receiver
(e.g. TSF slave)
awake
sleep again
scheduled wake-up time
actual doze duration

## Slide 5: Wake-up accurately by TFM2P
Wake-up Scheduling;
(1) △compensated=4ppm, = 44ppm ; ~doubly improved
(2) △compensated=4ppm, = 4.1ppm ; ~ten-times improved
scheduled wake-up time
Less wake-up margin
by timer frequency accuracy compensation
awake
sleep again
actual doze duration
Sender
(e.g. TSF master)
Receiver
(e.g. TSF slave)

## Slide 6: Time Measurement (1)
Timing Measurement Procedure; 10.23.5 (IEEE802.11-2012)

## Slide 7: Time Measurement (2)
Timing Measurement Procedure; 10.23.5 (IEEE802.11-2012)
Need std’ed mechanism of ToD/ToA time stamp
Proposed Measurement Point for both ToD/ToA
  Either end of STF or start of LTF : tLTF
Proposed ToA validation by Sig with no CRC error
  Every detection of tLTF is stored (over written) if CRC passed.
By TFM2 Procedure
  ToA stamp of frame destined to the node itself only be used.
Hardware assist does help !

## Slide 8: Frequency Measurement (1)
Two time measurements apart each other as specified are used to calculate each time offsets.
            dot11MgmtOptionTimingMsmtActivated (existing)
t1=ToD(M1)
t4=ToA(Ack)
t5=ToD(M2)
t8=ToA(Ack)
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2=ToA(M1)
t3=ToD(M1)
t6=ToA(M1)
t7=ToD(M1)
t1and t4 are known
t5and t8 are known
offset1=[(t2-t1)-(t4-t3)]/2
offset2=[(t6-t5)-(t8-t7)]/2
Sending STA(f1)
Receiving STA(f2)

## Slide 9: Frequency Measurement (2)
Two time offsets apart each other as specified are finally used to estimate frequency difference.
            dot11MgmtOptionFrequencyMsmtActivated (New)
t1=ToD(M1)
t4=ToA(Ack)
t5=ToD(M2)
t8=ToA(Ack)
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2=ToA(M1)
t3=ToD(M1)
t6=ToA(M1)
t7=ToD(M1)
offset1=[(t2-t1)-(t4-t3)]/2
offset2=[(t6-t5)-(t8-t7)]/2
Sending STA(f1)
Receiving STA(f2)
f1⧋
f2 =
f2= f1

## Slide 10: Effective combination with existing PS scheme
AP TSF accuracy advertise can help with TFM2P (11-12/130r0)
TSF as a base, DTIM, TBTT in BSS ( AP, STA), MBSS and TDLS.
Existing PS scheme;
        PS-Mode
        (U-APSD)
        S-APSD
        (U-PSMP)
        S-PSMP
        SM-PS static/Dynamic
        WNM-Sleep mode
        (TDLS Peer u-APSD)
        TDLS Peer PMS
        TXOP PS-mode
        FMS / TIM Broadcast / TFS

## Slide 11
Straw poll (1)
Do you support …
to include “Time & freq. measurement procedure” in Slide 9 as an enhanced PS feature into specification framework document?
  Yes
  No
  Abstain

## Slide 12
Straw poll (2)
Do you support …
to include “Hardware time stamp function of ToD and ToA for existing IEEE802.11-2012 time measurement mechanism” into specification framework document?
  Yes
  No
  Abstain

## Slide 13: References
[1] 11-12/130r0 “Beacon Reception of Long Sleeper”
[2] IEEE802.11-2012
[3] IEEE1588/PTP
[4] 11-11/0905r5” TGah Functional Requirements and Evaluation Methodology Rev. 5”
[5] PAR and 5C

## Slide 14: Examples

## Slide 15: Frequency Measurement (example 1)
f1⧋ =
f2 = =
= 10000000
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578901-1234567890)-(1234667890-1234678901)]/2
= 11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627477-1235616466)-(1235716466-1235727477)]/2
= 11011
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
No frequency error
Propagation Delay=0
f2= f1 = f1

## Slide 16: Frequency Measurement (example 2)
f1⧋
f2= f1 = f1
f2 = =
= 10000000
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578902-1234567890)-(1234667892-1234678902)]/2
= (11012+11010)/2=11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627478-1235616466)-(1235716468-1235727478)]/2
= (11012+11010)/2=11011
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
No frequency error
Propagation Delay=1uSec

## Slide 17: Frequency Measurement (example 3)
f2 = =
= 10000038.15
f2= f1 = 1.000003815 f1
f1⧋ =
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578902-1234567890)-(1234667892-1234678902)]/2
= (11012+11010)/2=11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627482-1235616466)-(1235716468-1235727482)]/2
= (11016+11014)/2=11015
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
f2 frequency offset ≈ 4ppm
Propagation Delay=1uSec

## Slide 18: Frequency Measurement (example 4)
f2 = =
= 10000076.29
f2= f1 = 1.000003815 f1
f1⧋ =
38.15
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578902-1234567890)-(1234667892-1234678902)]/2
= (11012+11010)/2=11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627482-1235616466)-(1235716468-1235727482)]/2
= (11016+11014)/2=11015
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
f1,f2 frequency offset ≈ 4ppm
Propagation Delay=1uSec

## Slide 19: End