## Slide 1: PS Mode Enhancements with Timing Indication
Date: 2012-07-11
Authors:

## Slide 2: Abstract
We consider an enhancement of the PS mode in
802.11ah to save energy and message exchanges in case of pending data at the AP side

## Slide 3: Introduction
One of the use cases of 802.11ah includes sensors and meters that transmit at low rate over long distances to an AP [1],[2]
Energy efficiency is a key metric in wireless systems
  Increases lifetime of battery powered nodes
  Reduces electricity bills of nodes with renewable energy supply
Energy efficiency of sensor networks that must be deployed for several years is of paramount importance
  STAs should sleep as much as possible and only wake up to transmit data
  Redundant message exchanges should be eliminated

## Slide 4: Downlink Traffic Indication
An AP indicates the existence of downlink traffic through the TIM in the Beacon frame [3]
A STA waking up from its PS mode seeing its TIM bit set transmits a PS-Poll to the AP requesting data

## Slide 5: PS-Poll Message
The AP responds with an ACK, a DATA frame or sends no response to a PS-Poll
ACK can indicate:
  The existence of DATA (TIM bit was set)
  The lack of DATA (PS Poll was sent without receiving TIM) [4]
According to PS-Mode, a STA stays awake until it receives
  The DATA
  Another Beacon Frame whose TIM indicates that AP does not have any buffered DATA
If TIM bit in next Beacon is set STA sends another PS-Poll

## Slide 6: Response to a PS-Poll Message
If a DATA frame is received by STA
  The STA ACKs the frame
If no response is received
  PS-Poll is lost
  The STA will retransmit the PS-Poll at a later time
If an ACK is received by the STA
  The AP may be unable to send the packet immediately
  Postpones transmission at a later time
    But does not send any indication about when the DATA will be sent

## Slide 7: Responding an ACK to a PS-Poll
An AP responds with an ACK even in the absence of downlink DATA [4]
  When DATA is not available at the AP
  When DATA is available at the AP
The STA still has to wait awake for the DATA to come
Can be a considerably long time in loaded network
Beacon
Beacon
PS
Poll
ACK
BU=1
DATA
Awake
Doze
Doze
AP
STA
Awake
Awake
Beacon
Beacon
PS
Poll
ACK
BU=0
Awake
Doze
Doze
AP
STA
Awake
Awake

## Slide 8: Active/Doze State Timing Indication
STA can switch between Active/ Doze States after a PS-Poll
If the AP knew a Doze/Active state transition pattern for the STA after sending the ACK
  The STA can go to sleep according to the pattern
  The AP can transmit the packet when the STA is expected to be active

## Slide 9: Active/Doze State Timing Indication
STA can indicate a time when it goes to Doze state
  This time can be relative
      E.g., t time units or t beacon intervals (short or long) ahead of time
  Time can also be absolute and based on e.g., a global clock
  STA may also indicate a DRX pattern of on/off periods
    A default pattern may be defined
    It may be chosen from a set of possible patterns
  PS-Poll timing indication can improve the energy efficiency of the STA

## Slide 10: Example 1
STA starts a DRX pattern after the ACK with DATA indication until the next Beacon
  Remains active for a smaller period of time
  Saves energy by sleeping more
Beacon
Beacon
PS
Poll
ACK
BU=1
DATA
Awake
Doze
Doze
AP
STA
Awake
Doze
Doze
Awake
Awake
Doze
Awake
Awake

## Slide 11: Example 2
The pattern can be replaced by Doze state if all the DATA have been delivered by the AP
Beacon
Beacon
PS
Poll
ACK
BU=1
DATA
Awake
Doze
Doze
AP
STA
Awake
Doze
Doze
Awake
Awake
Doze
Skips DRX pattern and goes Doze state if AP indicates no more data
Awake
Awake

## Slide 12: Conclusions
Energy efficiency is of paramount importance in sensor applications
We proposed an enhancement of the PS Poll message that can improve the energy consumption of the STAs

## Slide 13: References
[1] 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document
[2] 11-11-0905-05-00ah-tgah-functional-requirements-and-evaluation-methodology
[3] 802.11 REVmbD.12.0
[4] 11-12-0127-01-00ah-lowe-power-medium-access

## Slide 14: Straw Poll
Do you support the idea that a STA indicates timing information such as a DRX pattern to the AP to further improve the energy savings?
Y: N: A: