## Slide 1: AID reassignment for TIM and non-TIM modes switching
Date: 2012-07-13
Authors:
Name | Affiliations | Address | Phone | email
Xun Yang (Sunny) | Huawei |  |  | yangxun.yang@huawei.com
Betty Zhao | Huawei |  |  | betty.zhao@huawei.com
David Xun Yang | Huawei |  |  | David.yangxun@huawei.com
Osama Aboul-Magd | Huawei |  |  | Osama.Aboulmagd@huawei.com
Young Hoon Kwon | Huawei |  |  | younghoon.kwon@huawei.com
George Calcev | Huawei |  |  | George.calcev@huawei.com
Yongho Seok | LG Electronics |  |  | 
Seunghee Han | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jinsam Kwak | LG Electronics |  |  | 
Matthew Fischer | Broadcom |  |  | 
Eric Wong | Broadcom |  |  | 
Simone Merlin | Qualcomm |  |  | 
Zhi Quan | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 

## Slide 2
Name | Affiliations | Address | Phone | email
Yong Liu | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Raja Banerjea | Marvell |  |  | 
Minyoung Park | Intel Corp. |  |  | 
Tom Tetzlaff | Intel Corp. |  |  | 
Emily Qi | Intel Corp. |  |  | 
Thomas Kenney | Intel Corp. |  |  | 
ChaoChun Wang | MediaTek |  |  | 
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Ponnampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Sun, Bo | ZTE |  |  | 
Lv, Kaiying | ZTE |  |  | 
Huai-Rong Shao | Samsung |  |  | 
Chiu Ngo | Samsung |  |  | 
Minho Cheong | ETRI |  |  | 
Jae Seung Lee | ETRI |  |  | 
Heejung Yu | ETRI |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Chittabrara Ghosh | Nokia |  |  | 
Esa Tumaala | Nokia |  |  | 
Authors:

## Slide 3: Introduction
“11ah STAs can choose not to have a TIM entry for the DL traffic signalling.” “11ah STAs shall inform AP if they do not need a TIM entry for the DL signalling during the association process.” [1]
So a STA shall be in one of the two modes: TIM mode (with a TIM entry) or non-TIM mode (without a TIM entry).
- STAs that are not low power and/or have delay-sensitive DL traffic may choose TIM mode.
- STAs that are low power and/or have delay-tolerant DL traffic may choose non-TIM mode.
Some STAs may need to switch between TIM mode and non-TIM mode during operation.
- E.g. The smart meters on intelligent appliances: When the appliance is on, the smart meters need to be in TIM mode to receive control messages from AP. When the appliance is off, the smart meters need to be in non-TIM mode to save power.

## Slide 4: Problem
TIM bitmap sent by AP need not to contain the bits of non-TIM STAs.
But it’s unavoidably to mix the non-TIM STAs bits into all other bits of TIM bitmap when the STAs change their TIM/non-TIM mode.
- In the figure, if AP needs to indicate DL data for STA 1, 2, 3 and 5 after STA 5 changing from non-TIM mode to TIM mode, the length of TIM bitmap is 7 bits.
STAs having a TIM entry
STAs without a TIM entry
Vacant TIM bits
Bit 1 STA 1 | Bit 2 STA 2 | Bit 3 | Bit 4 STA 3
Bit 5 STA 4 | Bit 6 | Bit 7 STA 5 | Bit 8 STA 6
Bit 1 STA 1 | Bit 2 STA 2 | Bit 3 | Bit 4 STA 3
Bit 5 STA 4 | Bit 6 | Bit 7 STA 5 | Bit 8 STA 6

## Slide 5: Proposed Solution
To reduce the size of TIM bitmap sent by AP (i.e. excluding non-TIM STAs bits), the bits of non-TIM STAs and the bits of TIM STAs should be always in separated parts of TIM bitmap.
If the bits of STAs in TIM mode and non-TIM mode are mixed after the STA changing mode, AP should reassign the STA a new AID.
- In the figure, AP reassigns STA 5 a new AID corresponding to Bit 3 in TIM bitmap after STA 5 changing from non-TIM mode to TIM mode. If AP needs to indicate DL data for STA 1, 2, 3 and 5, the length of TIM bitmap is 4 bits.
When the size of TIM bitmap reaches hundreds of bits, AID reassignment will be more helpful for TIM compression.
STAs having a TIM entry
STAs without a TIM entry
Vacant TIM bits
Bit 1 STA 1 | Bit 2 STA 2 | Bit 3 | Bit 4 STA 3
Bit 5 STA 4 | Bit 6 | Bit 7 STA 5 | Bit 8 STA 6
Bit 1 STA 1 | Bit 2 STA 2 | Bit 3 STA 5 | Bit 4 STA 3
Bit 5 STA 4 | Bit 6 | Bit 7 | Bit 8 STA 6

## Slide 6: Proposed Solution
3 methods for AP to reassign AID when the STA switches between TIM mode and non-TIM mode.
- Use reassociation request/response command
- Use TIM mode switch request/response command (new commands)
- Use PS-Poll or trigger frame
The general process is
- STA sends reassociation request or TIM mode switch request to AP, or indicates the request in PS-Poll or trigger frame, when it wants to change the TIM/non-TIM mode.
- AP replies reassociation response or TIM mode switch response with a new AID. The STA uses the new AID in the future operations.
- If AP cannot reassign STA a new AID, AP only replies an ACK to STA.
- The format of above frames are TBD.

## Slide 7: Straw Poll 1
Do you support that STA can switch between TIM mode (STAs have a TIM entry) and non-TIM mode (STAs do not have a TIM entry) during operation?

## Slide 8: Straw Poll 2
Do you support that AP may reassign a new AID to STA when it switches between TIM mode and non-TIM mode ?

## Slide 9: References
[1] 11-11-1137-09-00ah-specification-framework-for-tgah