## Slide 1: Requirements on WLAN Cellular Offload
Date: 2012-09-18
Authors:

## Slide 2: Abstract
We have proposed a new activity to improve system capacity to support important applications of WLAN such as cellular data offload.
This presentation gives some background information why we think capacity enhancement is necessary and summarizes the requirements for the WLAN cellular offload.

## Slide 3: Introduction
Mobile data traffic
  Due to wide spread of smartphones, explosion of mobile data traffic has been recognized.
  The amount of mobile data traffic is anticipated to increase of more than 10 times in the next several years.
  Cellular data offload will be more important for the WLANs in the near future.
Current situations
  2.4 GHz band: Almost saturated in many places because
    only three non-overlapping channels are available
    huge amount of data exchanged by increased number of devices
    many operators deploy their hotspot APs, especially in the urban areas, that results very dense deployment of APs
      11-1413-r3 shows that 25% of airtime is occupied by beacon, probe request or probe response frames.
  5 GHz band: Not utilized so much.

## Slide 4: Issues
Significant interference observed in the 2.4 GHz band which results in poor user experience.
  It is sometimes very difficult just to connect to an AP in Tokyo area.
The 5 GHz band will also be very crowded in near future.
  Recent smartphones, tablets and Ultrabooks start to support the 5 GHz band.
  802.11ac will extend the bandwidth/channel and there may be less number of non-overlapping channels.
  In many countries, not all of the channels in 5 GHz band are always available due to the DFS Requirements and limitation of the indoor use.
  As a result, many BSSs in the 5 GHz band may be using the same channel.
As an operator, we need to improve user experience of our customers

## Slide 5: Requirements for the cellular data offload
WLANs need to provide better user experience compared to the cellular systems in terms of data rate, cost effectiveness, etc.
Requirements in 12/910r0 Carrier Oriented Wi-Fi for Cellular Offload by Laurent (ORANGE) contains many of the requirements.
We also think it very important to enhance the system capacity to support huge amount of data traffic. Hopefully, the system capacity shall be increased in proportional to the number of APs where densely deployed.

## Slide 6: Recent activities
Promote the use of 5 GHz band - on going activities:
  The 802.11ac will accelerate the use of 5 GHz band.
  Operators extensively deploying their hotspot APs supporting the 5 GHz band in places where available.
  Some mechanisms for this purpose such as fast session handover between 2.4 GHz and 5 GHz bands have been discussed outside the IEEE 802.11.
Observation
  The above activities will provide near term solutions to improve user experiences of cellular offload.
  However, there are still remaining issues that should be resolved in IEEE 802.11 community.

## Slide 7: Topics for IEEE 802.11 Standardization
Proposed standardization activity
Interference Management/Alignment/Coordination
to enhance the system capacity, and
to improve the flexibility for WLAN area configuration
  Benefits of having the interference management/coordination:
    By mitigating the effect of interference, communication quality will also be improved
    Although the concept of TXOP defined in 802.11e provides a kind of fairness, we can discuss additional consideration for it.
  Drawback
    Additional complexity is expected.

## Slide 8: Proposed Goals
Reduced Interference:
  This is something we would like to have. It might, however, be difficult to explain quantitatively.
  We need clear performance criteria that can be measured easily.
Examples of performance criterion:
  Stability, Fairness:
    These are very important features. But it will be difficult to set a goal that everybody agree.
  Throughput, System Capacity:
    Criterion that can be understood easily.
10 G bit/s of system capacity will be more understandable and acceptable for many people

## Slide 9: Summary
In order to support the use case of cellular offload,
  Near term solution
    Promote the use of 5 GHz band
    Some on-gong activities outside the IEEE 802
  Appropriate topics for the IEEE 802.11 community
    Capacity enhancement by interference management
    Proposed goal: to achieve 10 G bit/s of system capacity
Thank you very much!

## Slide 10: References
802.11-11-1464-02-0wng-the-better-spectrum-utilization-for-the-future-wlan-standardization
802.11-12-0068-00-0wng-discussion-on-resource-utilization
802.11-12-0910-00-0wng-Carrier-Oriented-WiFi-Cellular-Offload
802.11-12-0820-00-0wng-improved-spectrum-efficiency-for-the-next-generation-wlans