## Slide 1: WLAN Standardization in 3GPP A Tutorial
Date: 2012-09-18
Authors:

## Slide 2: Abstract
Overview of WLAN standardization
in 3GPP

## Slide 3: Agenda
3GPP Introduction
History of WLAN Interworking Projects
  Interworking
  Network Selection and Discovery
  Security
  Mobility
  Policy and charging control
Current Projects
Conclusions

## Slide 4: Overview of 3GPP
The 3rd Generation Partnership Project (3GPP) unites six telecommunications standard development organizations (ARIB, ATIS, CCSA, ETSI, TTA, TTC), known as “Organizational Partners”, and provides their members with a stable environment to produce the Reports and Specifications that define the global mobile technology
Market Representation Partners: IMS Forum, TD-Forum, GSA, GSM Association, IPv6 Forum, UMTS Forum, 4G Americas, TD SCDMA Industry Alliance, InfoCommunication Union, Small Cell Forum, CDMA Development Group, Cellular Operators Association of India (COAI), and NGMN Alliance
Global responsibility for IMS (IP Multimedia Subsystem)
Policy and Charging Control (PCC) for other access technologies: 3GPP2, ETSI TISPAN, etc.
Extensive re-use of IETF and OMA protocols
Co-operation with IETF, BBF, ITU, OMA, etc.

## Slide 5: 3GPP WG Structure
The Four Technical Specification Groups (TSGS) in 3GPP are:
  GSM EDGE Radio Access Networks (GERAN)
  Radio Access Networks (RAN)
  Service & Systems Aspects (SA)
  Core Network & Terminals (CT)
Each of the four TSGs has a set of Working Groups, which meet regularly four to six times a year
Each TSG has its own quarterly Plenary meeting where the work from its WGs is presented for information, discussion and approval
Each TSG has a particular area of responsibility for the Reports and Specifications within its own Terms of Reference
Working in three stages:
  Stage 1 defines requirements;
  Stage 2 defines architecture: and
  Stage 3 defines protocol level details
Study phase for technical solutions evaluation, feasibility, comparison and conclusion.
Work phase is to specify the normative specifications most often based on the output from the study phase.
Notes: Skip it

## Slide 6: 3GPP WG Details and Links
TSG GERAN GSM EDGE Radio Access Network | TSG RAN Radio Access Network | TSG SA Service & Systems Aspects | TSG CT Core Network & Terminals
GERAN WG1 Radio Aspects GERAN WG2 Protocol Aspects GERAN WG3 Terminal Testing | RAN WG1 Radio Layer 1 spec RAN WG2 Radio Layer 2 spec Radio Layer 3 RR spec RAN WG3 lub spec, lur spec, lu spec UTRAN O&M requirements RAN WG4 Radio Performance Protocol aspects RAN WG5 Mobile Terminal Conformance Testing | SA WG1 Services SA WG2 Architecture SA WG3 Security SA WG4 Codec SA WG5 Telecom Management | CT WG1 MM/CC/SM (lu) CT WG3 Interworking with external networks CT WG4 MAP/GTP/BCH/SS CT WG6 Smart Card Application Aspects
Groups active in WLAN Interworking
http://www.3gpp.org

## Slide 7: History of 3GPP - WLAN Interworking
3GPP first focused on an Interworking solution with WLAN technology in Release 6 (2004) including support for access to IMS (IP Multimedia Subsystem) and PS (Packet Services) over WLAN access
More complete incorporation of WLAN as part of non-3GPP connection to the Evolved Packet Core (EPC) in Release 8 (2008) – “the LTE release”
In Release 10 (2010), the EPS (Evolved Packet System) architecture was enhanced with support for non-seamless WLAN offload, which allows the operator to dynamically or statically configure the UE (User Equipment = mobile device) with inter-system routing policies that assist a dual-radio UE in selecting an IP interface with per-flow granularity
Policy and QoS enhancements for WLAN access to the EPC (in co-operation with BBF) in Release 11 (2011)
Support of trusted WLAN access without UE impacts in Release 11 (2011)
More ongoing work in Release 12 (2012)
Note: CS access is not discussed in this presentation.

## Slide 8: 3GPP Technical Specifications for WLAN Interworking
Stage 1
  TS 22.234 Requirements on 3GPP system to Wireless Local Area Network (WLAN) interworking
Stage 2
  TS 23.234 3GPP system to Wireless Local Area Network (WLAN) interworking; System description
  TS 33.234 3G security; Wireless Local Area Network (WLAN) interworking security
  TS 23.402 Architecture enhancements for non-3GPP accesses
  TS 33.402 3GPP System Architecture Evolution (SAE); Security aspects of non-3GPP accesses
  TS 23.261 IP flow mobility and seamless Wireless Local Area Network (WLAN) offload; Stage 2
  TS 23.327 Mobility between 3GPP-Wireless Local Area Network (WLAN) interworking and 3GPP systems
Stage 3
  TS 24.234 3GPP system to Wireless Local Area Network (WLAN) interworking; WLAN User Equipment (WLAN UE) to network protocols; Stage 3
  TS 24.302 Access to the 3GPP Evolved Packet Core (EPC) via non-3GPP access networks; Stage 3
  TS 24.312 Access Network Discovery and Selection Function (ANDSF) Management Object (MO)
  TS 24.327 Mobility between 3GPP Wireless Local Area Network (WLAN) interworking (I-WLAN) and 3GPP systems; General Packet Radio System (GPRS) and 3GPP I-WLAN aspects; Stage 3
Notes: Quick skip

## Slide 9: WLAN Interworking in Release 6
The first 3GPP interworking solution with WLAN technology

## Slide 10: 3GPP - WLAN Networking Components
Packet Data Gateway (PDG)
  3GPP PS based services (appear the first time in Scenario 3) are accessed via a Packet Data Gateway
  “GGSN”-like functionality i.e. charging data generation, IP address management, tunnel endpoint, QoS handling, service based local policy enforcement
Wireless Access Gateway (WAG)
  A gateway via which data to/from the WLAN AN shall be routed via a PLMN through a selected PDG in order to provide a WLAN UE with 3G PS based services
  Charging data generation, routing enforcement
3GPP AAA Server/Proxy
  All AAA related tasks, and relaying when needed
HSS / HLR (Home Subscriber Server / Home Location Register)
  Located within the 3GPP subscriber's home network
  Contains required authentication and subscription data to access the WLAN-IW service
OCS / CCF / CGw (Online Charging System / Call Control Function / Charging Gateway )
  Charging data collection, accounting, online charging, etc.
Notes: skip

## Slide 11: Access Types
WLAN 3GPP IP Access
  Authorized subscribers access Packet Switched (PS) services, e.g. 3GPP IMS service, using a secure tunnel
  Since WLAN hotspots are generally not considered secure, an IPSec tunnel between the UE and the Packet Data Gateway (PDG) is needed for accessing 3GPP IP Access service
  Wireless APN (Access Point Name), similar to GPRS APN, but for WLAN access
  Multiple tunnels can be authorized for previously authenticated subscribers allowing access to any number of services simultaneously
  A separate tunnel authentication is needed
WLAN Direct IP Access
  Authorized subscribers access local IP networks such as the Internet or Intranet directly from the WLAN
  The 3GPP AAA Server performs authentication of subscriber requests from RADIUS and Diameter WLAN ANs, using either the EAP-SIM (Extensible Authentication Protocol-Subscriber Identity Module) or EAP-AKA (Extensible Authentication Protocol-Authentication and Key Agreement) protocol
  The 3GPP based authentication is performed against the subscriber information in the HSS. Authentication is initiated directly from the WLAN AN (Access Network)
  After successful authentication, authorization is performed, resulting in the return of policy information to the WLAN AN to provision the session. Subscriber access is provided only to the local IP network such as the Internet or Intranet directly from the WLAN AN
Notes: skip

## Slide 12: 3GPP - WLAN Interworking Architecture

## Slide 13: Network Selection and Advertisement
Contains both
  WLAN access network selection
  PLMN network selection
Two modes
  Automatic and manual
Network Access Identifier (NAI) has an important role in
  Authentication
  AAA routing
  NAI decoration for roaming
  PLMN discovery
WLAN access network selection
  SSID based
  Users & operator have “preferred” lists
PLMN selection
  EAP based advertisement
  IEEE 802.11u based advertisement
3GPP PLMN
Roaming Partner X
Roaming Partner Y
WLAN A
WLAN B
WLAN C
SSID A
SSID B
SSID C
Roaming Agreement

## Slide 14: WLAN Interworking in Release 8
More complete incorporation of WLAN as part of non-3GPP support to the Evolved Packet Core (EPC)
Slide 14
September 2012

## Slide 15: Non-3GPP Access Interworking
Session mobility with IP address preservation is provided between the 3GPP network and the WLAN network with the P-GW acting as the user plane anchor between the two access networks
  S2a: network based IP mobility for trusted non-3GPP access with GTP or PMIPv6
  S2b: network based IP mobility for untrusted non-3GPP access with GTP or PMIPv6
  S2c: client based IP mobility for non-3GPP access with DSMIPv6
Multiple PDN connections over non-3GPP access
Access authentication in non-3GPP access using EAP-AKA or EAP-AKA’
Access Network Discovery and Selection Function
Security architecture for non-3GPP accesses to EPS

## Slide 16: Trusted vs Untrusted Networks
Home operator decides if a non-3GPP access network is trusted or un-trusted
Depends largely on whether the home operator trusts the security of the hotspot deployment
May also be affected by the business relationship between the hotspot provider and the home operator
For example, when a subscriber of Operator A using a Wi-Fi enabled device connects to Wi-Fi Provider B’s hotspot, Provider B’s hotspot might be considered as an un-trusted WLAN access – particularly if the hotspot provider is a café owner using the public Internet to connect to the home operator! In this case, the specifications allow for a device to establish a secure tunnel via an ePDG before the traffic is routed to Operator A’s core network
If the subscriber connects to Operator A’s own Wi-Fi hotspot, the hotspot is considered trusted WLAN access and no secure tunnel is required by the specifications to route traffic to the core network

## Slide 17: Non-3GPP Access Interworking Architecture (S2a, S2b)

## Slide 18: Non-3GPP Access Interworking Architecture (S2c)

## Slide 19: Access Network Discovery and Selection Function (ANDSF)
The data management and control functionality to provide network discovery and selection assistance data per operators' policy
The ANDSF shall respond to UE requests for network discovery information (pull mode operation) and may initiate data transfer to the UE (push mode operation), based on network triggers or as a result of previous communication with the UE
The ANDSF shall provide the following information:
  Access network discovery information
  Inter-System Mobility Policy (ISMP)
  Inter-System Routing Policy (ISRP)
  UE location information
3GPP PLMN
Roaming Partner X
Roaming Partner Y
WLAN A
WLAN B
WLAN C
SSID A
SSID B
SSID C
Roaming agreement

## Slide 20: WLAN Interworking in Release 10
Non-seamless WLAN offload
Slide 20
September 2012

## Slide 21: Non-Seamless WLAN Offload
A UE supporting non-seamless WLAN offload may, while connected to WLAN access, routes specific IP flows via the WLAN access without traversing the EPC
These IP flows are identified via user preferences, the local operating environment information, and via policies that may be statically pre-configured by the operator on the UE, or dynamically set by the operator via the ANDSF
For such IP flows the UE uses the local IP address allocated by the WLAN access network and no IP address preservation is provided between WLAN and 3GPP accesses

## Slide 22: WLAN Interworking in Release 11
Policy and QoS Enhancement on WLAN Access via a EPC with Broad Band Forum Co-operation
Support of Trusted WLAN Access Procedure Without UE Impacts
Slide 22
September 2012

## Slide 23: Policy and QoS Enhancements in WLAN Access
Policy and Charging Control on both home routed traffic and non-seamless offload traffic over untrusted WLAN access
Support of UE reflective QoS for uplink
IKEv2 based tunnel authentication with ePDG
Multiple PDN connections supported with one PDN connection per IKEv2 tunnel with the same ePDG
Support of inter-access handover and IP preservation
3GPP based access authentication (EAP-AKA) is optional

## Slide 24: Support of Trusted WLAN Access Procedure Without UE Impacts
The S2a interface between the TWAN and the PGW is either GTP or PMIPv6
No impact to the UE was considered. The solution works with legacy UEs that connect to WLAN using standard 802.11 and EAP procedures
3GPP based access authentication (EAP-AKA’)
The TWAN provides either EPC routed traffic or non-seamless offloading
If EPC routed traffic, only one PDN connection with default APN, and no IP mobility is supported

## Slide 25: WLAN Interworking in Release 12
On-going Working Items and Study Items
Slide 25
September 2012

## Slide 26: Ongoing Working Items in Release 12
WLAN Network Selection for 3GPP Terminals (WLAN_NS)
  To evaluate and if needed enhance existing 3GPP solutions for network selection for WLAN taking into account WFA Hotspot 2.0 solutions.
  The proposed work is based on existing TS 23.402 architectures.
  3GPP operator’s policies for WLAN network selection will be provisioned on 3GPP terminals via pre-configuration or using ANDSF.
Policy and Charging Control for Supporting Fixed Broadband Access Networks (P4C)
  Policy and Charging Control in the fixed broadband access network in the convergent scenario where a single operator is deploying both the fixed broadband access network and the Evolved Packet Core (EPC).

## Slide 27: Ongoing Study Items in Release 12
Study on Trusted WLAN Access with Modified UEs (FS_SAMOG)
  Handover between 3GPP and WLAN via S2a with IP address preservation
  Connection type request from the UE (request for EPC-routed connection via S2a or for local IP session, i.e. non-seamless WLAN offload)
  Attach to non-default APN and support for multiple PDN connections
  Support for simultaneous EPC-routed traffic and offload (local access)
Study on Optimized Offloading to WLAN in 3GPP-RAT Mobility (FS_WORM)
  Minimizing user and service impact and better using simultaneous connectivity to a 3GPP access and to WLAN access at mobility
  ANDSF enhancements to enable policy differentiation of 3GPP RATs (e.g. E-UTRAN versus UTRAN, GERAN vs. UTRAN) with respect to WLAN
Study on Multi Access PDN Connectivity and IP Flow Mobility (FS_MAPIM)
  Accessing a PDN simultaneously via a 3GPP and a non 3GPP access system
  Operator policies for guiding and configuring UE IP flow routing via different access systems
  Dynamic movement of PDN IP flows between access systems
  3GPP-non3GPP handovers when UE is connected to different PDNs via different accesses
Study on IP Flow Mobility Support for S2a and S2b Interfaces (FS_NBIFOM)
  Define the corresponding IP flow mobility functionality standardized for DSMIPv6 in Rel-10 for PMIP and GTP-based S2a and S2b

## Slide 28: Conclusions
3GPP has a long history incorporating IEEE 802.11 WLAN technology into mobile networks
Recent renewed interest due to mobile network capacity demands, data offload and the introduction of heterogeneous networks
Trusted WLAN networks use existing IEEE 802.11 protocols, authentication procedures and devices
WLAN interworking continues to evolve in 3GPP
Converged 3GPP-WLAN network architecture is a key priority for 3GPP mobile operators

## Slide 29: Q & A

## Slide 30: Backups

## Slide 31: Example of WLAN UE-Initiated Tunnel Establishment
Slide 31
September 2012

## Slide 32: Architecture for Untrusted Fixed Broadband Access Network
Slide 32

## Slide 33: Security Architecture for non-3GPP Accesses to EPS
Network access security (I): the set of security features that provide users with secure access to services while terminated at 3GPP EPC. Radio Access protection is a non-3GPP access specific and outside the scope of the present document.
Network domain security (II): the set of security features that enable nodes to securely exchange signalling data, and protect against attacks on the wireline network.
Non-3GPP domain security (III): the set of security features are a non-3GPP access specific and outside the scope of the present document.
Application domain security (IV): the set of security features that enable applications in the user and in the provider domain to securely exchange messages.
User domain security (V): the set of security features that secure access to the mobile station. If the terminal does not support 3GPP access capabilities, 3GPP does not specify how user domain security is achieved.
Slide 33

## Slide 34: UE Location Information
Slide 34
September 2012

## Slide 35: Network Discovery Information
Slide 35
September 2012

## Slide 36: S2a GTP Initial Attachment
Slide 36
September 2012

## Slide 37: Architecture for Home NodeB
Slide 37

## Slide 38: Bearer Model for PDN Connectivity Service with GTP based S2a
Slide 38

## Slide 39: QoS Architecture for 3GPP - WLAN IP Access
Slide 39
September 2012

## Slide 40: QoS for 3GPP and Fixed Broadband Access Interworking
Slide 40