## Slide 1: TSF Timer Freq. Management and Measurement Procedure (TFM2P)
Date: 2012-10-31
Authors:

## Slide 2: Abstract
First half part of detailed three procedures of enhanced power saving function which employs the proposed TFM2P (TSF timer Frequency Management & Measurement Procedure) is presented.
( This partial submission is only for conference call. )
TFM2P can be used with existing PS mechanisms to allow STA waking up precisely and sleeping more, for following operational conditions;
numerous numbers of sensors or meters, with lower traffic at each STA, requiring battery conservation. (use case 1a/c/d/e/f)
access control using wake-up timing control schemes using TSF timer synchronization, rather than simple ALOHA. (RAW, TWT, PS-mode, etc.)
Notes: /c

## Slide 3: Principle of PS feature
Synchronize peer nodes to TSF
Schedule or Trigger for STA wake-up
Sleep as long as possible for peer nodes to queue
Awake as short as possible to communicate quickly
Accuracy of TSF sync does set the duty ratio , due to wake-up margin.
; for small
  c.f. Peer to peer clock frequency accuracy=40ppm,
  (1) = (36ms / 15min) + 40 = 40 + 40 ppm
  (2) = (360us / hour) + 40 = 0.1 + 40 ppm or = (3.6ms / 10 hour) +40 = 0.1 +40 ppm

## Slide 4: Wake-up synchronization Simple AP announcement of TSF accuracy (1)
Wake-up Timing margin depends on TSF timer freq. accuracy △;
Wake-up margin -△· (TW – TS)
AP
(e.g. TSF master)
STA
(e.g. TSF slave)
sleep again
scheduled wake-up time (ideal case)
actual sleep duration
TW
± △· (TW –TS)
≈
TW
notified
△ includes
accuracy of
both AP & STA
< 11-12/130r0 “Beacon Reception of Long Sleeper” >
  AP is supposed to announce TSF accuracy △, (△<100ppm)
  STA is able to wake up at (TW –TS)(1 - △) +TS
  TS : TSF timer value just after last time it was synchronized
STA
awake
TS
(IEEE802.11-2012)
Tolerance
±100ppm

## Slide 5: Wake-up synchronization Simple AP announcement of TSF accuracy (2)
Awake period of STA may become much longer than actual
Communication.
Wake-up margin - △· (TW –TS)
AP
(e.g. TSF master)
STA
(e.g. TSF slave)
sleep again
scheduled wake-up time (ideal case)
actual sleep duration
TW
± △· (TW –TS)
≈
actual
communication
TW
notified
TW-actual
actual wake-up point of time
Communication may happen within green window.
STA have to be awake during entire blue period
while actual communication duration may be a part of awake period.
STA
awake
± △·( TW – TS)
STA awake

## Slide 6: Wake-up sync. using TFM2P AP announcement of TSF timer stability (1)
Wake-up Timer Stability information (±ε) as well as △;
compensated by measured TSF frequency Tw-compen
announced AP
( TSF master)
Receiver side
measured STA
(e.g. TSF master)
sleep
again
scheduled wake-up time (ideal case)
TW
± △· TW
measured AP side
point of time (by STA)
±ε
△measured
≈
Tw notified after TSF frequency measurement
STA
awake
-ε
wake-up margin
< TFM2P involves two parameters, i.e. △ and ε >
  AP advertise △worst and ε
  STA to wake up at,
  (TW-compen –TS)(1 - ε)+TS ≃ (TW –TS)(1 + △measured - ε) +TS

## Slide 7: Wake-up sync. using TFM2P AP announcement of TSF timer stability (1)
Wake-up Timer Stability information (±ε) as well as △ ;
compensated by measured TSF frequency Tw-compen
announced AP
( TSF master)
Receiver side
measured STA
(e.g. TSF master)
sleep
again
scheduled wake-up time (ideal case)
TW
± △· TW
measured
point of time
-ε
△measured
≈
Tw notified after TSF frequency measurement
actual
communication
TW-actual
actual point of time
STA
awake
STA to wake up at
(TW-compen –TS)(1 - ε)+TS ≃ (TW –TS)(1 + △measured - ε)+TS
after once TFM2P has carried out .

## Slide 8: Comparison of Wake-up synchronization (1)
Simple Accuracy Announcement and TFM2P (frequency measurement)
(Tw - TS) (1- △advertised ) + TS
Less wake-up margin
by TSF freq. offset compensation
and freq. stability information
awake
sleep again
sleep
STA w/t TFM2P
(e.g. TSF slave)
wake-up margin
using accuracy information
(△advertised )
AP
(e.g. TSF master)
STA w/o TFM2P
(e.g. TSF slave)
wake up
sleep again
scheduled wake-up time Tw
sleep
± △advertised · ( TW –TS)
awake
actual
communication
Informed Tw is used
with △advertised
(TW – TS)(1 + △measured - εadvertised) + TS
Informed Tw and εadvertised
is used with
measured frequecy

## Slide 9: Comparison of Wake-up synchronization (2)
AP
STA
STA
STA
AP
STA
STA
STA
AP
STA
STA
STA
Simple
accuracy
announcement
(broadcast)
Broadcast
(uni-directional)
Receiving
broadcasted
accuracy information,
then calculate wake-up margin, △AP+STA
Time Stamp
announcement
for TFM2P
(broadcast)
Time Stamp
handshake for
TFM2P
(node by node)
Broadcast
(uni-directional)
Unicast handshake
(node by node)
accuracy △AP
accuracy
accuracy
Stability ε
B1+B1timestamp
B2+B2timestamp
Stability ε
M1+Ack
M2+Ack
M4+Ack
M5+Ack
M6+Ack
Receiving
four broadcasted
time stamp for measuring TSF freq.,
then calculate wake-up margin, △measured , ε
B1+B1timestamp
B2+B2timestamp
B2+B2timestamp
B1+B1timestamp
Handshaking
two time measurement
to determine each precise offset and freq.,
then calculate wake-up margin, △measured , ε
M3+Ack
M7+Ack
M8+Ack
Proposed three procedures of TFM2P for Power Saving
M9+w/o Ack

## Slide 10: Comparison of Wake-up synchronization (3)
Scheme | Broadcast or Handshake | Inaccuracy information | Resulting Wake-up Accuracy | Battery life improvement (ex. estimated) | Update | Required mechanism | PHY/MAC Support
IEEE802.11-2012 (Conventional) | None | Pre-defined by Std. | ±100 ppm +offset | Reference (1.0) | None | TSF synch only | Not required
Timer accuracy notification [11-12/130r0] | Broadcast w/o handshake | by AP announcement | ±20~50 ppm +offset | 1.6 times (1.2~2.0) | Not Required | TSF timer freq. accuracy advertisement | MAC: required
TFM2P | Broadcast w/o handshake | by direct TSF frequency measurement + AP stability advertisement | ±2~10 ppm +offset | 2.5 times (1.5~4.0) | Conditionally preferred | TSF timer freq. accuracy advertisement + Two time measurements + Calculation & compensation | MAC: required PHY: optional
 | Node by node w/t bi-directional handshake |  | ±1~5 ppm null offset |  | Conditionally Required |  | MAC: required PHY : preferable

## Slide 11: Typical mechanism of TFM2P using Broadcast (1)
Full beacons with DTIM always carry ToD time stamp for TFM2P.
All ToD time stamp correspond to N-times previous DTIM beacon.
Each pair of ToD time stamp may be used for TSF freq. estimation.
Beacon Interval
Beacon Transmissions
( can be short beacon )
Busy medium other transmissions
Full Beacon DTIM
N-times previous ToD time stamp
Full Beacon DTIM
N-times previous ToD time stamp
N-times DTIM Interval ( N ≥ 1 )
TIM
TIM
TIM
TIM
≈
≈
≈
TFM2P frequency measurement pair
DTIM
DTIM
AP as Clock master broadcasts with no handshake

## Slide 12: Typical mechanism of TFM2P using Broadcast (2)
t1=ToD(B1)
t5=ToD(B2)
B2
B2timestamp
B1
B1timestamp
t2=ToA(B1)
t6=ToA(B2)
t1 are known
t5 are known
Sending STA(f1)
Receiving STA(f2)
: can be a network wide common value
of virtual master clock frequency, and
determines the resolution of each time
stamp measurement.
e.g. 1MHz, and 1us (i.e. TSF resolution) ( TBD : defined by upper layer or fixed )
f1⧋
f2 =
f2= f1
dot11MgmtOptionTFM2PActivated=1
AP as Clock master broadcasts with no handshake

## Slide 13: Typical mechanism of TFM2P using Broadcast (3)
t1=ToD(B1)
t5=ToD(B2)
B2
B2timestamp
B1
B1timestamp
t2=ToA(B1)
t6=ToA(B2)
t1 are known
t5 are known
Sending STA(f1)
Receiving STA(f2)
f1⧋ = 1MHz : f1 with no error
i.e. = (t5-t1) ( perfectly accurate timestamp )
No information has to be informed to peer node
for f2 calculation.
f2= f1
dot11MgmtOptionTFM2PActivated=1
f2 =
therefore : = ⧋1+δ2
f1 ≈ at AP, as master frequency;
δ2 (e.g. ppm) should be the calibration factor of f2 to schedule Tw , wake-up time.

## Slide 14
t1=ToD(M1)
t4=ToA(Ack)
t5=ToD(M2)
t8=ToA(Ack)
M2
Ack
Ack
M1
Ack
Ack
t2=ToA(M1)
t3=ToD(M1)
t6=ToA(M2)
t7=ToD(M2)
t1and t4 are known
t5and t8 are known
offset1 ⧋ [(t2-t1)-(t4-t3)]/2
offset2 ⧋ [(t6-t5)-(t8-t7)]/2
Sending STA(f1)
Receiving STA(f2)
M2timestamp
f1⧋
: Network wide virtual master clock
frequency. However, in general, there
may exist no master clock station,
neither AP nor STA. Therefore, each
STA may behave to synchronize to
hypothetical or specific STA ‘s master
clock with freq. of , using any pre-
defined control algorithm.
Typically, the freq. may determine
the resolution of time stamp, and Tw .
dot11MgmtOptionTFM2PActivated=1
dot11MgmtOptionTimingMsmtActivated (existing) = 1
TFM2P mechanism by node-by-node handshake (1)
How entire network synchronizes each other is out of scope of this standard.
M1timestamp

## Slide 15
t1=ToD(M1)
t4=ToA(Ack)
t5=ToD(M2)
t8=ToA(Ack)
M2
Ack
Ack
M1
Ack
Ack
t2=ToA(M1)
t3=ToD(M1)
t6=ToA(M2)
t7=ToD(M2)
offset1=[(t2-t1)-(t4-t3)]/2
offset2=[(t6-t5)-(t8-t7)]/2
Sending STA(f1)
Receiving STA(f2)
f1⧋ = ⧋ 1+δ1
and therefore ratio / ⧋ p, have to be known by all STAs within network.
If STA(f1) knows the accuracy of f1 , i.e. ,
δ1 (ppm) should be informed to STA(f2).
At STA(f2) side, = (1+δ1 ) can be re-calculated.
f2= f1
TFM2P mechanism by node-by-node handshake (2)
How all STAs synchronizes each other is out of scope of this standard.
M1timestamp
M2timestamp
dot11MgmtOptionTFM2PActivated=1
dot11MgmtOptionTimingMsmtActivated (existing) = 1
f2⧋ = ⧋ 1+δ2

## Slide 16
End of first part for conference call.
Continued to full submission at San Antonio plenary.
See you there!