## Slide 1: Channel Access issues of OBSSs with difference coverage sizes
Slide 1
Date: 2012-11-12
Authors:

## Slide 2
Slide 2

## Slide 3
Slide 3

## Slide 4: 11ah OBSS issue
A long range BSS has a coverage area which has a radius that is multiples of that of a short range BSS.
  A managing entity sets up long or short range BSS
  Any one can set up short range BSS
  Long range BSS has narrower channel bandwidth, 1 MHz while short range BSS has wider bandwidth such as 2, 4, 8 MHz
    We assume the short range STA is capable of receiving 1 and 2 MHz frames and the long range STA is capable of receiving 1 MHz frame only
A managed long range BSS may encloses several short range BSSs
  The un-managed short range BSSs will affect the operation of long range BSS
The presentation is to get consensus about whether and how to address the problem. It is not intend to discuss the specific solution.
  Two possible solution are attached in the back up section.

## Slide 5: Overview
A STAO associated with the long range APL that is also within the coverage of a short range BSS.
A STAL associated with the long range APL that is not within the coverage of the plurality of short range BSSs.
A STAS associated with a short range APS that is also within the coverage of the long range BSS
APS
APS
APL
STAL
STAO
STAS
STAS

## Slide 6: Problem
The APss and STAss will hear the traffic of the long range BSSs and set up collision avoidance scheme accordingly.
Some of the APL and STALs' may not hear the traffic inside some of the short range BSSs and would not set up collision avoidance scheme accordingly.
As a result, the traffic in the long range BSS may collide with the traffic in some of the short range BSSs and causes data loss.

## Slide 7: Possible mechanisms to address the problem
Sharing channel in time domain – Re-use the current protocol elements
  Time Division mechanisms by physical grouping or logical grouping of STAs
Coordinated Channel Access - Re-use the current protocol elements
  Centralized coordination mechanisms
  Distributed mechanisms to reserve channel time
Can 802.11 TXOP protection mechanism be modified to address the problem?
  A mechanism for setting NAV of STALs by STA in an overlapping short range BSS
    A mechanism allows an STA, STAS, STAO, or other STAs, resides in the short range BSS to set the NAV of STAL associated with the long range APL.

## Slide 8: Motion
Move to add a section “OBSS mitigation procedures” in the 11ah framework specification document to address the overlapping BSS problem described in page 6?
  Yes
  No
  Abstain