## Slide 1: Channel indication in RAW/TWT
Date: 2013-01-14
Authors:

## Slide 4: Summary
Narrowband channel selection protocol was adopted [1]
  Narrowband transmission (1/2 MHz) may suffer from high diversity loss
  The approved concept [1] allows STAs to transmit to the AP on a preferred channel within the BSS BW; more detailed recap in next slide
  Flexible multichannel access allow STAs to avoid fading channels
Some MAC aspects need be defined
We propose a simple way to manage the MAC for multichannel access
  Solves the multichannel hidden node issue
  Is similar to frequency hopping solutions from other standards
  Enables frequency channel selection also for APs that are only able to detect packet on a single channel

## Slide 5: Frequency selective transmissions - Recap
AP Assumptions:
  AP is able to detect and receive a packet on any of the channels it indicates in the beacon
    May be one channel (primary) or multiple channels within the BSS BW
    Detection on multiple channels requires special hardware capabilities
  AP is not able to detect/decode parallel transmissions on different channels
Beacons or sounding signals sent after the beacon can be used by a STA to estimate the best channel to be used
  AP may send more than one Beacon per TBTT on more than one subchannel of the BSS
  Beacons include indication of following sounding frames
STAs are allowed to choose any permitted 2 MHz subchannel of a wideband BSS on which to transmit and receive
  Beacons include the indication of the allowed channels for transmission
  MAC needs to ensure that no parallel transmissions on different channels occur

## Slide 6: MAC
We want to enable the following MAC behavior
  Within a beacon period, AP defines multiple time intervals and defines a ‘temporary primary’ channel per each interval of time
    ‘temporary primary’ channel is the one where CSMA is done and where AP is able to detect a packet: all transmissions shall include the temporary primary channel
Benefits
  At each moment in time STAs contend on a single channel: no parallel transmissions
  AP can detect packets only on one channel only (the temporary primary channel)
  Within a beacon period each STA has still the chance to transmit on the preferred channel (allocated intervals should cover all the channels)
BCN
BCN
CH1
CH2
TBTT
Interval 1
CSMA done
on CH1
TBTT
Interval 2
CSMA done
on CH2

## Slide 7: Use of RAW
11ah adopted the definition of a Restricted Access Window [2]
  An interval of time during which the access is restricted to a group of STAs
  RAWs are defined in a beacon
  The concept of a Periodic RAW was also introduced [3]
We can reuse the RAW definition to
  Define the interval of time and indicate a ‘temporary primary channel’
    Add a channel indication field in RPS IE [2]
    Each RAW may be advertised in its corresponding Beacon
  Allow all STAs to access during a RAW, so that the only restriction is the channel that can be used during the RAW
TBTT
BCN
BCN
CH1
CH2
TBTT
RAW 1
CSMA done
on CH1
RAW 2
CSMA done
on CH2

## Slide 8: RAW Parameter Set Element
4.4.3.1.2 in Extend SFD defines the fields in the RAW PS IE:
Feature | Value | Interpretation
Page ID | TBD bits | Indicates the page index for hierarchical AID (based on hierarchical AID) of the allocated group
Block Offset | TBD bits | Assuming 32 blocks per page, these bits indicate the starting block index of the allocated group
Block Range | TBD bits | Indicates the number of blocks (starting from the block offset) for the allocated group
RAW Start Time | 8 bits | Duration in TU from end of beacon transmission to RAW Start time
RAW Duration | TBD bits | Duration of RAW in TU
Channel | TBD bits | Indicates the ‘primary’ channel during this RAW, where CSMA is done
Access restricted to paged STA only | 2 bits | Bit 1: Set to 1 if only STA with their TIM bit set to 1 are allowed to perform UL transmissions Bit 2: Set to 1 if RAW is reserved for frames with duration smaller than slot duration, such as PS-Polls / trigger frames (ignored if Bit 1 is not set)
Group/Resource allocation frame indication | 1 bit | Set to 1 to indicate if STAs need to wake up at the beginning of the RAW to receive group addressed frames such as resource allocation (format of the resource allocation frame TBD)
Slot definition | TBD bits | Include Slot duration signaling Slot assignment to STA Cross boundary transmissions allowed/not allowed Format is TBD
Include signaling that allows to indicate a group that includes all the STAs (‘omni group’)

## Slide 9: TWT
11ah also defines the concept of TWT [4]
  STA and AP agree on a time where STA is awake for communication
  STA can sleep otherwise
If AP operates with a frequency selective MAC protocol, STA waking up at TWT needs to know on which channel to tune its receiver/transmitter
We propose to include in TWT and indication of the channel to be used
BCN
PIFS separated Beacon
BCN
CH1
CH2
TBTT
AP on CH1
TWT for STAn on CH2
TWT for STAn on CH1
AP on CH2

## Slide 10: Conclusion
We propose to add to the RAW/TWT definition an indication of the channel to be used as ‘temporary primary channel’
  Implicitly avoids the MAC issue related to parallel transmissions on different channels
    At each moment in time STAs contend on a single channel and transmit at least on that channel
  Enables frequency selective protocol for APs that can detect packets on a single channel (the temporary primary channel)

## Slide 11: Straw poll 1
Do you agree to include a channel indication in the RPS IE?

## Slide 12: Straw poll 2
Do you agree to allow for the indication of a ‘omni group’ in the RSP IE?

## Slide 13: Straw poll 3
Do you agree to include a channel indication in TWT setup?

## Slide 14: References
[1] 11-12-1338-00-00ah-frequency-selective-transmission.pptx
[2] 11-12-0843-00-00ah-restricted-access-window-signaling-for-uplink-channel-access.pptx
[3] 11-12-1311-00-00ah-periodic-channel-access.pptx
[4] 11-12-0823-00-00ah-targetwaketime.pptx