## Slide 1: Flexible Multicast
Date: 2013-01-14
Authors:

## Slide 2
Authors continued:

## Slide 3
Authors continued:

## Slide 4: Introduction
In 11ah use case, 6000 STAs may belong to different message groups.
- STAs in different communities
- Different types of meters: electricity, gas, water, …
- Different types of monitors: video, environment, …
- Offload STAs and sensor STAs
The broadcast messages in different message groups (i.e. multicast) have different data amount and transmission pattern.

## Slide 5: Issues
In current spec, there’re two ways to manage multicast groups.
- Multicast-group address: “An address associated by higher level convention with a group of logically related STAs.”
- FMSID: “FMSID is a 1-octet identifier assigned by the AP. Inclusion of an FMSID indicates the AP has buffered BUs for the corresponding group addressed stream that is scheduled for transmission immediately after the DTIM Beacon frame.”
The above two methods are not suitable for managing multicast groups in 11ah use case (6000 STAs, most are low power sensors)
- If AP has to indicate buffered BUs for too many multicast groups in one beacon, the size of beacon will be very big.
- If AP broadcasts the messages which are for a group of STAs to all the STAs, some STAs will waste power receiving and then discarding the messages.
Notes: A STA shall discard an MPDU with a group address in the Address 1 field if the value in the Address 1 field does not match any value in the dot11GroupAddressesTable and does not match the Broadcast address value.
first check FCS

## Slide 6: Proposed Solution
In current TIM structure [1], there’re 2192 AIDs unused.
- 8 STAs * 8 sub-blocks * 32 blocks * 4 pages – 6000 STAs
Some of the unused AIDs can be used as MID (Multicast ID) to indicate multicast groups.
Considering TIM compression, all MIDs may be allocated in the contiguous (sub)blocks, or a fixed part of TIM that is dedicated to MIDs.
- Details are TBD

## Slide 7: Proposed Solution
If the STA belongs to one or multiple multicast groups, AP assigns one AID and one or multiple MIDs to the STA at association. Otherwise, AP assigns AID to the STA as normal.
- New IE in association response frame (TBD)
If the STA moves to another multicast group during operation, AP informs the STA a new MID.

## Slide 8: Example 1
In current spec, all STAs receive group addressed BUs after DTIM.
- A STA needs to receive all the group addressed BUs, and then discards the BUs not for it.
With the MIDs indicated in DTIM, the STA will know whether (explicitly) and when (implicitly) there’re group addressed BUs for it.
- If MIDn = 1, AP has buffered BUs for the STAs with MIDn.
- After receiving DTIM, STA goes back to sleep, and then wakes up and receives group addressed BUs in the order determined by DTIM bitmap.
AP
DTIM
MID
AID
AID
Data for STAs with MID 0
Data for STAs with MID 2
Data
Data
Data
…
STAs with MID 0
STAs with MID 2
Other STAs
Normal unicast data according to TIM
Wake up & receive
Sleep
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 0 | 1 | 0

## Slide 9: Example 2
If the group accepts the TIM signaling method in [2], the group addressed BUs can be scheduled after each DTIM/TIM.
- If the (sub)block containing the STA’s MID is in Segment Count IE, the STA continues to receive DTIM.
- If the STA’s MID is 1 in DTIM, the STA wakes up after the Nth DTIM/TIM to receive its group addressed BUs. N is the MID’s order among all the MIDs set to 1 in DTIM.
AP
DTIM
MID
Page Segments
Data for STA with MID 0
Data for STA with MID 2
TIM
TIM
Data for STAs with MID 4
DTIM
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 0 | 1 | 0

## Slide 10: Conclusion
Some of the unused AIDs can be used to indicate multicast groups (MID).
A STA can belong to multiple multicast groups, move to another multicast group during operation, and only receive its own group addressed BUs.

## Slide 11: Pre-Motion
Do you agree that an AID can indicate a group of STAs?

## Slide 12: Motion
Move to add the text “an AID can indicate a group of STAs” into the spec framework