## Slide 1: Proposal of RoF Extension Link Backhaul for Category 4
Date: 2013-01-23
Authors:

## Slide 2: Abstract
RoF (Radio on Fiber) extension link is proposed as one of usage models of 11aj backhaul. RoF extension link can extend wireless access area to the different location without signal degradation and frequency interference. RoF extension link has broadband transmission capability because of O/E and E/O broadband conversion characteristics and can transmit signals at 45-GHz and 60-GHz bands simultaneously. The experimental results of RoF extension link are also presented.
The aim of this contribution is to add usage model 4c in the IEEE 802.11aj Usage Models Document IEEE 802.11-12/1145r1.

## Slide 3: Overview of WFA VHT usage models for 802.11ad
Category | # | Usage Model
1.Wireless Display | 1a | Desktop Storage & Display
 | 1b | Projection to TV or Projector in Conf Rom
 | 1c | In room Gaming
 | 1d | Streaming from Camcorder to Display
 | 1e | Broadcast TV Field Pick Up
 | 1f | Medical Imaging Surgical Procedure Support
2.Distribution of HDTV | 2a | Lightly compressed video streaming around home
 | 2b | Compr. video steaming in a room/ t.o. home
 | 2c | Intra Large Vehicle (e.g. airplane ) Applications
 | 2d | Wireless Networking for Small Office
 | 2e | Remote medical assistance
3.Rapid Upload / Download | 3a | Rapid Sync-n-Go file transfer
 | 3b | Picture by Picture viewing
 | 3c | Airplane docking
 | 3d | Movie Content Download to car
 | 3e | Police / Surveillance Car Upload
4.Backhaul | 4a | Multi-Media Mesh backhaul
 | 4b | Point to Point backhaul
5.Outdoor Campus /Auditorium | 5a | Video demos / telepresence in Auditorium
 | 5b | Public Safety Mesh
6.Manufacturing Floor | 6a | Manufacturing floor automation
7.Cordless computing | 7a | Wireless IO / Docking

## Slide 4: Category 4: Backhaul
Multi-Media Mesh Backhaul
  Hotspot
  Enterprise
  Small Office or Home
  Campus-wide deployments
  Municipal deployments
Point-to-Point Backhaul
RoF* Extension Link Backhaul
* Radio on Fiber
4

## Slide 5: Usage Model 4c: RoF Extension Link Backhaul
Projector
RoF Extension Link
1st
1st floor
2nd floor
Access Point
O/E&E/O devices
O/E&E/O devices

## Slide 6: Usage Model 4c: RoF Extension Link Backhaul
6
Pre-Conditions:
Wireless zones are connected via RoF extension link. The individual wireless zones can support high-speed-data traffic requirements that are limited by the VHT link capabilities.
Application:
Traffic is bidirectional and is comprised of subcarriers which include data, voice, video, and any kinds of signals. These subcarriers are equivalent to radio frequencies, i.e. either 45GHz or 60 GHz bands. RoF extension link extends coverage areas without any performance degradation of traffic requirements.
Environment:
Environment can be home, office, manufacturing floor, etc.
Point-to-point link distance can be extended up to 20 km due to low insertion loss of optical fiber cables. Typically locations are Non-Line-of-Sight. No frequency interferences can be managed by use of optical fiber cable.
Traffic Conditions:
RoF extension link can carry any type of traffic due to broadband transmission capability of RoF devices. End of each link is heavily loaded with equal amount of traffic in both directions.
Use Case:
Wirelessly separated spaces such as rooms of houses surrounded by concretes are directly connected through RoF extension link without any digital signal processing units.
In spite of physical and electromagnetic separation, one wireless zone is extended to another wireless zone which has the same characteristics of the original one.
Users at different locations can take advantage of broadband multi-media applications.

## Slide 7
RoFシステム・実験概略
100-kHz-linewidth
tunable laser
Mach-Zehnder
Optical modulator
Optical
band-pass
Filter 1
Er-doped
fiber amplifier
Photodetector
Optical
band-pass
Filter 2
RoF Tx
RoF Rx
Vector network analyzer
Optical fiber
0~15 km
Tunable laser: Yenista optics OSICS TLS-AG (Power stability: ±0.03 dB)
MZ modulator: GIGOPTIX LX8901 (3-dB BW:>65 GHz)
Photodetector: u2t photonics XPDV4120 (3-dB BW:100 GHz)
EDFA: Amonics Burst-mode EDFA (Sat. power 20 dBm, NF:<5.5 dB)
Bandpass filter1: BW > 1 nm for generation of single sideband signal
Bandpass filter2: BW ~ 1 nm for suppression of ASE noises from EDFA
2013/1/18 菅野@NICT
-18 dBm
Experimental Setup of RoF Link

## Slide 8
RoFシステムf特測定結果
Amplitude Deviation: < 2 dBp-p at 40.5-47 GHz
  ~ 2 dBp-p at 57-66 GHz
2013/1/18 菅野@NICT

## Slide 9
RoFシステム ファイバ伝送後f特比較
Frequency response of RoF link at 40-48 GHz and 56-67 GHz bands
2013/1/18 菅野@NICT

## Slide 10: Summary
RoF extension link backhaul was proposed for Category 4 (Backhaul)
RoF extension link backhaul can extend wireless access area through optical fiber up to 20 km without signal degradation and frequency interference.
The amplitude characteristics at 40-48 GHz and 56-67 GHz bands of RoF link were experimentally evaluated and the amplitude deviation less than 2 dBp-p was achieved.
Data transmission experiment of RoF link will be presented at the next meeting.

## Slide 11: Straw Poll
Do you agree that IEEE802.11aj Task Group considers that the proposed RoF extension link can be one of usage models of backhaul ?
- Yes:
- No:
- Abstain:

## Slide 12: Straw Poll
Do you agree that IEEE802.11aj Task Group considers that the proposed RoF extension link should be icluded in the Functional Requirement Document for 11aj?
- Yes:
- No:
- Abstain:

## Slide 13: Acknowledgments
This work was supported in part by "The research and
development project for the expansion of radio spectrum
resources" of the Ministry of Internal Affairs and
Communications in Japan.