## Slide 1: Resource Allocation Frame Format for RAW-based Medium Access
Date: 2013-03-18
Authors:

## Slide 4: Motivation
Motion passed in July 2012 IEEE meeting on RPS IE with Resource Allocation (RA) frame indication as one of the Options field [1]
  STAs wake up for delivery information of downlink traffic
Motion passed on “Uplink Channel Access General Procedure” [2]
  Indication of the downlink BU delivery slot should not overload the beacon
    New management frame indicates the downlink BU delivery slot per each STA after all PS-Poll/Trigger frame transmission completed.
Single/multi-user medium access signaling to STAs prior to medium access
STAs with different MCS and amount of buffered data, result in variable slot durations
Propose to define a RA frame format with above essential information

## Slide 5: Illustration of RA Frame with DL/UL Traffic
AP
STA 4
STA 3
STA 1
RPS IE
Data 1
x0
x1
x2
x3
x4
x5
x6
Data 4
Data 3
RAW
RA Frame
Operation example in RAW after PS-Poll and UDI frame transmissions
  STA 1: SU DL transmission
  STA 2: SU UL transmission
  STAs 3 and 4: MU DL transmissions
Data 2
STA 2
PS-Poll
PS-Poll
PS-Poll
ACK
UDI
ACK
ACK
ACK
ACK
ACK
ACK
ACK

## Slide 6: Power Save Operation using RA Frame
STAs wake up at beginning of RAW to receive RA frame
AP may indicate scheduling information in RA frame with following information:
    RAW Group assigned current RAW for medium access
    Revised RAW duration
    STA address or Modified TIM bitmap to determine assigned slots
    Slot assignments with variable slot durations
After receiving scheduling information in RA frame, each STA goes to sleep state till the indicated slot for medium access

## Slide 7: Unified UL and DL Resource Allocation Frame Format
RAW Group (TBD octets) is identical to the group in RPS IE
RAW Duration (TBD octets) is revised from RAW Duration in RPS IE based on PS-Polls and UDIs
Slot assignment (2 octets/MU Group and TBD octets/STA) defines access slot allocations for STAs
  Independent of TIM bitmap
  1 bit indication for SU-STAs within RAW for UL (bit set to 0) or DL traffic, bit reserved for MU-MIMO group
  Multi-user MIMO supported when multiple STAs are assigned identical slot within RAW
STA Address may be either a partial AID (TBD bits) or a Group ID (6 bits) for a MU group
  1 bit indicator prior to the address for indication of either partial AID (bit set to 0) or Group ID (bit set to 1)
Slot Start Offset (1 octet) is start time of STA’s medium access, relative to the end of the RA frame, in TBD units
  Offset determined by AP based on buffered DL data for STAs from whom PS-Polls were received
  Offset from UDIs indicating amount of buffered traffic

## Slide 8: Summary
We proposed an approach of indicating individual STA AIDs and their corresponding delivery intervals for both uplink and downlink transmission
  TIM Bitmap independent approach
  Supports MU-MIMO using common Slot Start Offsets for multiple STAs

## Slide 9: Straw Poll 1
Do you agree to define the resource allocation frame based on the approach illustrated in Slide 5?

## Slide 10: Motion 1
Move to define the resource allocation frame format based on the approach illustrated in Slide 5?

## Slide 11: References
[1] doc.: IEEE 802.11-12/0843r0: “Restricted Access Window Signaling for Uplink Channel Access”
[2] doc.: IEEE 802.11-12/0831r0: “Uplink Channel Access General Procedure”