## Slide 1: Beyond 802.11ac – A Very High Capacity WLAN
Date: 2013-03-19
Authors:

## Slide 2: Abstract
We propose to create a new Study Group to enhance the system capacity of 802.11 WLAN by introducing some new PHY & MAC features.
The objective includes but not limited to support the use cases of cellular data offload in areas where APs are densely deployed.

## Slide 3: Background
802.11acが世に出始めようとしてる今、何故新たな標準が必要なのか？
Year
1G
10G
100M
Wireless LANs
10M
1M
100k
100G
Data Rate [bit/s]
Cellular
LTE-Advanced
2005
2010
2015
2000
1995
GSM
PDC
WCDMA
HSDPA
LTE
.11b
802.11
.11a
.11g
.11n
.11ad
.11ac
?
Cellular companies have started 4G/LTE services offering max. data rate of 100 M bit/s. One of those companies is planning to start LTE-Advanced service in 2015 which offers max. 1 G bit/s.
WLANs also needs to be upgraded to support increasing demands of data communications and emerging applications together with the cellular systems.

## Slide 4: Important applications for the WLAN
Cellular data offload
  In public places, i.e. hotspots
  In the home/residential area
Other Emerging applications
  VoIP with QoS and handover support
  WLAN Navigation & contents distribution, etc.
Dense WLAN deployment is anticipated:
APs are densely deployed in many places to support many STAs and emerging applications
More and more people are using tethering function of smart phone or mobile router for the Internet access

## Slide 5: What we hope for the WLAN
WLANs as an alternative to the cellular system in home, office and public hotspots
  Need to support use cases such as cellular data offloading in home and public areas (hotspots).
Requirements
  To maintain throughput in places where APs are densely deployed = very high system capacity / m2
Our Proposal
  A maximum multi-STA/aggregated throughput (measured at MAC SAP of APs) of at least 10 G bit/s
  Requirement for the single link throughput to be discussed in the new study group.

## Slide 6: Current situation
The 802.11ac enables gigabit class data transmission capability using 5GHz band.
  Great achievement!
  The benefit of high data rate comes from wider channel operations and increased number of spatial streams.
  DL MU-MIMO improves the spectrum efficiency by allowing simultaneous transmissions of multiple data frames to different users.
However, demands for the bandwidth continue to increase.
  As more people use high performance and high functionality terminals, the WLAN system will be required to have enough capability to satisfy their needs for data communications.
  We would like to consider to add some features to the 802.11ac standard to enhance the system capacity.

## Slide 7: Some issues observed
Low throughput performance in hotspots
Chart: 
| 0.30694444444444441 | 0.30763888888888891 | 0.31319444444444444 | 0.31388888888888888 | 0.32569444444444445 | 0.3263888888888889 | 0.33194444444444443 | 0.33263888888888887 | 0.3430555555555555 | 0.34791666666666665 | 0.3520833333333333 | 0.3527777777777778 | 0.35486111111111113 | 0.35625000000000001 | 0.35694444444444445 | 0.35833333333333334 | 0.36041666666666666 | 0.3611111111111111 | 0.36458333333333331 | 0.36527777777777781 | 0.36736111111111108 | 0.36805555555555558
DL(LTE) | 21.63 | 14.984 | 16.714 | 11.668 | 8.702 | 9.356 | 12.908 | 12.424
DL(Wi-Fi) | 2.627 | 2.6 | 2.265 | 0.6 | 1.039 | 1.304 | 0.243 | 0.507 | 1.068 | 0.422 | 0.652 | 2.456 | 2.396 | 0.626
Results of throughput measurement at the Shinagawa station in Tokyo area.
Throughput of LTE is much higher than the WLAN!
In such places, people may not be happy to use WLAN, and cellular offload will not be successful.
What can we do to improve WLANs?

## Slide 8: Classification of the issues
Operational issues
  What we need is a guideline
  Some standardization bodies and/or industry alliance issues guidelines for appropriate operation.
Upper layer issues
  Other standardization bodies such as Wi-Fi Alliance and IETF will be right place to do.
  Upper layer issues related to cellular data offload are considered in the WFA as a part of the next generation hotspot project.
MAC & PHY related issues
  It is more appropriate to consider this kind of issues here in IEEE 802.11
We propose to start a new project to standardize new PHY & MAC features

## Slide 9: Basic Ideas
To achieve higher spectrum efficiency;
  802.11a and 802.11g introduced OFDM PHY in 5 GHz band and 2.4 GHz band, respectively.
  802.11n introduced the single user MIMO technology supporting up to 4 spatial streams.
  802.11ac is specifying DL MU-MIMO that makes simultaneous point-to-multipoint transmissions.
In the next generation WLAN, we would like to enhance the spectrum efficiency by,
  Exploiting the unused frequency resource
  Allowing simultaneous transmissions of multiple stations

## Slide 10: Example of possible technologies
Multi-User Multi-Channel (MU-MC) Transmissions
Mutual Interference Suppression
Freq.
Time
802.11a
802.11n
40 MHz
802.11ac
80 MHz
802.11ac
160 MHz
Freq.
Time
802.11a
802.11n
40 MHz
802.11ac
80 MHz
MU-MC
Capable
STA
MU-MC
Capable
STA
Ch.1
Ch.2
Ch.3
Ch.4
Ch.5
Ch.6
Ch.7
Ch.8
MU-MC
Capable
STA
MU-MC
Capable
STA
or,
802.11ac
160 MHz
Ch.1
Ch.2
Ch.3
Ch.4
Ch.5
Ch.6
Ch.7
Ch.8
AP2
STA1
STA3
AP1
Interference
Suppression
STA2
STA4
For more information, please refer to our previous presentations such as
[3] 12/0820r0, Improved spectrum efficiency for the next generation WLANs, NTT
[5] 12/1063r0, Requirements for WLAN Cellular Offload, NTT.

## Slide 11: Conclusions
We propose to start a new 802.11 study group to enhance the PHY & MAC features to be capable of operating in a densely deployed environment for the purpose of supporting important use cases and applications for the wireless LANs such as cellular data offload.

## Slide 12: Motion
Request approval by IEEE 802 LMSC to form an 802.11 Study Group to consider the high capacity WLAN as described in doc 11-13-xxxx-00 with the intent of creating a PAR and five criteria.
Moved: <name>, Seconded: <name>, Result: y-n-a

## Slide 13: References
  [1] 11/1464r2, The better spectrum utilization for the future WLAN standardization, NTT
  [2] 12/0068r1, Discussions on the better resource utilization for the next generation WLANs, NTT
  [3] 12/0820r0, Improved spectrum efficiency for the next generation WLANs, NTT
  [4] 12/0910r0, Carrier oriented WIFI cellular offload, ORANGE
  [5] 12/1063r0, Requirements for WLAN Cellular Offload, NTT
  [6] 12/1123r0, Carrier Oriented WIFI for Cellular Offload, ORANGE
  [7] 12/1126r0, Wi-Fi techniques for hotspot deployment and cellular offload, Samsung
  [8] 13/0098r0, 802.11: Looking Ahead to the Future – Part II, Huawei
  [9] 13/0113r0, Application and Requirements for Next Generation WLAN, Samsung