## Slide 1: Operation With Small Batteries
Date: 2013-3-17
Authors:

## Slide 4: Introduction
Packet transmission (PPDU) in 802.11 can span several milliseconds
  802.11ah is going to allow >20ms PPDUs
  Multiple packets can be sent back to back
Some simple devices operated by small batteries may have issues in:
  sustaining continuous TX/RX (Active) operation longer than Xms
  performing TX/RX operation shorter than Xms, but spaced in time less than Yms
  ‘X’ and ‘Y’ may depend on battery features or supply circuit design
This presentation proposes signaling for a STA to indicate
  Max continuous awake time
  Recovery time

## Slide 5: Background - I
Typical battery power supply system as in picture
Reducing peak current at the battery increases battery life by enabling higher utilization of the energy in the battery.
Board level bypass capacitance can be used to source high currents, but limited to short bursts
  Need to limit the duration of RX or TX event
We must wait for the capacitor to recharge between bursts
  Need to lower bound the time between consecutive TX/RX events
Burst and recharge periods varies with capacitor size and with battery quality and freshness
  Each STA may have different requirements

## Slide 6: Background - II
Operation with small batteries is affected by current drain amplitude and pattern in time
  Long active time negatively effect battery life or require more capable batteries/additional capacitor
  After an active period, supply systems requires some time to recover
To enable reliable operation with small batteries, from the standard point of view we need the following tools:
  STA decides the maximum duration of an active period/RX
  STA is enabled to have some time for recovery

## Slide 7: MAX Awake Duration Indication
A receiver STA indicates to a transmitter STAs the maximum continuous duration of time it can be in awake state
  Let’s call this time the MAX_awake_duration
  STA communicates the limitation to the AP or to the peer TDLS STA in e.g. the Capabilities element that is included in Probe request, (Re) Association request, TBD.
    A fixed value; not many reasons to have this dynamically changed during operation
A transmitter STA receiving this indication shall plan for frames exchanges compatible with the receiver STA’s limitation
  U-APSD: similar to existing U-APSD coexistence
  TWT: indicate a max awake time
  RAW: indicate a max awake time from star of the slot, or max slot size
  When the transmitter can not complete a frames exchanges within MAX Awake duration, a new back-off procedure is invoked after stopping the current transmission.
Details of the signaling are TBD

## Slide 8: Recovery Time Indication
STA indicates a Recovery time that a transmitter should wait after the end of a previous awake period of the STA, before sending a new PPDU addressed to the STA
  STA communicates the limitation to the AP or to the peer TDLS STA by including it in e.g. the Capabilities element that is included in Probe request, (Re) Association request, TBD
    A fixed value; not many reasons to have this dynamically changed during operation
A transmitter STA receiving this indication shall plan for frames exchanges compatible with the receiver STA’s limitation
Depending on the operation mode/access protocol used, this may have different effects
  PS-Poll initiated by a STA: generally no effect, since the STA is in control of PS-Poll exchange initiation
    Except the case where AP delays the Data response (discussed later)
  TWT: minimum separation between two TWTs
  RAW: minimum separation between two RAWs/slots in a RAW

## Slide 9: Example of operation mode - I
Assume STA is using PS-Poll/trigger frames to poll for data (TIM or non-TIM STA)
Poll
Packet(s)/ACK(s)
Less than MAX Awake Duration
Backoff
AP stores in a register for STA1: Current TSF+ MAX RX Duration(STA1)
AP can make sure that transmission will not exceed the time in the register
Same as when setting NAV or honoring a TXOP Limit
Backoff
Backoff
Case 1 (immediate Data)
Case 2: (delayed Data)
Option1
Case 2 (delayed Data)
Option2
STA discounts some backoff time from the max advertised awake time
Poll
Packet(s)/ACK(s)
Less than MAX Awake Duration
ACK
Similar to
U-APSD
Coexistence
Poll
Packet(s)/ACK(s)
Less than MAX Awake Duration
ACK
> Recovery time
Less than MAX Awake Duration
Recovery time

## Slide 10: Example of operation mode - II
Assume a TWT/RAW is in place
  AP can schedule TWTs/RAWs and transmissions to honor STA’s limitations
Packet(s)/ACK(s)
Less than MAX Awake Duration
TWT or RAW slot start time per STA already known at AP
AP can make sure that transmission will not exceed the TWT + Max Awake time
Next TWT or RAW slot for this STA
MAX Awake Duration
> Recovery time

## Slide 11: Conclusions
Sensor STAs likely will have to operate with small batteries
Limitations coming from battery/supply circuit design may imply that:
  STA is not able to operate in Active mode (TX/RX) for more than Xms
  STA may need a “recovery time” in between operations
Current specifications define PPDUs up to several milliseconds long (>20ms); multiple frames can also be exchanged back to back
  This is not compatible with the operation limitations mentioned above
We propose to define signaling to allow a receiver STA to indicate to a transmitter STA:
  Max Awake Time
  Recovery time
Transmitter STA should operate compatibly with the limitations of the receiver STA

## Slide 12: Straw poll
Do you support the mechanism described in slide 7, first two bullets?

## Slide 13: Straw poll
Do you support the mechanism described in slide 8, first two bullets?

## Slide 14: Appendix

## Slide 15: Related discussion
STA with these hardware limitation may prefer not to listen to beacons
  (That is going to be a STA’s choice, we are not preventing any operation)
  STA operating in non-TIM mode will poll AP for management updates (which may have to be delivered in fragments)
  11ah accepted a mechanism that allows a STA to explicitly indicate which management info it wants
How are broadcast/multicast packets delivered, if they exceed the MAX_Awake_Duration limit?
  STAs may decide to operate in non-TIM mode, in which case they are anyway are not listening to Beacon and Broadcast/Multicast sent after the beacon
  DMS can be used for non-TIM STA and the resulting unicast packets can be fragmented
    DMS also allows to send groupcast data at high MCS
    Along DMS, STA can indicate filtering of all unnecessary traffic