## Slide 1: Flexible Multicast follow-up
Date: 2013-03-17
Authors:

## Slide 2
Authors:
Huawei

## Slide 3
Authors:

## Slide 4: Introduction
In Jan. meeting, the concept of using AID as multicast ID (MID) was approved.
  “an AID can indicate a group of STAs”
This contribution continues to discuss how to use MID.

## Slide 5: MID Assignment
AID Request IE (blue fields are modification)
 | Element ID | Length | AID Request Mode | Wakeup Interval/Multicast Listen Interval (Optional) | Peer STA Address (Optional) | Service Type (Optional) | Group Address (Optional)
Octets: | 1 | 1 | 1 | 0 or 2 | 0 or 6 | 0 or 1 | 0 or 6
 | Wakeup Interval Present | Peer STA Address Present | Service Type Present | Non-TIM Mode Switch | TIM Mode Switch | Group Address Present | Reserved | Reserved
Bits: | B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7

## Slide 6: MID Assignment
Group Address: The group MAC address of the STA
Multicast Listen Interval: How often the STA listens to the DTIM Beacon for group addressed BUs. The value is the units of DTIM interval. If Group Address Present bit is set to 1, “Wakeup Interval/Multicast Listen Interval” field is filled with the value of Multicast Listen Interval.
  STAs with same group MAC address may need different Multicast Listen Intervals because of their different power constraints.
  e.g. STA 1, STA 2 and STA 3 are a multicast group with same group address. STA 1 and 2 have enough power and require to listen to every DTIM beacon. STA 3 is low power device and requires to listen to DTIM beacon every 4 DTIM intervals. Therefore, STA 1 and 2 will be assigned a MID, and STA 3 will be assigned another MID.
Notes: A STA shall discard an MPDU with a group address in the Address 1 field if the value in the Address 1 field does not match any value in the dot11GroupAddressesTable and does not match the Broadcast address value.
first check FCS

## Slide 7: MID Assignment
 | Element ID | Length | AID or MID | AID Switch Count | Wakeup Interval
Octets: | 1 | 1 | 2 | 1 | 2
AID Response IE (blue fields are modification)
  “AID or MID” field contain AID or MID that is assigned to the requesting STA. If it’s MID, the STA should link the MID to its corresponding Group Address and Multicast Listen Interval.
Notes: A STA shall discard an MPDU with a group address in the Address 1 field if the value in the Address 1 field does not match any value in the dot11GroupAddressesTable and does not match the Broadcast address value.
first check FCS

## Slide 8: SP 1
Do you support the modification on AID Request IE and AID Response IE on slide 5, 6 (first 2 bullets) and 7?

## Slide 9: SP 2
Do you support that 13bits MID can be used in short MAC header and as Partial MID (the computing rule is same as AID)?