## Slide 1: Efficient Frequency Spectrum Utilization
Date: 2013-05-13
Authors:

## Slide 2: Background
Discussion result on the previous meeting
Straw Poll: Do you support starting a new study group called “high efficiency WLAN” to enhance 802.11 PHY and MAC in 2.4 and 5GHz with a focus on:
  Improving spectrum efficiency and area throughput
  Improving real world performance in indoor and outdoor deployments
    in the presence of interfering sources, dense heterogeneous networks
    in moderate to heavy user loaded APs

## Slide 3: Introduction
Regarding a frequency spectrum of HEW SG, an initial consensus looks like covering both 2.4GHz and 5GHz.
The discussion for opening the new unlicensed frequency spectrum in 5GHz has been ongoing in IEEE 802.11 REG SC and Wi-Fi Alliance Spectrum & Regulatory TG.
In this presentation, we would like to discuss the usage scenario of the newly opened frequency spectrum in 5GHz.

## Slide 4: Band plan with new spectrum Importance of Additional Spectrum [1]
Wide bandwidth channels desired to support high throughput requirements
At the same time, large number non-overlapping channels desired to support high QoS requirements
  To avoid co-channel interference
Current UNII spectrum allows only
  Six 80 MHz channels
  Two 160 MHz channels
Additional unlicensed use of 5.35-5.47 GHz and 5.85-5.925 GHz would allow
  Nine 80 MHz channels
  Four 160 MHz channels
144
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
IEEE channel #
20 MHz
40 MHz
80 MHz
160 MHz
UNII-1
UNII-2
UNII-2
UNII-3
5250
MHz
5350
MHz
5470
MHz
5725
MHz
NEW
96
92
88
84
80
76
72
68
169
173
177
181
5825
MHz
5925
MHz
NEW
Currently available channels
New channels

## Slide 5: Frequency Spectrum Usage Scenario
Terminologies
  Legacy frequency spectrum: currently available unlicensed frequency spectrum
  Legacy STA : it supports only the legacy frequency spectrum and it does not support the newly opened frequency spectrum
  HEW STA and AP: it supports both the legacy frequency spectrum and the newly opened frequency spectrum
Scenario 1) The primary channel of HEW AP is located in the newly opened frequency spectrum
Scenario 2) The primary channel of HEW AP is located in the legacy frequency spectrum

## Slide 6: Frequency Spectrum Usage Analysis (1/2)
If the primary channel of HEW AP is located in the newly opened frequency spectrum
  Pros: The spectrum efficiency of the newly opened frequency spectrum is the most optimized.
  Cons: The legacy STA is not supported. For supporting the legacy STA, AP shall have multiple radio interfaces.
20 MHz
40 MHz
80 MHz
160 MHz
UNII-1
UNII-2
UNII-2
UNII-3
5250
MHz
5350
MHz
5470
MHz
5725
MHz
NEW
5825
MHz
5925
MHz
NEW
HEW BSS Operation (20MHz/40MHz/80MHz/160MHz)

## Slide 7: Frequency Spectrum Usage Analysis (2/2)
If the primary channel of AP is located in the legacy frequency spectrum
  Pros: AP can easily support both legacy STA and HEW STA.
  Cons: The newly opened spectrum is used only for a secondary “X” MHz channel. So, it is hard to fully utilize the newly opened frequency spectrum.
20 MHz
40 MHz
80 MHz
160 MHz
UNII-1
UNII-2
UNII-2
UNII-3
5250
MHz
5350
MHz
5470
MHz
5725
MHz
NEW
5825
MHz
5925
MHz
NEW
HEW BSS Operation (20MHz/40MHz/80MHz/80+80MHz)

## Slide 8: Discussion
We need other solution for improving the utilization of the newly opened frequency spectrum
  Legacy frequency spectrum and newly opened frequency spectrum are concurrently operated
Candidate technologies
  FDMA (see a next slide), Multi-channel operation
20 MHz
40 MHz
80 MHz
160 MHz
UNII-1
UNII-2
UNII-2
UNII-3
5250
MHz
5350
MHz
5470
MHz
5725
MHz
NEW
5825
MHz
5925
MHz
NEW
HEW BSS Operation (20MHz/40MHz/80MHz/20+20MHz/40+40MHz/80+80MHz)

## Slide 9: Discussion
FDMA
DATA
(HEW AP  Legacy STA)
Legacy Frequency Spectrum
Newly Opened Frequency Spectrum
DATA
(HEW AP  HEW STA)
PHY Preamble
PHY Preamble
DATA
(HEW AP HEW STA)
PHY Preamble
PHY Preamble
DATA
(HEW AP Legacy STA)
Downlink FDMA
Uplink FDMA

## Slide 10: Conclusion
It is expected that new unlicensed frequency spectrum will be opened in the near future
At this moment, available solution for supporting both the legacy frequency spectrum and the newly opened frequency spectrum is to use two different radio interfaces
But, in the future, it is important to improve the utilization of the newly opened frequency spectrum with a low cost
20 MHz
40 MHz
80 MHz
160 MHz
UNII-1
UNII-2
UNII-2
UNII-3
NEW
NEW
Legacy BSS (1st interface)
HEW BSS (2nd interface)

## Slide 11: References
[1] https://mentor.ieee.org/802.11/dcn/13/11-13-0282-03-0000-802-5-ghz-tutorial.pptx