## Slide 1: HEW Scenarios and Goals
Date: 2013-04-13
Authors:

## Slide 2: Introduction
The HEW study group was formed
  Request approval by IEEE 802 LMSC to form an 802.11 Study Group to consider High-efficiency WLAN [as described in doc 11-13-0339r2] with the intent of creating a PAR and five criteria.
  Do you support starting a new study group called “high efficiency WLAN” to enhance 802.11 PHY and MAC in 2.4 and 5GHz with a focus on:
    Improving spectrum efficiency and area throughput
    Improving real world performance in indoor and outdoor deployments
      in the presence of interfering sources, dense heterogeneous networks
      in moderate to heavy user loaded APs
    Result: 128/1/27
This presentation provides our view of the HEW goals

## Slide 3: HEW Scope I - Background
Past 11b/g/n/ac focused on optimizing link throughput in isolated BSS. E.g., 11ac PAR:
  5.2 Scope of Proposed Standard: This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control Layer (MAC) that enable modes of operation capable of supporting:
    A maximum multi-station (STA) throughput (measured at the MAC data service access point), of at least 1 Gbps and a maximum single link throughput (measured at the MAC data service access point), of at least 500 Mbps.
    Below 6 GHz carrier frequency operation excluding 2.4 GHz operation while ensuring backward compatibility and coexistence with legacy IEEE802.11 devices in the 5 GHz unlicensed band.
  Purpose of Proposed Standard: The purpose of the amendment is to improve the 802.11 wireless local area network (LAN) user experience by providing significantly higher basic service set (BSS) throughput for existing WLAN application areas and to enable new market segments for operation below 6 GHz including distribution of multiple multimedia/data streams.

## Slide 4: HEW Scope II – OBSS
HEW focus should be on improving MAC and PHY for operation in networks with dense STAs and BSSs that potentially interfere with each other
  Real world networks often consist of OBSSs and large numbers of STAs
    Several well known examples: apartments, enterprise, stadiums, malls, airports…
    2.4GHz already congested, and likely 5GHz to be congested soon
    Increased of P2P services in the same area.
    802.11 enabled smartphones/tablets is the fastest growing market
  There is much evidence of issues due to OBSS/dense deployments
    Insufficient per-user throughput for common applications
  MAC/PHY operations of current 802.11 is not designed/optimized for efficient OBSS and dense network operation
  Solutions to these issues will have a broad sets of applicability

## Slide 5: HEW Scope III – User Experience
HEW focus should be on improving per-user experience; overall network efficiency/throughput also to be improved
  HEW evaluation metrics should include per-user throughput metrics
    Important to (somehow) look at the ‘tail’ performance in the per-user throughput CDF
    Metric need be designed according to per-user traffic specifications
  HEW evaluation metrics should include aggregate throughput
    Subject to per-user throughput improvements/QoS limitations, i.e. support higher throughput for more users, not just higher throughput for a few user
  Performance improvement can be compared to 11n/ac in the respective bands
11ac
HEW
CDF
Tput

## Slide 6: Scenarios and Evaluation
HEW SG should define reference scenarios and target metrics for
  Assessing feasibility
  Evaluate quality of solutions to be adopted in the standard
Detailed simulations to be used for evaluating candidate solutions
  Need to agree on simulation methodology
The following 3 scenarios are proposed for representing the most relevant classes of dense networks issues
  Residential
  Enterprise
  Outdoor

## Slide 7: Residential
Apartment building with several apartments
A closed BSS per apartment
  Only users in the apartment can connect with the apartment’s AP
Random APs locations
Several STAs per each apartment
Traffic profile defined per STA
  Similar to 11ac, but with updated profiles to reflect current/future profiles; include P2P
This scenario will highlight realistic issues related to worst case interference due to closed unplanned deployments

## Slide 8: Enterprise
Enterprise building
One ESS constituting of several APs
  Users can connect with any AP (‘open’ APs)
  May include also an interfering (closed) ESS
Planned (regular) APs locations
Several STAs per AP
Traffic profile defined per STA
  Similar to 11ac, but with updated profiles to reflect current/future profiles; include P2P
This scenario will highlight realistic issues and solutions in open networks where a certain level of control is possible

## Slide 9: Outdoor
Dense outdoor deployment
One ESS constituting of several APs
  Users can connect with any AP (‘open’ APs)
  May include also an interfering (closed) ESS
Several STAs, with mobility
Outdoor channel with longer delay spread than indoors
Traffic profile derived from typical mobile applications (TBD)
This scenario will highlight realistic issues in dense outdoor networks with mobility

## Slide 10: Summary
HEW should focus on addressing dense networks with potentially high OBSS interference
  Need to agree on reference scenarios that are representative of real world deployments and use cases. These scenarios will be used to identify issues and evaluate solutions
    Residential, Enterprise, Outdoor
  Need to define traffic models
HEW should focus on improving per-user throughput; aggregate throughput also important
  Need to agree on exact metrics for evaluation of solutions quality
A detailed simulation methodology need be agreed and used for assessing the quality of candidate solutions