## Slide 1: Full-duplex Technology for HEW
Date: 2013-07-14
Authors:

## Slide 2: Abstract
As part of the effort to develop a PAR and 5C for High Efficiency WLAN (HEW), the IEEE 802.11 HEW Study Group is collecting inputs from the 802.11 WG members on new PHY and MAC technologies to increase the spectrum efficiency and area throughput of 802.11 WLANs.
This presentation introduces the full-duplex (FD) technology that makes it possible to double the instantaneous PHY spectral efficiency.
The goal of this presentation is to start a reflexion process in the HEW SG about the relevance/timeliness of this technology for HEW.

## Slide 3: Motivation (1)
2.4 and 5GHz spectrum scarcity
Steady, seemingly unstoppable increase in throughput requirements
Existing extensions cannot “stretch” infinitely:
  Higher bandwidth and/or more frequency bands
  Larger constellation size
  More spatial streams
Innovative solutions needed at PHY, MAC and topology level

## Slide 4: Motivation (2)
Most (TDD) wireless bi-directional links deployed today are half-duplex (HD):
Throughput can significantly be increased if the two nodes are able to transmit simultaneously. Full-duplex is an emerging radio transmission paradigm.
  ? Considered in 802.11 HEW SG ?
TX data (from STA1 to STA2)
RX data (from STA2 to STA1)
TX data (from STA1 to STA2)
RX data (from STA2 to STA1)

## Slide 5: Motivation (3)
Pros
  Increased spectral efficiency
  Up to 100% link capacity improvement over traditional half-duplex system
  More flexibility in spectrum usage
  Reduced air interface delay
  May ease / solve the hidden node problem
  . . .
Cons
  More complex antenna / transceiver / DSP design
  Simpler for SISO than for MIMO
  MAC and protocol must be adapted
  . . .

## Slide 6: Taxonomy (1)
AP is full-duplex
STA is full-duplex
AP is full-duplex
STAs are half-duplex

## Slide 7: Taxonomy (2)
Device start transmitting, then receives
Device starts receiving, then transmits
Synchronous
Impacts the estimation of desired channel / self-interference channel
TX data (from STA1 to STA2)
RX data (from STA2 to STA1)
TX data (from STA1 to STA2)
RX data (from STA2 to STA1)
TX data (from STA1 to STA2)
RX data (from STA2 to STA1)

## Slide 8: Challenges and solutions (1)
Self-interference mechanisms in full-duplex transceiver
Example budget:
  20MHz bandwidth and 10+5 dB NF: noise floor at -86dBm/20MHz
  PT = +10dBm
   roughly 10 + 86 = 96 dB of self-interference rejection needed
  Observations:
    Self-interference rejection requirement is harder for higher PT
    Self-interference rejection requirement is easier for larger bandwidth

## Slide 9: Challenges and solutions (2)
[DUPLO-D1.1]

## Slide 10: Challenges and solutions (3)
Three main cancellation techniques
  At the antenna level
    Antenna layout minimizes leakage from TX antenna into RX antenna
    Circulator with high isolation if common TX and RX antenna
  RF/IF/analog baseband cancellation
    Sample of (non-ideal) transmitted signal is injected with opposite phase (and delay?) into the receiver
  Digital baseband cancellation
    Scaled/delayed/rotated version of ideal TX baseband signal is subtracted from received baseband
    Can be implemented per sub-carrier
In practice combination of above techniques is needed to achieve 80-110 dB self-interference cancellation

## Slide 11: Challenges and solutions (4)
Cancellation requires some form of “channel estimation” from TX to RX
  Can be implicit for RF/IF/analog cancellation
  Probably explicit for digital cancellation
SISO transceiver needs to cancel ONE TX leakage
NTX x NRX MIMO transceiver needs to cancel NTX leakages into all NRX RX branches:  more complex

## Slide 12: State-of-the-Art (1)
Many groups and oganizations are very active on FD and have demonstrators at various levels of maturity
  Rice Univ.: http://warp.rice.edu/trac/wiki/about
  Stanford Univ.: http://sing.stanford.edu/fullduplex/
  Princeton Univ.: http://scenic.princeton.edu/pt-full-duplex.php
  Univ. Waterloo: http://www.cst.uwaterloo.ca/twoWayWireless.php
  IMEC
  . . .
  European FP7 project DUPLO
    Partners: Renesas Mobile, Univ. Twente, Univ. Oulu, Univ. Surrey, IMEC, Thales, TTI
    http://www.fp7-duplo.eu/index.php
See also upcoming CFP for JSAC on FD:
  http://www.jsac.ucsd.edu/Calls/Full-duplexCFP.pdf

## Slide 13: State-of-the-Art (2)
Self-interference rejection requirements: 80 to 110 dB
Antenna-level cancellation: 25 to 40 dB (a)
RF/IF/analog: 20 to 30 dB (b)
Digital baseband: 20 to 30 dB (c)
Numbers from:
(a): Univ. Waterloo, (b): Stanford Univ. (active balun), (c): Stanford Univ. (time dependent)

## Slide 14: Example of FD in access coordination
[DUPLO-D1.1]

## Slide 15: Example of FD in access coordination
[DUPLO-D1.1]

## Slide 16: Example of FD in access coordination
But interference regions are different

## Slide 17: Qualitative impact on metrics
PHY layer
  signal-to-noise-and-interference ratio (  )
MAC layer
  MAC delay (  )
  Link reliability (  )
Network layer
  Achievable throughput (  )
  End-to-end delays (  )
  Node buffer space (  )
  Delay jitter (  )
  Packet loss ratio (  )
  Energy expended per packet (  )
  Route lifetime (  )

## Slide 18: Best use cases
Full-duplex is more suitable for
  Short range wireless links (because of lower PT)
  Ad hoc links
  Relaying
  Small cells

## Slide 19: Conclusions
Full-duplex is an emerging radio paradigm that has the potential to improve the efficiency of future WLANs.
Good results have been booked by several organizations and more to come from research projects.
Full-duplex can be beneficial to certain HEW use cases.

## Slide 20: References
13/0339r10 “High-efficiency WLAN Straw poll”
13/0331r5 “High-Efficiency WLAN”, Laurent Cariou (Orange)
FP7 DUPLO project: http://www.fp7-duplo.eu/index.php
[DUPLO-D1.1]: INFSO-ICT-316369 DUPLO-Report D1.1, System Scenarios and Technical Requirements for Full-Duplex Concept, April 2013, http://www.fp7-duplo.eu/images/docs/Deliverables/D1_1_v_1.0.pdf.