## Slide 1: CC9 Clarification regarding CID800
Date: 2013-07-18
Authors:

## Slide 2: Abstract
Clarification of the accuracy of partial TSF timer value concerning short beacon.

## Slide 3: Partial TSF timer accuracy
Base standard says; The accuracy of the TSF timer shall be no worse than ±0.01%.
Current draft 0.1 additionally says; The accuracy of the TSF timer shall be no worse than ±0.01%. with respect to the last 4 bytes of the TSF.

## Slide 4: Timer accuracy difference: example 1
TSF Timer is supposed to be used as lap time function of a stop watch, for example; t1
6 | 4 | 9 | 2 | 1 | 3 | 7 | 8
Timer value at a time t1
6 | 4 | 9 | 3 | 1 | 0 | 9 | 1
Timer value at a time t2
0 | 0 | 0 | 0 | 9 | 7 | 1 | 3
Timer value difference
Accuracy of ±0.01% max means; 9713 ×10-4 → 0.9713
time
Timer value at a time t1
Timer value at a time t2
9 | 7 | 1 | 3
Timer value difference
Accuracy of ±0.01% max means; 9713 ×10-4 → 0.9713
time
1 | 3 | 7 | 8
1 | 0 | 9 | 1
No difference

## Slide 5: Timer accuracy difference: example 2
TSF Timer is supposed to be used as lap time function of a stop watch, for example; t1
6 | 4 | 9 | 2 | 1 | 3 | 7 | 8
Timer value at a time t1
6 | 4 | 9 | 4 | 1 | 0 | 9 | 1
Timer value at a time t2
0 | 0 | 0 | 1 | 9 | 7 | 1 | 3
Timer value difference
Accuracy of ±0.01% max means; 19713 ×10-4 → 1.9713
time
Timer value at a time t1
Timer value at a time t2
9 | 7 | 1 | 3
Timer value difference
Accuracy of ±0.01% max means; 9713 ×10-4 → 0.9713
time
1 | 3 | 7 | 8
1 | 0 | 9 | 1
orders of magnitude higher accuracy
in case of much longer period

## Slide 6: Short beacon TSF timer value
Partial TSF Timer value for short beacon
No need to say any specific accuracy in terms of partial TSF timer value
TSF Timer : 8 octet → 5 bn years
Partial TSF Timer : 4 octet → 1.2 hour
Still long enough
for the assumed period of short beacon
264
232

## Slide 7: Discussion
Any missing factors?