## Slide 1: CC9 Possible Integration with TSF Timer accuracy regarding CID773 & 774
Date: 2013-07-18
Authors:

## Slide 2: Abstract
TSF timer accuracy element has been introduced to indicate the accuracy of TSF timer in transmitting STA, which is no worse than 100ppm specified in the base standard, IEEE802.11-2012.
TSF accuracy related information includes an absolute accuracy of initial tolerance and a relative stability which is the sum of aging rate and worst temperature drift after peer TSF timer has synchronized with it, and maybe some other useful parameter in future.
For this end, TSF timer accuracy field is additionally defined for the stability and future use of expansion.

## Slide 3: TSF timer accuracy
Base standard says; The accuracy of the TSF timer shall be no worse than ±0.01%.
7bit field is sufficient to specify 100ppm (0.01%).
    TSF Timer Accuracy field of TSF Timer Accuracy Element [8.4.2.170p]
    TSF Timer Accuracy field encoding
Element ID(1 Octet) | Length(1 Octet) | TSF Timer Accuracy (1 Octet)
Bit 0-5 | Bit 6 | Bit 7 | Usage
1-127 |  | 0 | Absolute Accuracy (1-100) in unit of ppm
1-63 | 0 | 1 | Stability (1-50) in unit of ppm (for during TBTT)
1-63 | 1 | 1 | Reserved

## Slide 4: Straw Poll
Do you agree to extend TSF Timer Accuracy field by limiting the accuracy value to 7bit to accommodate other relating information like TSF Stability than the absolute (TSF) Accuracy for future usage?
Yes
No
Abstain

## Slide 5: Straw Poll
Do you agree to integrate the TSF Stability information and the reserved future usage as described in page 3 ?
Yes
No
Abstain

## Slide 6: Reference
[1] 11-12/130r0 “Beacon Reception of Long Sleeper”