## Slide 1: HEW Evaluation Metrics Suggestions
Date: 2013-9-16
Authors:
Name | Affiliation | Address | Email
Yonggang Fang | ZTETX | San Diego, USA | yfang@ztetx.com
Bo Sun | ZTE | Xi An, China | sun.bo1@zte.com.cn
Zhendong Luo | CATR | Beijing, China | luozhendong@ritt.cn
Meng Yang | CATR | Beijing, China | yangmeng@ritt.cn

## Slide 2: Introduction
HEW SG
  IEEE 802 LMSC approved formation of 802.11 Study Group to investigate High-efficiency WLAN (HEW) in March meeting of 2013.
  The goal of HEW SG is to improve 802.11 PHY and MAC layers performance in frequency bands of 2.4 and 5 GHz with a focus on:
    spectrum efficiency and area throughput improvement
    real world performance improvement in indoor and outdoor deployments
      in the presence of interfering sources, dense heterogeneous networks
      in moderate to heavy user loaded APs

## Slide 3: Introduction
HEW SG (continued)
  In previous meetings, presentations submitted to HEW for considerations include
    Use cases and traffic models
    Efficiency issues in the existing WLAN
    Channel models and evaluation methodology
    Suggested improvements
  This contribution suggests evaluation metrics to formalize a way to measure the performance of existing WLAN and future HEW.
Slide 3

## Slide 4: HEW Evaluation Targets
HEW needs to consider measurements and improvements on
  efficiency of isolated BSS, which is more focusing on evaluation of technology in the ideal scenario.
  efficiency on overlapping BSS, which is used to evaluate the system level performance in the real world, including overloaded scenario .
  user experience, which is to evaluate user acceptance level of communication network.
Slide 4
Current 11
HEW
CDF
Tput

## Slide 5: HEW Evaluation Scenarios
HEW evaluation could be performed in following scenarios
  Outdoor deployment scenario
    It is OBSS in medium or high density such as in Train/Metro stations
    Measurements should consider the area throughput with stations in low mobility.
  Indoor/Outdoor deployments scenario
    It is OBSS in the dense urban apartments, stadiums, airports and enterprise environments
    Measurements should consider the area throughput with stations in nomadic
  It should consider: planned deployment, and unplanned deployment.
Slide 5
Aspects | Considerations
Outdoor high density (both AP and STA) | Outdoor model, OBSS interference, low mobility,
Indoor high density (both AP and STA) | Indoor model, OBSS interference, nomadic,

## Slide 6: HEW Evaluation Methodology
System Configurations
  For multi-layer network configuration
    Frequency reuse factor = 1 and = 3 at 5 GHz Band.
  Antenna configuration
    Baseline: 2 antenna at AP, 1 antenna at STA; (0 – 6dBi).
    Advanced: 4 antenna at AP; 2 at STA; (0 – 6dBi).
  SU and MU configurations
    Evaluate the point to point situation.
Slide 6

## Slide 7: HEW Evaluation Methodology
Traffic Models
  Full buffer models (for simplicity)
  Non-full buffer models (for real world) – TR36.814
  IP based traffic
    Half-duplex transmission: different split of uplink and downlink traffic loads
    Full-duplex transmission: simultaneous uplink and downlink transmission
  Mixed traffic model
    Comprise a large packets (web, video, etc) and small packets (ACKs)
  Maximum number of served stations
    Light load: traffic should be finite buffer (burst) and a single connection is not overloading the system.
    Heavy load:
    Overloaded:
Slide 7

## Slide 8: HEW Evaluation Metrics – Link Level
Receiver Performance Measurements
  RF Receiver Sensitivity and Dynamic Range
    Minimum received power measured at the station antenna connector at which the frame error rate (FER) does not exceed a specified value (dBm / BW)
    The receiver dynamic range is the input power range at the station antenna connector over which the FER does not exceed a specific value (dB)
  Adjacent Channel Selectivity
    A measurement of the ability to receive a signal on the assigned frequency channel in the presence of another signal that is offset from the center frequency of the assigned channel.
  Self-Interference Suppression
    A measurement of the ability to receive a signal on the assigned frequency channel in presence of signal that is transmitted from its transmitter on the same frequency channel (full-duplexer)
Slide 8

## Slide 9: HEW Evaluation Metrics – Link Level
Transmitter Performance Measurements
  Frequency Accuracy
  Link Adaption
    Select proper MCS based on RF condition including evaluating condition of low SNR and congestion.
  Radiated Spurious Emissions
    Measure spurious emissions generated or amplified in a receiver and radiated by the antenna, housing and all power, control, and audio leads connected to the receiver.
Slide 9

## Slide 10: HEW Evaluation Metrics – Link Level
MAC Efficiency Measurements
  PHY Throughput :
    payload transmitted at PHY layer / the time to transmit the payload
  MAC Throughput :
    payload transmitted at MAC layer / the time to transmit the payload
  MAC Efficiency = MAC throughput / PHY throughput
    MAC efficiency should be measured with bi-direction in full-buffer and different loading in
      Point to point,
      Point to multi-points
  Note: the idle time is not included.
Slide 10

## Slide 11: HEW Evaluation Metrics – System Level
Spectrum Efficiency Measurements
  Spectrum efficiency is measured in bps/Hz.
  Medium Utilization
    It is to measure utilization (occupancy ratio) of the medium.
    Transmission time / (transmission + idle time)
  The spectrum efficiency should also consider to maximize the utilization of all available spectrum, including balancing loads among different frequency channels.
Slide 11
Freq.
Time
802.11a
802.11n
40 MHz
802.11ac
80 MHz
HEW
Capable
STA
HEW
Capable
STA
HEW
Capable
STA
HEW
Capable
STA
or,
802.11ac
160 MHz
Ch.1
Ch.2
Ch.3
Ch.4
Ch.5
Ch.6
Ch.7
Ch.8

## Slide 12: HEW Evaluation Metrics – System Level
Throughput Measurements
  Single user throughput
    It needs to measure 5 percentile and 95 percentile user throughput in the center of cell and at the edge of cell.
  Network Capacity
    This measurement is to evaluate the system level capacity measured with 95 percentile together with 5 percentile for robustness in the network.
    BW (Hz) x BSS Spectrum Efficiency (bps/Hz/BSS) x # of BSS
Slide 12

## Slide 13: HEW Evaluation Metrics – System Level
Robustness Measurements
  The robustness of connection is to evaluate the wireless connection reliability and strategy in different scenario.
    Strategy for association could be
      always connected or
      connected with minimum rate, or
      blocked when the admitted data rate is not met.
  Maximum supported active transmission stations (at minimum data rate or average data rate according to different profiles)
  Successful transmission ratio (or re-trial rate) for different access category and profiles
Slide 13

## Slide 14: HEW Evaluation Metrics – System Level
Availability (or Outage)
  This measurement is more focusing on the system level communication performance in OBSS. Even the radio link signal is good, the communication link may not be available due to high congestion, overloading or interference from neighbor BSS.
    Percentage of the transmit packet without response in total transmissions.
Slide 14

## Slide 15: HEW Evaluation Metrics – System Level
User Experience Measurements
  Network selection and association latency (ms)
    Measure the delay of initial network acquisition and association
  Association Successful Ratio
  Data transmission latency (ms)
    MAC latency
      STA initiated transmission
      AP imitated polling transmission
    Network latency (ms)
    QoS latency (ms)
      Voice and video streaming latency
      BE latency
Slide 15

## Slide 16: HEW Evaluation Metrics – System Level
Network Performance Measurements
  Handoff latency (ms)
    This measurement is to measure the user performance of service interrupt during the handoff when re-association from one AP to another (re-selecting network)
      Active handoff from one AP to another (seamless handoff)
      Handoff to other frequency channel in re-association or active handoff
  Handoff Successful Ratio
    Service continuity with minimum QoS guarantee or
    Without service continuity
Slide 16

## Slide 17: References
11-13-0657-06-0hew-hew-sg-usage-models-and-requirements-liaison-with-wfa
11-13-0722-01-0hew-hew-evaluation-methodology
11-13-0764-01-0hew-full-duplex-technology-for-hew
11-13-0765-02-0hew-co-time-co-frequency-full-duplex-for-802-11-wlan
11-13-0804-00-0hew-impact-of-network-configuration-on-quality-of-experience-in-wlan-networks
11-13-0805-02-0hew-on-definition-of-dense-networks-and-performance-metric
11-13-0847-01-0hew-evaluation-criteria-and-simulation-scenarios
11-13-0854-01-0hew-consideration-on-efficiency-enhancement
11-13-0869-00-0hew-simulation-scenarios-and-metrics-for-hew
Slide 17