## Slide 1: Tag Stacking Problem and Options
Date: 2013-09-17
Authors:

## Slide 2: Abstract
This presentation discusses payload encoding and the conversion thereof in relation to P802.11ak.

## Slide 3: Background
802.11 and the rest of the world use different frame payload encodings. 802.11 uses LLC (LSAP-LSAP-Control) encoding while the rest of the world uses Length/Type encoding.
This is not a problem for simple payloads as usually occur at the edge of the network. But, in the general case of a payload with multiple tags (VLAN, congestion, security, proprietary, etc.), including future tags yet to be defined, it is not possible to convert from one to the other which might be required on entry to or exit from an 802.11ak link.
To fix this requires a frame format change, at least under some circumstances.

## Slide 4: The Question:
The diagram below is from 802.11-2012 Table P-3.
Does anyone use this format? Or any other cases of stacked SNAP/LLC encoding? If so, please tell TGak.
Some proposed solutions to the problem on the previous slide prohibit the use of this encoding.
Slide 4
Norman Finn, Cisco Systems
. 6 2 L 6 2 M
EtherType
81-00
Tag value
87-65
SNAP
AA-AA-03-00-00-00
08-06
EtherType
IP ARP packet
data
SNAP
AA-AA-03-00-00-00

## Slide 5: References
For further discussion of this topic, come to the TGak session tomorrow, Thursday, AM1.
More detailed discussion of some aspects of these issues is in document 11-13/0952r2.
The current text of P802.1Qbz Draft 1.3 contains a new tag stacking scheme. P802.1Qbz has passed Task Group Ballot with no “Disapprove” votes.

## Slide 6: Encoding Alternatives
Such a payload could be encoded in a new scheme, keeping one initial LLC, as:
Or, using entirely Length/Type encoding in 11ak as:
Slide 6
Norman Finn, Cisco Systems
. 6 2 L 2 M
EtherType
81-00
Tag value
87-65
SNAP
AA-AA-03-00-00-00
08-06
EtherType
IP ARP packet
data
2 L 2 M
EtherType
81-00
Tag value
87-65
08-06
EtherType
IP ARP packet
data

## Slide 7: The Options
Assume it is impractical to change the rest of the world to use LLC or to change all of 802.11 to use Length/Type. Then two possibilities are:
Change all 802.11 payloads so that they always start with one LLC but any subsequent encodings in that payload are Length/Type.
  This is the current 802.1Qbz proposal.
Change some 802.11 payload (at least payloads on 802.11ak links) so that they are completely Length Type encoded.
  This is a possible alternative.

## Slide 8: End-to-end tag stacking today All tags must be translated at once by B3
B5
B4
B3
B1
E1
E2
data
Q
CA
data
Q
S
CA
B2
data
Q
S
CA
BA
I
data
Q
S
CA
BA
I
data
Q
S
CA
data
CA
LT
L/T
L/T
LLC
LLC
LLC
LLC
LLC
LLC
LLC
LLC
LLC
L/T
L/T
L/T
L/T
L/T
802.1Q decoder ring: BA = Backbone Addresses, I = I-tag, CA = Customer Addresses, S = Service VLAN tags, Q = Customer VLAN tags.
LLC encoding on LLC media
Length/Type encoding on L/T media

## Slide 9: 802.1Qbz end-to-end tag stacking method One translation per tag or media change
B5
B4
B3
B1
E1
E2
data
Q
CA
data
Q
S
CA
B2
data
Q
S
CA
BA
I
data
Q
S
CA
BA
I
data
Q
S
CA
data
CA
LLC encoding on LLC media
Length/Type encoding on L/T media
L/T
L/T
L/T
L/T
L/T
L/T
L/T
L/T
LLC
L/T
LLC
LLC
L/T
L/T
L/T
L/T
L/T
802.1Q decoder ring: BA = Backbone Addresses, I = I-tag, CA = Customer Addresses, S = Service VLAN tags, Q = Customer VLAN tags.

## Slide 10: Old and new tag stacking
NOW
All tags and original payload are LLC encoded
One bridge must fix all tags and original payload
Cannot introduce new end-to-end tags
Most frames 6 bytes longer per tag
802.1Qbz proposal
First tag or payload is LLC and rest of frame is Length/Type
Each LLC bridge fixes one tag or payload
Can introduce new end-to-end tags
Most frames 6 bytes shorter per tag