## Slide 1: System Level Simulation Parameters
Date: 2013-11-11
Authors:

## Slide 2: Introduction
In evaluation methodology document [1], three tools are defined to enable the assessment of proposed HEW techniques performance and gain relative to 11ac;
  PER Simulation
  PHY System Simulation
  MAC System Simulation
In channel model document [2], following channel models are proposed to used for HEW evaluation;
  Indoor channel model: TGn/TGac channel model [5], [6]
  Outdoor channel model: ITU Channel [4]
    HEW design shall ensure that Wi-Fi works well under UMi
    HEW design should ensure that Wi-Fi still works under UMa (connection is supported but reduced performance is possible)
In this contribution, we provide parameters/models need to be defined especially for system level simulation based on simulation scenario document [3] and ITU document [4].

## Slide 3: Basic Parameters Based on [3], [4]
Topology Description
  Include inter-cell(?) distance for scenario 3 and 4
AP location, AP antenna height
STA location
Minimum distance between STA and serving AP
  For 0dBi antenna gain AP, we may not need this parameter.
Number of STA and STA type
  Portion of indoor Users when AP is in outdoor (O-to-I): Simulation Scenario 4 only (Note that in UMi channel model, this is 50%)
Center Frequency and BW
Traffic Model
  Traffic type, data size, data arrival time, outage condition, …
Thermal noise level
Cable Loss

## Slide 4
 | Residential | Enterprise | Indoor Small BSSs | Outdoor Large BSS
Topology Description | Multi-floor building • 5 floors, 3 m height in each floor • 2x10 rooms in each floor • Room size:10m x 10m x 3m | Office floor configuration (see Figure 1) a. 8 offices b. 64 cubicles per office c. Each cubicle has 4 STAs | BSSs are placed in a regular and symmetric grid as in Figure 5. Each BSS in Figure 5 has the following configuration : BSS radius: R meters (7m [#1248] / 12m [Stadium, #722,#1079] TBD) Inter-cell distance (ICD): 2*h meters h=sqrt(R2-R2/4) | Outdoor street deployment Overlap of 3 operators BSS layout configuration Planned deployment: 19 hexagonal grid as in Figure 8. With ICD: 2*h meters (130m, TBD) h=sqrt(R2-R2/4) R meters defined as the distance for MCS0 sensitivity
APs location, AP antenna heights | One AP per apartment, in random location (in three dimentional? Or in two dimentional while fixed z location?) within the apartment | Each AP is located at the center of the office Installed on the ceiling at (x=10,y=10,z=3) | AP is placed at the center of the cell with antenna height TBD m. | Place APs on the center of the each BSS, +/- an offset with TBD standard deviation with antenna height TBD m.
STAs location | In each room that has an AP, place N+M STAs in random xy-locations (uniform distribution) at 1.5m above the floor level. | Placed randomly in a cubicle (x,y,z=1) (In the figure 4, x and y are 2.) STA1: laptop STA2: monitor STA3: smartphone or tablet STA4: Hard disk Keyboard/mouse (TBR) | 30 [#1248] -72 [Stadium, #722,#1079] (TBD) STAs are placed randomly #1248 / in a regular grid (#722,#1079) in a BSS | “50-100” STAs are placed randomly in a BSS.
Note: Black text is from [3]. Red text is proposed modification/addition

## Slide 5
 | Residential | Enterprise | Indoor Small BSSs | Outdoor Large BSS
Minimum distance between STA and serving AP (? TBD) | TBD m | TBD m | TBD m | TBD m
Number of STA and STAs type | N STAs in each room. STA_1 to STA_{N-M}: HEW STA_{N-M+1} to STA_{N} : non-HEW (N = TBD, M = TBD) | HEW Non-HEW? TBD N STAs in each cubicle. STA_1 to STA_{N-M}: HEW STA_{N-M+1} to STA_{N} : non-HEW (N = TBD, M = TBD) | {STAs 1 to N: HEW STAs} [STAs N+1 to TBD: non-HEW STAs] N STAs in each BSS. STA_1 to STA_{N-M}: HEW STA_{N-M+1} to STA_{N} : non-HEW (N = 30 [#1248] -72 [Stadium, #722,#1079] (TBD), M = TBD) | {STAs 1 to N: HEW STAs} [STAs N+1 to TBD: non-HEW STAs] N STAs in each BSS. TBD % of users are indoor users. (Note that in UMi channel model, this value is 50%.) STA_1 to STA_{N-M}: HEW STA_{N-M+1} to STA_{N} : non-HEW (N= 50 - 100 TBD, M = TBD)
Center frequency and BW | [20MHz BSS at 2.4GHz, 80MHz BSS at 5GHz] | [20MHz BSS at 2.4GHz, 80 MHz BSS at 5GHz] | {20MHz at 2.4GHz, 80 MHz at 5GHz} | {20MHz at 2.4GHz, 80 MHz at 5GHz}
Thermal Noise Level | -174 dBm/Hz | -174 dBm/Hz | -174 dBm/Hz | -174 dBm/Hz
Cable Loss | TBD dB | TBD dB | TBD dB | TBD dB
Note: Black text is from [3]. Red text is proposed modification/addition

## Slide 6: Channel Related Parameters [4]
Channel model for
  AP-STA
  STA-STA (Interference channel, May be long distance as well)
  AP-AP (Interference channel)
  STA-STA (P2P Link, Probably short distance)
For each channel model, we may need to define
  Delay Spread, AoA, AoD, Number of cluster, Cluster ASD, Cluster ASA, Per cluster shadowing std.
  Correlation distance
  K factor, LoS Probability
Pathloss for
  AP-STA
  STA-STA
  AP-AP (Interference channel)
Shadowing
Penetration Loss (Building, Car, …)

## Slide 7
 | Residential | Enterprise | Indoor Small BSSs | Outdoor Large BSS
Channel Model for AP-STA | TGn channel model B | TGn channel model D | Large open space with small BSSs | {Outdoor, ITU micro} {UMi}, [UMa]
Channel Model for STA-STA (interference channel) | TBD (Simple channel model is preferred) | TBD (Simple channel model is preferred) | TBD (Simple channel model is preferred) | TBD (Simple channel model is preferred)
Channel Model for AP-AP (interference channel) | Same as "Channel Model for AP-STA"? | Same as "Channel Model for AP-STA"? | TBD | TBD
Channel Model for STA-STA (P2P Link) | Same as "Channel Model for AP-STA"? | Same as "Channel Model for AP-STA"? | TBD | TBD
Pathloss for AP-STA | Based on Channel Model for AP-STA | Based on Channel Model for AP-STA | Based on Channel Model for AP-STA | Based on Channel Model for AP-STA
Pathloss for AP-AP (interference channel) | Same as "Pathloss for AP-STA"? | Same as "Pathloss for AP-STA"? | TBD | TBD
Pathloss for STA-STA (P2P Link) | Same as "Pathloss for AP-STA"? | Same as "Pathloss for AP-STA"? | TBD | TBD
Shadowing | Based on Channel Model for AP-STA | Based on Channel Model for AP-STA | Based on Channel Model for AP-STA | Based on Channel Model for AP-STA
Penentration Losses | TBD between apartments TBD between floors | TBD | None | None Based on Channel Model for AP-STA

## Slide 8: AP Related Parameters [3], [4]
Number of AP antenna elements, antenna type (uniform linear array, cross polarization, etc…) and antenna spacing
  Number of transmit antennas
  Number of receive antennas
AP antenna gain (boresight)
AP antenna pattern and antenna orientation
  Only when AP antenna gain is above 0dBi
Maximum AP transmit power
AP noise figure

## Slide 9: STA Related Parameters [3], [4]
Maximum STA transmit power
Number of STA antenna elements
  Number of transmit antennas
  Number of receive antennas
STA mobility model?
  Only for handover related simulation
STA speeds
  Including environment change
STA noise figure
STA antenna gain (boresight)

## Slide 10
 | Residential | Enterprise | Indoor Small BSSs | Outdoor Large BSS
AP # of TX antennas, antenna type and antenna spacing | {4}, ULA, 4 lambda? | {4}, ULA, 4 lambda? | {2, 4}, ULA, 4 lambda? | {2, 4}, ULA, 4 lambda?
AP # of RX antennas | {4} | {4} | {2, 4} | {2, 4}
AP Antenna Gain and Pattern | 0 dBi (Omni Directional) | 0 dBi (Omni Directional) | 0 dBi (Omni Directional) | 0 dBi (Omni Directional)
(Maximum) AP TX Power | {23}dBm | [24dBm] | [max 17dBm] | [30dBm]
AP Noise Figure | 5dB? | 5dB? | 5dB? | 5dB?
(Maximum) STA TX power | {17}dBm | [21dBm] | [max 15dBm] [max 19dBm] | [15dBm]
STA # of TX antennas, antenna type and antenna spacing | {1, 2}, ULA, 0.5 lambda? | {1, 2}, ULA, 0.5 lambda? | {1, 2}, ULA, 0.5 lambda? | {1, 2}, ULA, 0.5 lambda?
STA # of RX antennas | {1, 2} | {1, 2} | {1, 2} | {1, 2}
STA speeds (including environment change) | 3km/h | 3km/h | 3km/h | {3km/h}, [30km/h]
STA Noise Figure | 7dB | 7dB | 7dB | 7dB
STA Antenna Gain and Pattern | 0 dBi (Omni Directional) | 0 dBi (Omni Directional) | 0 dBi (Omni Directional) | 0 dBi (Omni Directional)

## Slide 11: Additional Parameters [3]
MCS
GI
Data Preamble
Primary Channels
Aggregation
Maximum number of retries
CTS/RTS
Rate adaptation method
MIMO Receiver type: MMSE, ML, etc
Scheduling (Can be defined in evaluation document)
EVM (error vector magnitude): 30dB?
…

## Slide 12: Reference
[1] 11-13/1051r1, “Evaluation Methodology ”
[2] 11-13/1135r4, “Summary On HEW Channel Models”
[3] 11-13/1001r4, “HEW SG Simulation Scenarios”
[4] Report ITU-R M.2135-1, “Guidelines for evaluation of radio interface technologies for IMT-Advanced”
[5] 11-03/0904r4, “TGn Channel Models”
[6] 11-09/0308r12, “TGac Channel Model Addendum”