## Slide 1: PHY Abstraction for HEW System Level Simulation
Date: 2013-11-11
Authors:

## Slide 2: Introduction
System simulation has been adopted as a powerful tool in investigating network performance.
  Critical to evaluate HEW, whose target includes improving system and edge-of-network throughput .
  Simulate multiple BSSs simultaneously on the intra- and inter-BSS interactions.
Physical layer abstraction is used to simplify the complicated simulation of a large number of APs and STAs.
  Relieve system simulation from transmitting and decoding real PHY packets, and align simulator behaviors from different companies.
  Predict if a packet can be successively received from instantaneous channel conditions.

## Slide 3: How Does PHY Abstraction Work?
System simulator transmitter “sends” a virtual encoded packet over frequency-selective channels.
  No encoding or signal generation actually happens.
  No packet travels through channels but channel realizations are generated.
System simulator receiver “receives” the virtual packet by calculating the post-processing SINR values per subcarrier.
  Equalizer/MIMO impact on performance kicks in.
PHY abstraction predicts instantaneous PER based on the SINR values (given the current channel realization).
  Namely, a function with a vector of SINR values as input and a PER as output.
  This function depends on the coding scheme (BCC, or LDPC)  one table per coding scheme.
System simulator takes the predicted PER to decide if this virtual packet has passed through.
  Flip a coin based on PER.
This approach has been widely used in IEEE 802.16m [1] and 3GPP [2].

## Slide 4: Challenge on PHY Abstraction
PHY abstraction function maps a vector to a scalar
  f: RNR; where N is the number of SINRs over frequency/time.
This is a very challenging task:
  It is impossible to pre-store the mapping table due to N-to-1 mapping, as well as arbitrary types of fading channels.
  It is, however, fairly easy to store a set of SNR vs. PER tables for AWGN channels (i.e., 1-to-1 mapping).
The solution is to find an AWGN channel at an equivalent SNR level having PER performance the same as the fading channel.
  In other words, map (compress) a vector of SINR values to a single SNR scalar  effective SNR mapping (ESM).
The key factors of ESM are
  (1) simple, (2) accurate, (3) channel independent (the ESM method, and the parameters do not change across different channel types).
  For example, linear/dB average SINR is NOT a good ESM method.

## Slide 5: ESM for PHY Abstraction
Effective SINR Mapping has been adopted in system level simulation for IEEE 802.16m[1] and 3GPP LTE [2,3].
Effective SINR is an average mapped equalizer-output SINR over all subcarriers.
  Hedge factors alpha and beta can be used to calibrate and compensate any residual errors.
OFDM transmission is modeled as an AWGN channel with one effective SINR.

## Slide 6: SINR Mapping Functions
A list of well-known SINR mapping functions
PHY Abstract | SINR Mapping | 
EESM [1, 2, 3] | Exponential mapping | 
MIESM (RBIR) [1, 2, 4] | Mutual information per symbol | 
MMIB [1, 2, 5] | Mutual information per bit | 

## Slide 7: MIESM for BICM
Suppose a SISO channel,
RBIR in the previous table is mutual information for such a SISO channel, achieved by coded modulation.
BICM is widely used for advanced wireless systems including WiFi.
  CM based mutual information (RBIR) is overestimated for BICM.

## Slide 8: MIESM for BICM (2)
Considering BICM, MIESM can be given as [6]
  Referred as “RBIR-BICM”
Mutual information for each bit is given as
Mutual information for this channel use is given by

## Slide 9: Difference of RBIR Mapping
RBIR and RBIR-BICM are close but with some gap.
  At most 1dB apart for 64QAM.

## Slide 10: Performance of PHY Abstraction
11ac, 1x1, 8000 bit per packet, MCS0-MCS7, BCC
  EESM is not considered here without well known parameters for BCC.
  Channel D-NLOS, AWGN
Effective SNR vs. PER curves for D-NLOS are referenced to SNR vs. PER curves for AWGN channels.
  The closer, the better!
All three methods (MMIB, RBIR, RBIR-BICM) provides good PER results referenced to AWGN.
  RBIR-BICM and MMIB (both bit-level MI) are closer than RBIR (symbol level MI) to AWGN performance except MCS0.
  All three methods perform the same for MCS0 (BPSK).

## Slide 11: Performance of PHY Abstraction
The gap between effective SNR to SNR is no more than 0.6dB across MCSs.

## Slide 12: RBIR-BICM Fine Tune
After applying some hedge factors per MCS (basically dB shift), RBIR-BICM can provides almost exact PER results as AWGN.

## Slide 13: Comments on RBIR-BICM
RBIR-BICM matches AWGN performance better than RBIR.
RBIR is easier to extend to high modulation than MMIB for the availability of theoretical expressions.
  Although still requires numerical evaluation (or via Monte Carlo), it does not require any curve fitting/parameter (a_k, c_k) optimization as for MMIB.

## Slide 14: Summary
Both MMIB and RBIR can effectively predict OFDM performance.
RBIR-BICM and MMIB perform better than RBIR referenced to AWGN results.
RBIR-BICM is easier to extend to high modulations than MMIB.
RBIR-BICM with some dB shift can almost exactly match AWGN performance.
Suggest to take RBIR-BICM as the PHY abstraction technique for HEW system simulations.

## Slide 15: References
[1] IEEE 802.16m-08/004r5, Jan. 2009
[2] R1-050680, “Text Proposal: Simulation Assumptions and Evaluation for EUTRA”, 3GPP TSG RAN WG1 #41bis, June, 2005
[3] R1-061626, “LTE Downlink System Performance Evaluation Results”, 3GPP TSG RAN1 #45, May, 2006
[4] 11-13-1131-00-0hew-phyabstraction-for-hew-system-level-simulation
[5] 11-13-1059-00-0hew-phy-abstraction-for-hew-evaluation-methodology
[6] “Bit-Interleaved Coded Modulation”, Giuseppe Caire, Giorgio Taricco, and Ezio Biglieri, IEEE Trans. Of Info. Theory, 1998.