## Slide 1
Date: 2014-01-11
Authors:
Discussion on CID2199
Name | Company | Address | Phone | Email
Carlos Cordeiro | Intel |  |  | Carlos.Cordeiro@intel.com

## Slide 2: CID2199 and goals for this presentation
The purpose of this presentation is to discuss a conceptual resolution to this CID
Text contribution would be crafted after TG agreement
2199 | 10.3.4.1 | 1411 | 32 | Section 10.3.4.1 states that DMG STAs do not support authentication and deauthentication. This appears to be an optimisation that should only apply to cases where the Open Authentication algorithm is used, otherwise 11ad STAs cannot make use of other authentication algorithms such as SAE, Fast BSS Transition and those in 11ai. Even when Open Authentication is in use I'm not sure how multi-band operation is affected by this restriction. | Restrict this optimisation to cases where the Open Authentication algorithm is in use. This will require also changes in other parts of the draft, such as Figure 10-12 which shows authentication and association states.

## Slide 3: Implications of rejecting the comment
As noted by the commenter, by not supporting authentication and deauthentication, “11ad STAs cannot make use of other authentication algorithms such as SAE, Fast BSS Transition and those in 11ai”
Such algorithms could be beneficial for DMG in the future, even though today we do not see market demand

## Slide 4: Proposed resolution 1
Insert the following at the last sentence in 10.3.4.1 “Authentication and deauthentication are not supported by DMG STAs when the Open Authentication algorithm is in use.”
(De)Authentication frames and associated behavior would become mandatory in DMG when Open Authentication is NOT in use
This would cause interoperability problems with legacy 11ad STAs, assuming there are STAs using algorithms other than Open Authentication

## Slide 5: Proposed resolution 2
An alternate resolution might be to define authentication and deuthentication as an optional capability of DMG STAs
This would allow implementations to make use of the capability without breaking interoperability with legacy STAs that implement other algorithms other than Open Authentication (assuming they exist)

## Slide 6: Proposed resolution 2
Define a new “Authentication Supported” capability as part of the DMG Capabilities element
  If set to 0 (default), the STA does not support (de)authentication. Legacy STAs would use this configuration
  If set to 1, then the DMG STA supports (de)authentication and can then make use of existing authentication algorithms.
A DMG STA with Authentication Supported=1 is capable of operating with a DMG STA with Authentication Supported=0
A DMG STA with Authentication Supported=1 would be allowed to perform (de)authentication with a peer STA only if the peer STA also has Authentication Supported=1
 |  | DMG STA B (Responder) | 
 |  | Authentication Supported = 0 | Authentication Supported = 1
DMG STA A (Initiator) | Authentication Supported = 0 | (De)Authentication not performed, i.e., legacy behavior | (De)Authentication not performed, i.e., legacy behavior
 | Authentication Supported = 1 | (De)Authentication not performed, i.e., legacy behavior | (De)Authentication may or may not be performed

## Slide 7: Some additional implications of the proposed resolutions
 | Resolution 1 | Resolution 2
Backward compatible to 11ad | No | Yes
State machine (10.3) description needs to be amended to accommodate new behaviour for DMG STAs | Yes | Yes
In a DMG BSS (where the PCP/AP supports (de)authentication), some STAs might use (de)authentication and some might not | Yes | Yes
A DMG STA needs to first discover the (de)authentication capability of a peer DMG STA before initiating (de)authentication with that peer DMG STA Can be done through DMG Beacon and/or probe exchange | Yes | No