## Slide 1: Long-Term SINR Calibration for System Simulation
Date: 2014-01-20
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com
Jinjing Jiang | Marvell Semiconductor |  |  | 
Yan Zhang | Marvell Semiconductor |  |  | 
Hongyuan Zhang | Marvell Semiconductor |  |  | 

## Slide 2: Overview
A step-by-step calibration was proposed in [1] with high level descriptions.
More details and examples of the first step of statistics-based calibration in this contribution.
Results also provide some insights of the simulation scenario under development.
Simulation Scenario
Static Radio statistics
(S/I distribution)
PHY statistics
(Freq-domain SINR distribution)
PHY Tput calibration
MAC calibration

## Slide 3: Static Radio Characteristics: Long Term SINR
Geometry, or long-term SINR, defines the average quality of reception.
  Expected received (desired) signal power over the sum of the interference power (and noise).
Expected received signal power of (desired or interfering) transmitter
  Include large scale fading (path-loss, shadowing factor)
  Include static transmission/receiving factors (transmit power, antenna gain, cable loss, noise figure, etc)
  Does not include small scale fading.
Propose to use long-term SINR as a static radio characteristic for system simulator calibration.
  Long-term SINR provide a high-level picture of the network (deployment and basic transmitter/receiver/propagation configuration).
  Calibrating long-term SINR aligns the system modeling.
  Long-term SINR is easy to calibrate.

## Slide 4: Definition of Long-Term SINR in WiFi
Contention based channel access in WiFi leads to no strict definition of long term SINR.
  Some rough definition is used.
  A good definition should capture the deployment and long term radio statistics.
Example: DL SINR of STA-m associated with AP-n

## Slide 5: Discussions on Long-Term SINR
DL/UL traffic time ratio models
  Assume αDL+ αUL=1  a fully occupied network
  Case 1: αDL: αUL =1  equal traffic in both way
  Case 2: αDL : αUL =1:NSTA  equal traffic from each STA including AP.
Probability of collision roughly models CSMA

## Slide 6: Tested Long-Term SINR
4 types of long-term SINR are tested in our contribution.

## Slide 7: Uplink Long-Term SINR
Similarly, uplink long-term SINR can be defined as:
  Average UL SINR per AP
  UL SINR per AP-STA link
An example of uplink long-term SINR under equal STA/AP traffic with CSMA off

## Slide 8: Procedure of Statistics Collection
The definition (and the parameters, such as αUL/αDL and PCCA if apply) is selected and fixed before calibration.
For the selected calibration scenario, multiple drops of STA/AP is done for convergence.
In each drop:
  Drop STAs/APs, and associate each STA with an AP.
    Randomly drop or load prefixed locations.
    Fixed association or signal-strength based association
  After STA/AP are dropped and associated, collect the long-term SINR observed at each STA (downlink) and AP (uplink).
After multiple drops:
  Generate the distribution (CDF) of long-term SINR for STAs (downlink) and APs (uplink) respectively collected over multiple drops.

## Slide 9: Simulation Setup
Simulation is based on scenario 1 to 4 in [2].
  Distribution of downlink long-term SINR are plotted as an example.
Detailed/optional simulation assumptions:
  2.4GHz Channel with 20MHz Bandwidth
  Noise Figure: 7dB
  Thermal noise: -174dBm/Hz
  No antenna gain, no cable loss
  Expected received signal power is defined in Appendix.
  CCA threshold: -82dBm
  Randomly drop STAs and APs (if apply)
  Association based on scenarios (fixed for scenario 1-2, signal-strength based for scenario 3-4).

## Slide 10: Scenario 1 – Residential: SINR
AP-AP, AP-STA and STA-STA: channel B
10 STA per BSS
  Scenario 1 is a severe interfered case (CSMA reduces interference by more than 20dB).

## Slide 11: Scenario 2 – Enterprise: SINR
AP-AP, AP-STA and STA-STA: channel D
  Scenario 2 is a sever interfered case (CSMA reduces interference by about 20dB).
  DL/UL traffic impact SINR more with CSMA due to the limited number of strong interfering APs.

## Slide 12: Scenario 3 – Indoor Small BSSs: Received SINR
  Scenario is a severe interfered case (CSMA reduces interference substantially).
  DL/UL traffic impact SINR more without CSMA due to the large number of strong interfering APs.
AP-AP and AP-STA: channel-D
STA-STA: channel B
30 STA per BSS
Hexagon layout of reuse 3

## Slide 13: Scenario 4 – Outdoor Large BSSs: Received SINR
  Scenario is a severe interfered case (CSMA reduces interference substantially).
  Using the same channel type for STA-STA causes a long tail for DL/UL=1/N (more severe interfering STAs)
AP-AP, AP-STA and STA-STA: UMi
Penetration loss 20dB (outdoor-indoor)
50 STA per BSS (50% indoor)
Hexagon layout of reuse 1

## Slide 14: Observations
All types of long-term SINR give very good insights into the system modeling and captures fundamental characteristics for calibration.
  Long-term SINR distributions with different traffic model (UL/DL time ratio) are within a relatively small difference.
  Long-term SINR distributions with or without CSMA are with some dBs shift.
We can select a type of definition solely based on complexity of calibration.
  Least ambiguity with equal STA/AP traffic and without CSMA.

## Slide 15: Summary
Use the distribution of long term SINR as the metric for system simulator calibration.
For simplicity and avoiding ambiguity, use the definition with equal STA/AP traffic and without CSMA as the metric for calibration.

## Slide 16: References
[1] 11-13-1392-00-0hew-methodology-of-calibrating-system-simulation-results
[2] 11-13-1001-05-0hew-HEW-evaluation-simulation-scenarios-document-template

## Slide 17: Appendix: Expected Received Signal Power
Received signal power at receiver RX from transmitter TX.

## Slide 18: Appendix: Scenario 1 – Residential: Received Signal Power

## Slide 19: Appendix: Scenario 1 – Residential: Interference Signal Power

## Slide 20: Appendix: Scenario 2 – Enterprise: Received Signal Power

## Slide 21: Appendix: Scenario 2 – Enterprise: Interference Signal Power

## Slide 22: Appendix: Scenario 3 – Indoor Small BSSs: Received Signal Power

## Slide 23: Appendix: Scenario 3 – Indoor Small BSSs: Received Signal over white noise

## Slide 24: Appendix: Scenario 3 – Indoor Small BSSs: Interference Signal Power

## Slide 25: Appendix: Scenario 4 – Outdoor Large BSSs: Received Signal Power

## Slide 26: Appendix: Scenario 4 – Outdoor Large BSSs: Received Signal over white noise

## Slide 27: Appendix: Scenario 4 – Outdoor Large BSSs: Interference Signal Power