## Slide 1: CID 1551: CCMP Header Compression
Date: 22 Jan. 2014
Name | Company | Address | Phone | Email
Menzo Wentink | Qualcomm | The Netherlands | +31-65-183-6231 | mwentink@qualcomm.com
Jouni Malinen | Qualcomm | Finland |  | 
Alfred Asterjadhi | Qualcomm | San Diego |  | 
Simone Merlin | Qualcomm | San Diego |  | 
Amin Jafarian | Qualcomm | San Diego |  | 
Minyoung Park | Intel Corp. |  |  | 
Tom Tetzlaff | Intel Corp. |  |  | 
Emily Qi | Intel Corp. |  |  | 
Liwen Chu | Marvell |  |  | 
Jinjing Jiang | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Hui-Ling Lou | Marvell |  |  | 
Yongho Seok | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jin Sam Kwak | LG Electronics |  |  | 
Matthew Fischer | Broadcom |  |  | 
Rojan Chitrakar | Panasonic |  |  | 
Ken Mori | Panasonic |  |  | 
Authors:

## Slide 4: CCMP Header Compression
Compression of the CCMP header consists of three steps
  The packet number (PN) is transmitted only partly
  The transmitted part is combined with Sequence Control (SC)
  Key ID and Ext IV are omitted
CCMP header compression is proposed in combination with the 802.11ah short frame format
PN0
PN1
Rsvd
Key ID
- Ext IV
- Key ID
PN2
PN3
PN4
PN5
Current CCMP header
802.11ah short frame MAC header (A3, A4 are optional)

## Slide 5: 1. Transmit only part of the Packet Number
The PN is split into a Base PN (BPN) and a Transmitted PN (TPN)
  Transmitted PN = PN0|PN1 - transmitted
  Base PN = PN2|PN3|PN4|PN5 - stored
  The PN can be reconstructed as BPN|TPN
  The TPN rolls over every 2^16 packets
    the TPN size coincides with sequence control size, but exact size TBD
    the TPN size should be large enough to avoid frequent BPN sync events
PN0
PN1
PN2
PN3
PN4
PN5
Transmitted PN (TPN) - transmitted with each packet
Base PN (BPN) - stored

## Slide 6: 2. Combine Packet PN with Sequence Control
Combining the Transmitted PN (TPN) with Sequence Control causes that the Packet Number becomes unique per TID
  The TID is included in the Nonce, so the Nonce is still unique
    Technically the TID does not even have to be included in the Nonce, because there is a replay counter per TID
  The Packet Number now has to be fixed when the Sequence Number is determined
    This is not considered to be a problem
  The Fragment Number (FN) effectively reduces the PN space with 4 bits
    TPN range effectively becomes 2^12 when no fragmentation is used
PN0
PN1
FN
(4b)
SN
(12b)
=
Transmitted PN
Sequence Control

## Slide 7: 3. Omit Key ID and Ext IV
Ext IV is always 0 for CCMP, so it can be omitted
The Key ID is typically fixed for unicast traffic, but it can change for group traffic
  when the GTK is rekeyed and it is not possible to delay certain group traffic during this process, normal frames (with a Key ID) can be used to transmit such group frames