## Slide 1: PHY Abstraction
Date: 2014-03-17
Authors:

## Slide 2: Abstract
A lot of submissions ([1], [2], [3], [4]) have been presented in IEEE on PHY abstraction for 802.11ax
In these slides we convey our thoughts on that topic
  Review of general concepts and proposals so far
    PHY abstraction
    Effective SINR modeling
    Current proposals and some issues
  Alternative approach of short term effective SINR curves
    How to generate the curves

## Slide 3: Recall: PHY abstraction
The goal of PHY abstraction is to accurately predict link level performance in system simulations
The PHY abstraction must be designed such that PER1 = PER2
  Can be achieved through picking reasonable “Effective SINR computation” block and a matching reference curve
    Solution is not unique
Channel Model
Transmitted packets,
MCS, and SNR
PER1
Full receiver with demod and decoder
Link level simulation
Channel Model
Linear Equalizer
Eff. SINR to PER mapping, using a reference curve
PER2
PHY abstraction
Effective SINR computation

## Slide 4: General thoughts
As long as the reference curve generation and effective SINR computation are a good match, accurate modeling is guaranteed
Good to specify a PHY abstraction method for 11ax
  Helps calibrate initial system simulation results across companies
    Natural sanity check before extensive system simulations
The PHY abstraction method should be accurate without being complex
In the next few slides we look at various methods

## Slide 5: Effective SINR modeling
In general, effective SINR (SINReff ) can be calculated as follows
  where SINRi,n is the post processing SINR at the n-th subcarrier and i-th stream, N is the number of symbols for a coded block or the number of data subcarriers used in an OFDM system, Nss is the number of spatial streams and Φ is Effective SINR Mapping (ESM) function
Two alternatives
  Approach 1: Choose a parameterized ESM function and use AWGN PER curves
    Needs ‘MCS and possibly channel model dependent’ parameterization of the effective SINR computation function
    Submissions [1] , [2], [3] and [4] have proposed this
  Approach 2: Choose a simple capacity based ESM function and then use effective-SINR vs PER curves
    Need to agree on these curves
    Will show how such curves can be generated and that these curves are different from AWGN

## Slide 6: Proposals so far in HEW use Approach 1
The approaches of MMIB and MIESM(RBIR) proposed in [1], [2], [3] and [4] are an attempt to allow the use of an AWGN curve as the reference curve
  Needs MCS dependent parameterization of the effective SINR computation function
    Not clear if the parameters are valid for all channel models
  In some cases, inverses of these functions do not have a closed form
Main disadvantage of above approaches is an MCS dependent SINR
  Difficulty in comparing SINR CDFs for calibration
  Difficulty in doing even ideal rate selection
    Need to calculate separate SINRs for all MCSs before mapping each one of them to a rate
  Counter intuitive to make SINR a function of the MCS (and the channel model)

## Slide 7: Alternative Approach 2: Capacity based ESM and short term curves
Step 1: Use a simple capacity based function for the effective SINR mapping
where , i.e. the Shannon capacity formula, and is the post equalization
SINR of the i-th stream at n-th tone
Step 2: Look up a short-term effective SINR vs PER curve (details on next slides)
Pros
  Very simple and MCS independent effective SINR calculation function
    Leads to simpler rate selection and SINR CDF comparison
  Inverse of ESM function has a closed form
Need to agree on reference curves as AWGN curves do not work
  Short term effective SINR vs PER curves need to be used
  AWGN curves cannot be used  Due to the slope difference, effective SINR PER curve is not a simple shifted version of AWGN curve

## Slide 8: Definition: Short term effective SNR and long term SNR in link simulations
In the subsequent slides, we use the following terms
  Long term SNR : Ensemble average SNR of all the channel realizations of the channel
    The average SNR if you observed the channel ‘long term’
    Note that every realization can have a very different ‘instantaneous’ SNR due to fading
  Short term effective SNR : Instantaneous effective SNR of each channel realization
    Separate for each realization
    Calculated using ESM
      Indicative of the information carrying ability of that particular channel realization

## Slide 9: Traditional WiFi PER vs SNR curves : Long term SNR
In prior standards we have always used the ‘long term’ SNR on the x-axis of PER vs SNR curves
  Diagram above shows the method used to collect statistics
  Good for a link simulation or a static system
    E.g. It tells us, if we keep sending packets of one MCS for a long time at a certain average SNR in a particular channel model, how many packets are expected to go through?
  Cannot capture the dynamic behavior of a time-varying interference based system
    In those systems, not possible to go through all channel realizations for one interference condition or for one drop
In HEW, we will run highly dynamic system simulations
  Need to capture the receiver performance for a particular instantaneous SINR
Transmitted packet with a certain
MCS
Time
Channel (scaled by a
appropriately to achieve
the average ‘long term’ SNR).
Note: Same scaling for all realizations
Demod
and decode
Pass
Fail
or
+
Noise (fixed variance)
a
Channel gain
Average long term SNR
PER

## Slide 10: PER vs ‘Short term effective SNR’ curve
Tells the PER (for each MCS) for a certain instantaneous effective SNR in a specific channel model
  The curve we would get if we recorded effective SNR, and pass/fail, for every packet in a link-simulation
  Exactly the information we need for predicting the short-term performance in system simulations
  Different curve for each channel model
Possible method for curve generation
  Scale each channel realization to the achieve the effective SNR of interest and record statistics for that SNR

## Slide 11: Generating PER vs short term effective SNR curves
Record the effective SNR for each channel realization in the link simulation, scale the channel appropriately to achieve the desired short term effective SNR and collect statistics
  The curve is different than an AWGN curve and also different from a shifted AWGN curve
Frequency
One channel realization
Calculate the effective SINR for this realization assuming the fixed noise variance
Find the appropriate
scaling b needed to get to the
right effective SNR
Transmitted packet with a certain
MCS
Frequency
Channel scaled by b
to achieve
the ‘short term’ effective SNR for
which we are collecting statistics
Note: Different scaling for each realization
Demod
and decode
Pass
Fail
or
+
Noise (fixed variance)
b
Channel gain
Short term effective SNR
PER

## Slide 12: PER vs ‘short term effective SNR’ curve has a different slope when compared to AWGN
Generated PER vs effective SNR results for D-NLOS, convolutional coding
  Delta (distance between effective SINR and AWGN curves) is PER dependent !
  Shifted AWGN curve cannot be used as the effective SNR curve !
MCS | BCC Code Rate | Delta at 10% PER | Delta at 1% PER
0 | 1/2 | 1.4 | 2.3
1 | 1/2 | 1.4 | 2.2
2 | 3/4 | 4.2 | 7
3 | 1/2 | 1.5 | 2.5
4 | 3/4 | 3.7 | 6.4
5 | 2/3 | 2.4 | 3.8
6 | 3/4 | 3.5 | 6.4
7 | 5/6 | 4.5 | 7.6
Up-to 3dB difference for higher code rates !!

## Slide 13: Summary
Effective SINR calculation for PHY abstraction can be done in various ways as long as a matching reference curve is used
Approaches proposed so far have the following complexities
  SINR is MCS dependent
    Difficulty in comparing SINR CDFs for calibration
    Difficulty in doing even ideal rate selection
  Multiple MCS dependent (and possibly channel model dependent as well) parameters
  A complex “effective SINR mapping function” whose inverse does not have a closed form
We offered an easy alternative to overcome the issues with the proposed approaches
  Need to generate PER vs short term effective SINR reference curves as AWGN curves do not work
  Need a separate curve for each channel model

## Slide 14: References
[1] 11-13-1059-00-0hew-phy-abstraction-for-hew-evaluation-methodology.pptx
[2] 11-13-1131-00-0hew-phyabstraction-for-hew-system-level-simulation.pptx
[3] 11-14-0117-00-0hew-phy-abstraction-for-hew-system-level-simulation.pptx
[4] 11-14-0043-02-0hew-phy-abstraction-in-system-level-simulation-for-hew-study.pptx

## Slide 15: Appendix
Existing proposals

## Slide 16: Mutual Information based approach (MMIB in [1])
Effective SINR mapping (ESM) function for each modulation as follows (details in [1])
Pros
  Results in [1] show that using the above parameters, we can get match (with in 1 dB) with the AWGN curve for UMi channel model (both LOS and NLOS)
    Note: Do not see results for D-NLOS
  Only need to use AWGN curves Agreeing on AWGN curves is an easier job
Cons
  Inverting the ESM function above is not that straight forward
  Results for D-NLOS channel might indicate the need for channel model dependent parameters too
Modulation | Numerical Approximation
BPSK | K=1, a = [1], c = [2√2]
QPSK | K=1, a = [1], c = [2]
16-QAM | K=3, a = [0.5 0.25 0.25], c = [0.8 2.17 0.965]
64-QAM | K=3, a = [1/3 1/3 1/3], c = [1.47 0.529 0.366]

## Slide 17: Mutual Information ESM (MIESM) in [2]
MIESM
  Also called RBIR (Received Bit mutual Information Rate)
  It is a nonlinear mapping from post SNR to symbol-level mutual information
Pros
  Results in [2] show that using the above parameters, we can get match with AWGN results
    Note: Do not see results for D-NLOS or UMi channels
  Only need to use AWGN curves Agreeing on AWGN curves is an easier job
Cons
  Inverting the ESM function above is not that straight forward
  Results for different channel models might indicate the need for channel model dependent parameters too