## Slide 1: Cross-WG cooperation on OmniRAN P802.1CF E.g.: Network Discovery and Selection
Date: 2014-03-17
Authors:

## Slide 2: Abstract
The presentation provides an introduction into the structure and scope of the P802.1CF specification and outlines the cooperation with the IEEE 802 WGs based on the example of the Network Discovery and Selection section.

## Slide 3: OmniRAN P802.1CF provides a kind of ‘Stage 2’ Specification for IEEE 802
The ITU-T defined in its Rec. I.130 a sequential 3 stage process, which is nowadays commonly used in most telecommunication network standardization activities.
A ‘Stage 2’ specification provides a mapping of the existing IEEE 802 protocols to a functional network model, which facilitates easier evaluation and better understanding of end-to-end behavior.
‘External’ requirements from the service/deployment perspective
Develop a logical/functional model for evaluation of those requirements
Available IEEE 802 specifications of protocols and attributes.
?

## Slide 4: Scope of OmniRAN P802.1CF mapped to the IEEE 802 Reference Model
Scope of IEEE 802
Access Network
Medium
Medium
Medium
P802.1CF will define an abstraction of an access network based on IEEE 802 technologies
  The access network provides the link between a station (IP host) and the first hop router
The abstraction leads to very few generic interfaces for all kind of implementations
  R1 represents the PHY and MAC layer functions between terminal and base station, which are completely covered by the IEEE 802 specifications
  R2 represents a control interface between terminal and central control entity, e.g. for authentication
  R3 represents a control interface between the access network and a central control entity and the data path interface towards the first hop router, which is defined by the IEEE 802 Data Link SAP.
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control I/f
Higher Layers Control I/f
Higher Layers
R1
STA
CORE

## Slide 5: OmniRAN Access Scenario
CORE
Internet
R1
R3
STA
R2
CORE
Internet
R3
R5
R3
AN
ANI
ANI
ANI
AN
ANI
ANI
ANI
AN
ANI
ANI
ANI
STA Station
AN Access Network
ANI Access Network Interface
CORE COntrol and Router Entitiy
CORE
R5
R3

## Slide 6: Example ToC of the P802.1CF specification
Network Reference Model
Functional Description
Introduction and Scope
Abbreviations, Acronyms, Definitions, and Conventions
References
Network Reference Model
  Overview
  Reference Points
  Access Network Control Architecture
    Multiple deployment scenarios
Functional Design and Decomposition
  Network Discovery and Selection
  Association
  Authentication and Authorization
  Datapath establishment
  QoS and policy control
  Datapath relocation
  Datapath teardown
  Disassociation
  Accounting
Annex:
  Tenets (Informative)

## Slide 7: IEEE 802 Access Network Functional Diagram
L2 Configuration
AAA Policy
DHCP
Application
ANQP
Access Technology
Control I/f
Access Network
Network Selection
Accounting
Disassociation
Host Configuration
Application
Policy Control
Application
Host Config Release
Accounting
Authentication
Authorization
Association
Discovery
Link Establishment
Link Relocation
Link Teardown

## Slide 8: Example Chapter Structure
Functional Design and Decomposition
  Network Discovery and Selection
    Generic functional requirements and information flows
    Ethernet functional design <- 802.3
    WPAN functional design <- 802.15
    WLAN functional design <- 802.11
    WMAN functional design <- 802.16
    WRAN functional design <- 802.22
  Authentication
  Link establishment
  QoS and policy control
  Link relocation
  Link teardown
  Accounting

## Slide 9: NDS Functional Requirements
IEEE 802 network discovery and selection should support more complex scenarios:
  Multiple access technologies
  Multiple different access networks
  Multiple subscriptions
  Specific service requirements
  No a-priori knowledge about offered services
CORE
A
CORE
B
CORE
C
Access Network
>2<
Access Network
>3<
Access Network
>1<

## Slide 10: NDS Roles and Identifiers
User
  One or more Subscriptions
    Subscription Identifier {NAI} + Subscription Name {String}
Terminal
  Station
    STA {EUI-48}
Access Network
  One or more Access Network Interfaces
    ANI {EUI-48}
  Access Network
    AN Identifier {EUI-48} + AN Name {String}
  Supported Subscription Services
  Supported User Services
  Access Network Capabilities
    Record of capabilities {t.b.d. (ANQP???}
CORE
  Subscription Service – ‘Termination point of AAA’
    SSP Identifier {FQDN} + SSP Name {String}
  User Service – ‘Termination point of IEEE 802 user plane’
    USP Identifier {???} + USP Name {String}
FFS: Is model sufficient for complex roaming scenarios? Split of CORE into SSP and USP (control- & user plane functions)?

## Slide 11: Network Discovery and Selection Functions
A process which allows a station to retrieve the list of all access network interfaces in reach by
  Passive scanning
  Active scanning
  Data base query
Retrieving supplementory information for each of the access network interfaces to learn about
  Identity of the access network
  Supported Subscriptions
  Supported Services
Some algorithm in the station, which processes all the retrieved information, for determination of the ‘best’ access network interface to connect to.

## Slide 12: NDS Technology Specific Design
 |  | 802.3 | 802.11 | 802.15 | 802.16 | 802.22
Identifiers | STA | EUI-48 | EUI-48 | EUI-64 | EUI-48 | EUI-48
 | ANI | EUI-48 | EUI-48 | EUI-64 | EUI-48 | EUI-48
 | AN-id | ??? | EUI-48 | ??? | EUI-48 | EUI-48
 | AN-name | 256 Char | 30 Char | ??? |  | 
Subscriptions |  | NAI | NAI/PSK | ???/PSK | NAI | NAI
Multiple COREs |  | Info | ANQP | - | ? | -
Discovery process |  | manual | passive, active | passive, active | passive | passive
A specific section for each of the IEEE 802 access technologies should explain, how the generic requirements are supported and realized.
  It would be great, if references into the specifications would be provided.
OmniRAN would like to engage subject matter experts of the 802 WGs for creating the contributions on the particular access technologies.
  Necessary effort should be managable once a kind of template is established.
A thorough review should be performed by the WGs to ensure that the access technology specific content of P802.1CF is correct.

## Slide 13: Conclusion
The P802.1CF specification provides a kind of functional framework across all IEEE 802 access technologies.
The creation of the OmniRAN P802.1CF specification requires close cooperation with most of the IEEE 802 WGs.
The Network Discovery and Selection section may be a good candidate to establish and evaluate the procedures for cooperation.
Subject matter experts of the individual WGs should create technology specific input for P802.1CF
  A kind of template for each kind of contribution may reduce the necessary effort.
Would 802.11 ARC support the presented approach?