## Slide 1: What Is P2P Traffic in HEW Simulation Scenarios?
Date: 2014-03-20
Authors:

## Slide 2: Abstract
11-13-1001r8 HEW SG Simulation Scenarios document includes P2P traffic in every simulation scenario.
P2P Traffic is not defined in 802.11. This submission clarifies P2P Traffic and proposes additions to 13-1001 HEW SG Simulation Scenarios document.

## Slide 3: P2P Traffic Description in HEW Simulation Scenarios
The 14/1001 HEW SG Simulation Scenarios document shows that P2P traffic is transmitted between two client devices
14/1001 HEW SG Simulation Scenarios document does not yet describe details:
  Detailed P2P traffic model
  Network architecture for P2P traffic transmission
  Details of the traffic types handling

## Slide 4: BSS Type for P2P Traffic
P2P traffic may be transmitted at least in the following topologies:
  Mesh BSS (MBSS)
  Independent BSS (IBSS)
  Additional Infrastructure BSS
  Tunneled direct-link (TDLS)
The topology specific operating principles may not be critical in HEW scenarios
  Typically topology specific operation rules are visible in stand-by mode, HEW scenarios have high traffic load and high density of APs and STAs
Proposal: Do not consider topology specific operations for P2P traffic

## Slide 5: May a STA Transmit both Infrastructure and P2P Traffic?
Does a STA transmit P2P and UL traffic in a scenario?
  Should a STA have separate EDCA channel access for P2P and UL traffic? Or can the STA use the same EDCA to transmit traffic to different BSSs?
How the STA prioritizes and schedules traffic between multiple networks?
  Does UL and P2P traffic have the same priority?
  Proposal: The scheduling and channel access / EDCA use are not described in HEW Simulation Scenario document

## Slide 6: Is P2P Traffic Needed in All Simulation Scenarios?
Currently all HEW simulation scenarios have P2P traffic
  P2P traffic makes simulations even more complicated
  P2P complicates the understanding of system performance
Should there be at least one scenario, for instance scenario 1, that does not have P2P traffic?
  Proposal: Make P2P traffic optional