## Slide 1: PHY abstraction method comparison
Date: 2014-05-12
Authors:
Name | Affiliations | Address | Phone | Email
Tianyu Wu | MediaTek | San Jose, CA, USA |  | tianyu.wu@mediatek.com
Jianhan Liu | MediaTek | San Jose, CA, USA |  | jianhan.liu@mediatek.com
Thomas Pare | MediaTek | San Jose, CA, USA |  | thomas.pare@mediatek.com

## Slide 2: Background
General idea of PHY abstraction: Effective SINR Mapping (ESM)
A number of PHY calibration methods has been proposed
  EESM is introduced in [2, 3]
  RBIR/ RBIR-BICM is recommended in [1, 3, 6]
  MMIB is proposed in [5]
  Capacity based mapping is proposed in [4]
In this contribution, we compare different PHY calibration methods.

## Slide 3: List of PHY abstraction methods
PHY Abstract | SINR Mapping | 
EESM | Exponential mapping | 
CM based RBIR | Mutual information assuming CM | 
BICM based RBIR | Mutual information assuming BICM | 
MMIB | Mutual information per bit | 
CESM | Capacity based mapping | 

## Slide 4: Comparison of the Φ function
The Φ functions for RBIR-CM, RBIR-BICM and MMIB are similar. (Φ functions are normalized by the information bits carried by the modulation)
The MMIB parameters for 256 QAM is from [5].

## Slide 5: PHY abstraction selection criteria
Criteria for PHY abstraction method selection
  Channel type irrelevant
    Good effective SINR mapping function shall be channel irrelevant. The PER mapping shall have acceptable accuracy for all channel types.
    There are many channel types:
      Channel model A-F, Uma, Umi etc
      Beamformed MIMO channels
      Possibly OFDMA sub channels
    It’s impossible to optimize the SINR mapping function for each channel type.
  Instantaneous mapping accuracy
    The set of {channel realization, average SINR} combinations that map to an effective SINR shall have small PER difference from the predicted PER.

## Slide 6: PHY abstractions comparison – Channel irrelevance
In this simulation, we show the results for RBIR, RBIR-BICM, MMIB and CESM under different channel models and compare to the PER curve for AWGN channel.
Simulation settings:
  Channel models: B-NLOS, D-NLOS, E-LOS
  80MHz@5GHz, 1 by 1, 1024 Bytes packet, BCC
  Independent Channel realization for each effective snr.
    For each effective snr, simulate 2000 packets pass independent channel realizations.

## Slide 7: RBIR-CM with channel B,D,E

## Slide 8: RBIR-BICM with channel B,D,E

## Slide 9: MMIB with channel B,D,E

## Slide 10: RBIR,RBIR-BICM,MMIB with channel D

## Slide 11: CESM with channel B,D,E

## Slide 12: Observations
Results for RBIR , RBIR-BICM and MMIB are very similar and these 3 results are more channel irrelevant comparing to CESM
There is still a distance from AWGN channel
  All the results are shifted left side about 0.4 dB
  A channel irrelevant fitting parameter α might be helpful to further improve the accuracy.
  For MMIB with 256QAM, the result is less accurate and the parameters may need further optimization if MMIB is selected
For CESM, it seems harder to obtain a smooth curve. May need more simulation points compare to other methods.
RBIR-CM and RBIR-BICM seems more mature and can provide good accuracy for average PER prediction.

## Slide 13: Example of channel irrelevant curve fitting
For RBIR-CM, shift the curves by 0.4 dB (set α=1.0965 in the effective SNR mapping function) can obtain a more accurate result.

## Slide 14: PHY abstractions comparison – Instantaneous accuracy
In this simulation, we compare the results for RBIR, RBIR-BICM, MMIB and CESM under channel model D.
  For a given effective SINR, simulate the PER distribution of the channels that map to a fixed effective SINR.
  Compare and find the PHY abstraction method that has highest instantaneous accuracy.
Simulation settings:
  Channel model: D-NLOS
  MCS 4, 80MHz@5GHz, 1 by 1, 1024 Bytes packet, BCC

## Slide 17: Observations
The results shows that RBIR-CM, RBIR-BICM and MMIB provide similar accuracy on instantaneous PER prediction.
  MMIB seems slightly better and CESM is a little bit worse than other methods.
The PHY accuracy and SLS simulation complexity is a tradeoff
How accurate for PHY abstraction do we need for SLS?

## Slide 18: Other observations: Effect of BW
Simulation settings:
  Ch D, MCS 0,2,4,6,8
From the results we find that the effective SNR mapping is irrelevant to bandwidth.

## Slide 19: Other observations: Effect of Packet Length (1)

## Slide 20: Effect of Packet Length (2)
The PER for an arbitrary packet length PL can be given by:
where PL0 is the reference packet length and PERPL0 is the PER for the reference packet length PL0.
One problem for this method is that when PL/PL0 is too small to too large, the inaccuracy on the reference curve will be amplified.
Take 1024 Bytes as reference packet length and generate the PER curve for 256 and 4096 bytes as shown in next slide.

## Slide 21: Effect of Packet Length (3)
The error will be amplified when L/L0 is too big or too small.
  We may need a set of reference curves for different size of packets.

## Slide 22: Conclusion
RBIR can provide quite accurate prediction for average performance
An channel irrelevant curve fitting method can be used to further improve the accuracy
Instantaneous PER is hard to be precisely predicted.
Other observations:
  PHY abstraction methods are irrelevant to BW.
  PHY abstraction for different packet length might be calculated from a set of tables for several fixed packet length.
Prediction accuracy and simulation complexity is a tradeoff.
  Shall we consider some simple PHY abstraction method instead?

## Slide 23: References
[1] 11-13-1131-00-0hew-phyabstraction-for-hew-system-level-simulation
[2] 11-14-0043-02-0hew-phy-abstraction-in-system-level-simulation-for-hew-study
[3] 11-14-0117-00-0hew-phy-abstraction-for-hew-system-level-simulation
[4] 11-14-0330-03-0hew-hew-phy-abstraction
[5] 11-14-0353-00-0hew-suggestion-on-phy-abstraction-for-evaluation-methodology
[6] 11-14-0527-00-00ax-phy-abstraction-for-tgax-system-level-simulations