## Slide 1: Next Generation 802.11ad
Authors:
Name | Affiliation | Address | Phone | Email
Alecsander Eitan | Qualcomm |  |  | eitana@qti.qualcomm.com
Gal Basson | Wilocity |  |  | gal.basson@wilocity.com
Lei Wang | Marvell |  |  | leileiw@marvell.com
Dmitry Cherniavsky | Silicon Image |  |  | Dmitry.Cherniavsky@siliconimage.com
James Wang | Mediatek |  |  | james.wang@mediatek.com
Saishankar Nandagopalan | Tensorcom |  |  | nsai@tensorcom.com
Sven Mesecke | Nitero |  |  | smesecke@nitero.com

## Slide 2: Motivation and purpose
This presentation is a continuation to the following presentations 13/1408r1 and 14/136r3, which suggested MIMO and channel bonding as methods to increase throughput in 60 GHz
In this presentation, we show another possible mechanism to increase throughput, namely, the use of 64 QAM over SC modulation

## Slide 3: 802.11ad Attributes
~9GHz of unlicensed BW
Small antenna footprint
  Drives Antenna array implementations
  Beam forming  Directivity
Low operating SNR
  Drive relaxed system requirements
Capacity at 60GHz
  Spatial separation

## Slide 4: 802.11ad Antenna size
Wavelength is 5mm, typical array antenna spacing is 2.5mmmm
  Small foot print antenna
7x9 mm 24 3D antenna array
16 planar antenna array
17x8 mm 32 3D antenna array

## Slide 5: Low Operating SNR
802.11ad high rate is a result of using high BW (1.76 GHz)
The operating SNR for 4.6Gbps is lower than 14 dB

## Slide 6: Methods for increasing the TPT
Channel bonding feasibility
  We have suggested 2 additional BW
    Double channel-5.28GHz
    Quadruple channel-10.56GHz
    Triple channel should also be considered
    We have shown technology feasibility of such an analog FE today.
      Marinating low power
MIMO feasibility
  “Traditional MIMO”
  “Spatial orthogonal MIMO”
    For receiver simplification
  Shown channel measurement
    11-13 408r2

## Slide 7: 64QAM Motivation
Rate increase of 50% with the existing BW
4.62Gbps  6.93Gbps
Lower system power consumption
Increased efficiency
Is it feasible over SC

## Slide 8: 64QAM feasibility on SC
Can 64QAM be supported on SC
On the transmit side, SC has 2-3dB less P2A (Compared to OFDM), hence 2-3dB less backoff
On the receive side Channel may increase SNR requirements
  Many 60GHz are using array implementations
  Channel is very close to AWGN in the LOS case [408r2]
  Phase Noise (PN) immunity should be investigated
Gal/Alecs Wilocity/Qualcomm

## Slide 9: Simulation results for SC 64QAM
Fixed point implementation
  FDE equalization
AWGN
PN included both on TX and RX
No TX EVM
Modulation | Code Rate | Rx C/N
64QAM | 1/2 | 17.3dB
 | 5/8 | 19.1dB
 | 3/4 | 22.0dB
Gal/Alecs Wilocity/Qualcomm

## Slide 10: Coverage simulation
Based on Room coverage simulation
  Ray tracing
Varying room dimensions/networking nodes
Measured Radiation Pattern
BF impairments
Statistics on the room coverage

## Slide 11: Coverage - desktop scanning
Back of platform – 16QAM limited | Screen side– 16QAM limited
Back of platform – 64QAM limited | Screen side – 64QAM limited

## Slide 12: Coverage - Sit & Talk
Back of platform – 16QAM limited | Screen side– 16QAM limited
Back of platform – 64QAM limited | Screen side– 64QAM limited

## Slide 13: Coverage - room walk
Back of platform – 16QAM limited | Screen side– 16QAM limited
Back of platform – 64QAM limited | Screen side– 64QAM limited

## Slide 14: SC 64QAM: Additional Improvement
It is clear that the main multiplicative noise in the 60G link is the Phase Noise
Link budget can be further increased by using better suited constellation
Developed by DVB-S2X
8+16+20+20APSK

## Slide 15: Summary
Increasing demand for capacity and new applications are driving the desire to enhance 11ad to support these needs
Technical feasibility to enhance 11ad with MIMO and channel bonding has been demonstrated
  13/1408r1, 14/606r0
Suggest that 802.11 start a new SG on next generation 11ad

## Slide 16: Backup