## Slide 1: Envisioning 11ax PHY Structure - Part II
Date: 2014-07-14
Authors:

## Slide 2: Introduction
802.11ax supports the following scopes in PAR[1]
  Improvement in average throughput per station
  Robustness in outdoor propagation environments
To satisfy the suggested targets, increased FFT size and proper cyclic prefix (CP) length are proposed as a new 11ax frame structure in [2].
In this contribution, we analyze the impact of increased FFT size on carrier frequency offset (CFO) and the impact of CP length on outdoor robustness.

## Slide 3: Issues with PHY change in 11ax
4 times larger FFT size than that of 11ac is proposed in 11ax for both of average throughput enhancement and outdoor robustness [2][3][4]
Regarding increased FFT size, there are two issues:
  Issue 1. Carrier Frequency Offset (CFO): Since carrier spacing is reduced with larger FFT size, we need to check how sensitive it is to CFO.
  Issue 2. CP length: Since symbol duration is increased with larger FFT size, we need to analyze which CP length is necessary for outdoor robustness.
This contribution provides answers on the above two issues.

## Slide 4: Issue 1. Carrier Frequency Offset: Performance with increased FFT (1/3)
4 times larger FFT size does not show performance degradation compared to 11ac
But, 8 times larger FFT size show significant loss due to higher sensitivity on CFO.

## Slide 5: Issue 1. Carrier Frequency Offset: Performance with increased FFT (2/3)
With 4 times larger FFT size, CFO is compensated well irrespective of MCS both in indoor and outdoor channel.

## Slide 6: Issue 1. Carrier Frequency Offset: Performance with increased FFT (3/3)
With 4 times larger FFT size (78.125kHz subcarrier spacing), CFO is compensated well up to about 500kHz of CFO

## Slide 7: Issue 2. CP length: Performance with increased FFT (1/2)
Performance gain of 1/4 CP compared to 1/16 CP
  It is small in low SNR region but increases in higher SNR region
  It increases significantly with MCS

## Slide 8: Conclusion
When 4 times larger FFT is adopted in 11ax,
We have confirmed that CFO is not a critical issue.
  But, CFO can be critical when 8 times larger FFT is adopted
We have confirmed that conventional CP length (0.8us) does not secure the robustness in outdoor.
  Severe performance degradation for higher MCS

## Slide 9: Appendix

## Slide 10: Simulation Assumption for CFO
 | Conventional | 4 times FFT
FFT size | 64 | 256
Used data subcarriers | 52 | 242
Symbol length with CP | 4us | 13.6 us
CP length | 0.8us | 0.8us
Center frequency | 2.4GHz | 
Bandwidth | 20MHz | 
Channel model | Tgac B, Umi | 
Channel Estimation | Least Square | 
Data size | 100bit | 
MCS | 0, 8 | 
Carrier frequency offset | ±20ppm (uniformly generated within ± 48KHz in 2.4Ghz) | 

## Slide 11: Simulation Assumption for CP length
 | conventional | CP1 of 4 times FFT | CP2 of 4 times FFT
FFT size | 64 | 256 | 256
Used data subcarriers | 52 | 242 | 242
Symbol length with CP | 4.0us | 13.6us | 16.0us
CP length | 0.8us | 0.8us | 3.2us
Center frequency | 2.4GHz |  | 
Bandwidth | 20MHz |  | 
Channel model | Tgac B and D, UMi, UMa |  | 
Channel Estimation | Least Square |  | 
Data bit | 300bit or 2 symbol |  | 
MCS | 0, 4, 7 |  | 

## Slide 12: References
[1] 11-14/0165-01-0hew-hew-sg-proposed-par
[2] 11-14-xxxx-00-0ax-envisioning-11ax-frame-structure-part-I
[3] 11-13-0536-00-0hew-hew-sg-phy-considerations-for-outdoor-environment
[4] 11-13-0843-00-0hew-further-evaluation-on-outdoor-wi-fi