## Slide 1: DSC and Legacy Coexistence
Date: 14/07/2014
Authors:

## Slide 2: Abstract
Dynamic Sensitivity Control (DSC) techniques as discussed to date in TGax have shown promise to improve TGax STA performance.
However, TGax STA improvements using DSC should not adversely affect performance of legacy STAs.
Effects of DSC in mixed networks therefore needs careful study and proper mitigation methods should be considered.

## Slide 3: Introduction
DSPG’s presentation (11-14-0779-00-00ax-dsc-practical-usage) says,
  Legacy STA in the same network as a DSC STA is completely unaffected by the DSC STAs.
  The legacy STA may be held off from transmitting by STA in OBSS, but will compete equally with DSC STAs in same BSS
    As other DSC STAs will ignore OBSS STAs their traffic is often occurring during a time when the legacy STA cannot TX, and hence overall contention is lessened.
This effect cannot be ignored in the evaluation of 11ax.

## Slide 4: DSPG’s Simulation Results
DSC Network with
2 DSC STAs
2 Legacy STAs
OBSS Network
4 Legacy STAs
DSC 100Mbps
Legacy ~22Mbps
Legacy ~22Mbps
Legacy STAs are not affected
BUT look at the DSC STAs!
Quoted from:
11-14-0779-00-00ax-dsc-practical-usage

## Slide 5: Simulation Conditions
Each STA sends uplink UDP traffic (Full-buffer condition).
See backup slide for more detail.
50m
3m
3m
AP1
AP2
Case 1 (2 STAs per BSS)
Case 2 (24 STAs per BSS)
DSC STA or Legacy STA
DSC STA or Legacy STA
Legacy STA
Legacy STA
50m
3m
3m
AP1
AP2
Each STA is close enough to their AP so that each link satisfies the required SNR for used MCS, even if interference from OBSS is observed.
Packets from OBSS can be detected by only Legacy STAs. (See next slide)
Packets from OBSS can be detected by only Legacy STAs.

## Slide 6: Simulation Conditions (Relation between preamble detection threshold and distance from OBSS)
Receive level when Tx power is +15dBm
DSC STA cannot detect
packets from OBSS
Legacy STA can detect
packets from OBSS
Preamble detection
threshold for DSC STA
set to -62 dBm
Preamble detection
threshold for Legacy STA
set to -82 dBm
(Note)
Propagation loss model of TGn is used.
Fluctuation by fading is
not illustrated.

## Slide 7: Simulation Results (Case 1: 4 STAs)
50m
3m
3m
AP1
AP2
If the number of STAs is few,
there is less difference of Legacy STAs’ performance.
But...
STA4
STA1
STA2
STA3
DSC
Legacy
STA1 (DSC STA or Legacy STA)
STA2 (DSC STA or Legacy STA)
STA3 (Legacy STA)
STA4 (Legacy STA)

## Slide 8: Simulation Results (Case 2: 48 STAs)
As the number of STAs increases,
there is noticeable performance degradation of Legacy STAs.
DSC
Legacy
It is not negligible, especially in a dense scenario.
50m
3m
3m
AP1
AP2
STA1~12 (DSC STA or Legacy STA)
STA13~24 (DSC STA or Legacy STA)
STA25~36 (Legacy STA)
STA37~48 (Legacy STA)

## Slide 9: Simulation Results (Throughput Summary)
Throughput [Mbps] | All STAs are Legacy | STA1 and 2 use DSC
System Total | 25.32 | 35.60
DSC Total (per STA) | - | 25.25 (12.62)
Legacy Total (per STA) | 25.32 (6.33) | 10.35 (5.18)
Throughput [Mbps] | All STAs are Legacy | Half of STAs use DSC
System Total | 26.91 | 38.36
DSC Total (per STA) | - | 32.86 (1.37)
Legacy Total (per STA) | 26.91 (0.56) | 5.50 (0.23)
Case 1 (2 STAs per BSS)
Case 2 (24 STAs per BSS)
40% Up
42% Up
18% Down
59% Down
Throughput degradation for Legacy STA
depends on the number of STAs.

## Slide 10: Summary
The impact of using DSC in TGax on other Legacy STA exists and is not negligible.
As the number of STAs increases (e.g., dense scenarios), the degradation on performance of Legacy STAs also increases.
Suggest to evaluate impact on fairness with legacy STAs when conducting DSC simulations.

## Slide 11: Backup

## Slide 12: Simulation Conditions
Node & Topology | See right figures
Traffic Model & Load | Uplink UDP 100Mbps (from all STA)
Traffic Duration [sec] | 20
Access Category | AC_BE (CWmin=15, CWmax=1023, AIFSN=3)
Tx Power [dBm] | +15dBm
MCS | MCS5 (52Mbps) Fixed
Packet Length [byte] | (MPDU, MSDU, APP)=(1530, 1500, 1472) Fixed
L2 Retry | 10
Ack Rate | MCS0 Fixed
RTS/CTS | Disabled
Aggregation | Disabled
Channel | (Propagation, Shadow, Fading)= (TGn, Disabled, Flat Rayleigh)
Preamble Detection Threshold. [dBm] | -62 (on DSC STA, AP), -82 (on Legacy STA)
Energy Detection Threshold [dBm] | -62
Channel Setting [MHz] | (Center Freq, BW)=(2412, 20)
Detection Cancel behavior on PLCP error | Not emulated
50m
3m
3m
AP1
AP2
Case 1
Case 2
50m
3m
3m
AP1
AP2
DSC STA or Legacy STA
DSC STA or Legacy STA
Legacy STA
Legacy STA

## Slide 13: Confirmation of simulation conditions
What is the behavior of each STA when PLCP header has an error ?
  Is Rx canceled or does it continue to receive?
Does AP also enable DSC ?

## Slide 14: Behavior of DSC and Rx cancel on PLCP error
Preamble
Data
STA
AP
Detect depend on preamble level
SIG
When CRC of SIG is error,
Then Rx is cancelled.
“Busy” or “Idle” depends on Energy-Detection result
Rx
Preamble
Data
STA
AP
SIG
Not detect due to
high threshold
DSC
Rx cancel on PLCP error