## Slide 1: A Protocol Framework for Dynamic CCA
Date: 2014-07-14
Authors:

## Slide 2: Abstract
This presentation outlines a protocol for dynamically varying CCA thresholds.

## Slide 3: Introduction / Motivation
Modifying CCA rules to increase spatial reuse has been discussed in HEW/11ax
  Ron Porat, Nihar Jindal (Broadcom) presented results [1, 2] showing significantly increased throughput from adopting different CCA thresholds
      “Transmissions within the BSS are deferred to at the lowest possible level in order to on one hand side provide the lowest sensitivity and on the other hand side prevent intra-BSS multiple unsynchronized transmissions (which are bound to be unsuccessful)
      Transmissions that are perceived to belong to an OBSS (different color) are deferred to based on the CCA value (in 11ah 3 values of CCA levels exist)”
    >2x improvement in mean throughput, 2x in 5% outage throughput observed
  Graham Smith (DSP Group) presented results [3, 4, 5, 6] on “Dynamic Sensitivity Control”
      DSC sets RX Sensitivity according to the strength of received signal from AP (with margin M)
      CCA Threshold ← max(RX sensitivity, CCA threshold)
Enables gains by allowing multiple Tx where only one permitted today
  But raises several new issues that aren’t present in current 802.11

## Slide 4: Scenarios—I
AP1
AP2
STA1
STA2
STA1 is transmitting
STA2 detects STA1 and wants to assess whether it can transmit transmit

## Slide 5: Scenarios—II
AP1
AP2
STA1
STA2
Problem A: STA1 may cause interference at AP2 and cause STA2’s packet to fail transmit
A

## Slide 6: Scenarios—III
Problem A provides an immediate symptom at STA2: no ack from AP2
Problem B: STA2 may cause interference at AP1
  —More serious: no immediate symptom at STA2
AP1
AP2
STA1
STA2
B

## Slide 7: Scenarios—IV
AP1
STA1
STA2
STA2’s interference with STA1—AP1 transmission is relevant at the
intended receiver, AP1
But STA2 sees the energy from STA1, which is not enough information
B

## Slide 8: Scenarios—V
AP1
AP2
STA1
STA2
Even otherwise positive scenarios will cause serious issues in the presence of yet other devices
Problem C: STAs from BSS3 (previously quiet) have data and conclude, similarly to STA2, that they may transmit
B
(BSS3)
C

## Slide 9: List of issues
Robustness & stability: the protocol should be able to recover from errors and suboptimal policy choices
Parameter choices: the protocol should be able to determine and use effective values of CCA thresholds
  The cited experimental results show different CCA thresholds are optimal for different BSS configurations, traffic patterns, etc.
Fairness: the protocol should be able to provide its improved performance without significantly penalizing any individual devices
  It may be necessary to allow different CCA thresholds for different devices
Adaptability: the protocol should be capable of adapting to changed circumstances
Legacy: the protocol should work in mixed-mode and preserve legacy device performance

## Slide 10: A basic organizing principle
Each transmitting device indicates the increase in CCA threshold it permits other devices to use for this PPDU
and
adjusts this increase dynamically

## Slide 11: Example protocol—I
S = 0
C = 0
Tx packet to AP1
Get Ack?
C = 0
S--
C++
C == 16?
C = 0
S++
N
Y
Y
N
S appears in SIG field
C is internal counter
S = CCA Threshold increase multiplier

## Slide 12: Example protocol—II
AP1
AP2
STA1
STA2
B
STA2 looks at “color” first (can only transmit if there’s a mismatch)
STA2 reads S,
sets CCA Threshold CCA Threshold + S * 10 dB

## Slide 13: Text version
STA1 starts an internal counter at 0; sets two bits in SIG field to ‘00’; and transmits packet to AP1
Upon reception of acknowledgment from AP1, STA1 increments its counter
When counter reaches limit (say 16), STA1 resets internal counter to 0, sets two bits in SIG field to ‘01’, and transmits packet to AP1
And so on for SIG bits = ‘10’, ‘11’
If no acknowledgment is received, STA1 resets counter to 0 and changes two bits in SIG field to previous level (one level lower)
Any other device receiving a packet from STA1 sets its CCA threshold for purposes of that packet at 10dB x [number signaled in SIG field] higher than level it would otherwise use
Any such other device also checks ‘BSS Color’ or equivalent to avoid transmissions to currently transmitting/receiving devices in the same BSS
  Note: AP1 does the same, except that it maintains a separate counter and SIG field state for each STA it communicates with

## Slide 14: Discussion
CCA-threshold-offsets settle on values that can be supported in current conditions
  Except for 1-packet-in-17 lost (and that level can be adjusted as we wish)
  Reverts to baseline environment if no nonzero offsets work (“first, do no harm”)
Different devices may (and probably will) have different CCA-threshold-offsets
  Addresses “fairness” problem
  No need to determine and communicate overall optimum CCA thresholds
Adaptable
  Could state information be out of date?—Sure, but so could MCS. They’ll both adapt quickly
  What if configuration changes (noisy neighbor arrives/moves away)?—Offsets adjust quickly
Verifiable
  Easy to test: need only observe transmitter behavior
Compatible with legacy devices
  Legacy = ‘00’ always: always receive current level of protection, but also can’t benefit from relaxed requirements signaled by other devices

## Slide 15: Extra considerations
Protocol could operate on an AP-control basis
  AP decides if and when STAs associated in its BSS follow this operation
  Signaled in beacon—changes dynamically
  Allows different optimizations in large managed environments
Protocol could also operate on the basis of AP control of the enabling parameters
  AP signals (one of a set range of possible) set of parameters (counter limits, etc.)
  Allows AP to make its own assessment of when retransmissions are due to interference and when to collisions/low RSSI
  AP itself may adapt to its own perceived optimal level
  No need to determine and communicate overall optimum CCA thresholds

## Slide 16: References
“Improved Spatial Reuse Feasibility – Part I”, Ron Porat, Nihar Jindal (Broadcom), doc. IEEE 802.11-14/0082r0, January 2014.
“Improved Spatial Reuse Feasibility – Part II”, Ron Porat, Nihar Jindal (Broadcom), doc. IEEE 802.11-14/0083r0, January 2014.
“DSC Channel Selection and Legacy Sharing”, Graham Smith (DSP Group), doc. IEEE 802.11-14/0294, March 2014.
“Dynamic Sensitivity Control for HEW”, Graham Smith (DSP Group), doc. IEEE 802.11-13/1290r1, April 2014.
“Dynamic Sensitivity Control Implementation”, Graham Smith (DSP Group), doc. IEEE 802.11-14/0635r1, May 2014.
“DSC Practical Usage”, Graham Smith (DSP Group), doc. IEEE 802.11-14/0779r2, July 2014.
“Measurements on CCA Thresholds in OBSS Environment”, John (Ju-Hyun) Son, Jin Sam Kwak (WILUS Institute), Young Doo Kim, Hong Seok Shin (SK Telecom), doc. IEEE 802.11-14/0628r0, May 2014.
“Residential Scenario CCA/TPC Simulation Discussion”, Frank LaSita, Pengfei Xia, Joseph Lev (Interdigital), doc. IEEE 802.11-14/0578r0, May 2014.
“DSC and Legacy Coexistence,” Yuichi Morioka (Sony), et al., doc. IEEE 802.11-14/0854r0, July 2014.
“Evaluating Dynamic CCA/Receiver Sensitivity Algorithms”, Brian Hart (Cisco), et al., doc. IEEE 802.11-14/0856r0, July 2014.