## Slide 1: Calibration of System Level Simulators
Date: 2014-07-14
Authors:

## Slide 2: Outline
Abstract
Scenario1
  Parameters
  Results
Scenario3
  Parameters
  Results
Conclusions
Reference

## Slide 3: Abstract
Simulation calibration verifies that simulators generate the same results on the same simulation scenario
  Calibration improves simulations reliability
The presentation shows the calibration results for HEW scenario 1 and scenario 3 [1] with different channel allocation

## Slide 4
Scenario:
  5 floors building with 20 rooms (10x10x3) per each floor
  One AP per each room, x and y randomly chosen, z=1.5
Same parameters as in [1], except:
  Pathlos: 11nB
  Wall loss: 12 dB
  Floor loss: 17dB + 4dB per floor
  TX Power: STA= 15dBm; AP= 20dBm;
  1x1 antenna with 0dBi for AP’s, -2dBi for STAs
  Full buffer traffic model
  Static MCS7: 64QAM 5/6
Scenario 1 and Parameters

## Slide 5
The presentation explains and shows results to following metrics:
  SINR
  Throughput
  Number of concurrent transmissions
The results are presented for the following parameters:
  Traffic: DL/UL
  Number of STAs: 200, 1000
Simulation Results

## Slide 6
SINR
These figures show the CDF of SINR per MPDU containing user data
Left and right figures show SINR performance of 2 and 10 STAs per AP respectively

## Slide 7
Left and right figures show STA throughput performance of 2 and 10 STAs per AP respectively
CDF of STA Throughput

## Slide 8
Number of Concurrent Transmissions Statistics
The number of concurrent transmissions statistics shows the number of transmitting devices at the same symbol
  This metric does not show the number of successful transmissions
The number of concurrent transmissions indicates the level of channel reuse
  The physical and virtual carrier sensing affect to the number of simultaneous transmissions
  EDCA parameters, number of competing STAs and traffic amount affect to the number of simultaneous transmissions
The number concurrent transmissions affects to the interference level

## Slide 9
Left and right figures show the number of concurrent transmissions of 2 and 10 STAs per AP respectively
Number of Concurrent Transmissions

## Slide 10
Same parameters as in [1], except:
  Pathlos: 11nD
  TX Power: STA= 15dBm; AP= 20dBm;
  1x1 antenna with 0dBi for AP’s, -2dBi for STAs
  Full buffer traffic model
  Static MCS7: 64QAM 5/6
Scenario 3 and Parameters

## Slide 11
The presentation explains and shows results to following metrics:
  SINR
  Throughput
  Number of concurrent transmissions
The results are presented for the following parameters:
  Traffic: DL/UL
  Number of STAs: 570
Simulation Results

## Slide 12
SINR

## Slide 13
CDF of STA Throughput

## Slide 14
Number of Concurrent Transmissions

## Slide 15
The presentation shows the calibration results for HEW scenario 1 and HEW scenario 3
Conclusions

## Slide 16: References
[1] 11-14-0621-04-00ax-simulation_scenarios