## Slide 1: PHY Abstraction with Time Varying Interference
Date: 2014-09-15
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com

## Slide 2: Introduction
Basic procedure of PHY abstraction has been accepted in evaluation methodology document [1] in the July meeting.
The open issue is how to handle the interference varying across the transmission duration of a packet.
  This happens due to asynchronous transmission of interfering packets in OBSS.
Here we studied this open problem and propose a block-wise PER prediction solution.

## Slide 3: Recap of PHY Abstraction Procedure in [1]

## Slide 4: Discussions
Thorough studies on the basic procedure show good PER prediction.
  PHY abstraction works well for frequency selective interference.
However, the studies focuses on under the assumption of time-constant interference  the interferers over the whole packet.
  In such a case, the effective SNR based on one SINR vector over one OFDM symbol is the same as that based on SINR vectors over the packet.
  (T0=1, T=0) = (T0=1, T=packet_len-1) in STEP2-3
This is not the case if the interferers change over the packet.
  How to select T0/T for time-selective interference?

## Slide 5: Time Varying Interference
Frame
Interference Level
Time
(unit: OFDM
symbols)
L1
LN
L2
Interference Event N
Interference Event 1
L
T1=1
T2
T3
TN

## Slide 6: Potential Solutions
Whole packet average
  T0=1, T=L-1
  May discount strong interference given a short interleaver for BCC.
Weakest link
  T0=argmin_t SINR(t), T=0
  May overestimate strong (but short) interference
Block-wise PHY abstraction
  Balance between the two method above.
  For each event n, T0=Tn, T=0  PERn, n=1…N
  Final PER prediction:

## Slide 7: Case 1: 5dB Interference Rise x2
20MHz, 1x1, D_NLOS, ideal CE, 8000 bits packet
MCS 0/2/4/7/9
Interference rises 5dB every 1/3 of packet.
Frame
Interference Level
time
5dB
L/3
L/3
5dB
L/3
SNR

## Slide 8: PER Predict: Whole Packet Avg
Clearly discounted strong interference too much and underestimate PER

## Slide 9: PER Predict: Weakest Link
Use the last interference level for PHY abstraction
Overweight strong interference and overestimate PER (but closer than whole packet average)

## Slide 10: PER Prediction: Block-Wise
Very accurately predicted PER performance for time-varying interference.

## Slide 11: PER Prediction: LDPC
Weakest link and block-wise PHY abstraction provides close and accurate PER prediction.

## Slide 12: Case 2: 10dB Rise
20MHz, 1x1, D_NLOS, ideal CE, 8000 bits packet
MCS 0/2/4/7/9
Interference rises 10dB for the last ¼ of the packet.
Frame
Interference Level
time
10dB
3L/4
L/4

## Slide 13: PER Prediction: BCC
Block-wise PHY abstraction still work well, while weakest link still overestimate PER.

## Slide 14: PER Prediction: LDPC
Again, weakest link ≈ block-wise ≈ true PER

## Slide 15: Case 3: Short 15dB Rise
20MHz, 1x1, D_NLOS, ideal CE, 8000 bits packet
MCS 0/2/4/6/9
Interference rises 15dB for the last 6 OFDM symbols
Frame
Interference Level
time
15dB
3L/4
6

## Slide 16: PER Prediction: BCC
Same conclusion even for such a short interference pulse.

## Slide 17: Discussions on Block-Wise PHY Abstraction
It provides much better PER prediction than other methods.
The additional complexity is minimal.
  Post-equalization SINR calculation is anyway required for each interference event, for all methods.
  Effective SNR mapping and PER lookup for each event is trivial.
If interferences are assumed to change significantly, block-wise can be related to weakest-link by:

## Slide 18: Conclusion
Propose to update the basic PHY abstraction to block-wise PHY abstraction.

## Slide 19: Proposed Text Change in [1]

## Slide 20: Reference
[1] 11-14-0571-03-00ax-evaluation-methodology