## Slide 1: HEW PPDU Format for Supporting MIMO-OFDMA
Date: 2014-09-14
Authors:

## Slide 2: MIMO-OFDMA in High Efficiency WLAN
Current release of Wi-Fi devices is supporting
  20/40/80 MHz channel bandwidth
  Up to 4 space time streams for SU-MIMO
Next release of Wi-Fi devices is upcoming with following additional features
  160 MHz channel bandwidth, Downlink MU-MIMO
Candidate technologies (such OFDMA) of IEEE 802.11ax should be based on IEEE 802.11n/ac advanced MIMO technology (MU-MIMO, STBC)

## Slide 3: MIMO-OFDMA in High Efficiency WLAN
OFDMA is a promising technology for enhancing the user experience by serving the heterogeneous users simultaneously
In order to serve heterogeneous users (having different link quality), the following TXVECTOR parameters should be considered as user-specific values
  MCS: indicates the modulation and coding scheme
  NUM_STS: indicates the number of space-time streams
  STBC: indicates whether STBC is used
  FEC_CODING: indicates which FEC encoding is used

## Slide 4: HEW PPDU Format for Supporting MIMO-OFDMA
Proposed HEW PPDU format
  FFT size is increased N times to efficiently support MIMO-OFDMA
  For example, when N is 4, the following FFT size may be used for each channel bandwidth
    256 FFT on 20 MHz channel, 512 FFT on 40 MHz channel, 1024 FFT on 80 MHz channel, 2048 FFT on 160 MHz channel
    Also, single 20 MHz channel (256 FFT) can be composed of several sub-channels (e.g., 4 sub-channels in the below figure)

## Slide 5: HEW PPDU Format for Supporting MIMO-OFDMA
Proposed HEW SIG field design
  TXVECTOR parameter MCS on each sub-channels can be different
  TXVECTOR parameter NUM_STS on each sub-channels can be different
    The SU-MIMO and MU-MIMO can be applied to each sub-channels differently
  TXVECTOR parameter STBC on each sub-channels should be allowed
    IEEE 802.11ac does not allow STBC for MU-MIMO PPDU transmission
  TXVECTOR parameter FEC_CODING on each sub-channels can be different
  TXVECTOR parameter GI_TYPE on each sub-channels should be common

## Slide 6: HEW PPDU Format for Supporting MIMO-OFDMA
Proposed HEW SIG field design
 | 802.11ac MU-MIMO | 802.11ax MIMO-OFDMA
TXVECTOR parameter MCS | User-specific value | User-specific value
TXVECTOR parameter NUM_STS | User-specific value | User-specific value
TXVECTOR parameter STBC | Not Allowed | Allowed to either user-specific or common value
TXVECTOR parameter FEC_CODING | User-specific value | User-specific value
TXVECTOR parameter GI_TYPE | Common value | Common value
Discuss the more details
in the next slides

## Slide 7: Part 1) TXVECTOR parameter NUM_STS Discussion on HEW PPDU Format
When MIMO-OFDMA supports a user-specific TXVECTOR parameter NUM_STS, OFDM symbols alignment issue on HEW PSDUs is occurred
  OFDM symbols on HEW PSDUs should be aligned on each sub-channels
  Otherwise, each sub-channel needs a separate transmitter/receiver processing chains

## Slide 8: Part 1) TXVECTOR parameter NUM_STS Discussion on HEW PPDU Format
OFDM symbols alignment issue on HEW PSDUs
  Misalignment on the HEW PSDU transmission start time
    Because the number of the space time streams of the HEW PSDU transmitted on each sub-channels can be different, the number of HEW-LTFs transmitted on each sub-channels can be different
    When the OFDM symbol durations of HEW-LTF and HEW PSDU is different (such as Short GI), the OFDM symbols of HEW PSDUs are not aligned each other

## Slide 9: Part 1) TXVECTOR parameter NUM_STS Discussion on HEW PPDU Format
Proposed Solutions for OFDM symbols alignment
  First option is to make the OFDM symbol duration of HEW-LTF and the HEW PSDU as the same
  Second option is to make the number of HEW-LTFs transmitted on each sub-channels as the same

## Slide 10: Part 1) TXVECTOR parameter NUM_STS Discussion on HEW PPDU Format
First option for OFDM symbols alignment
  For example, AP transmits
    2 space time streams to each STA1 and STA2 on sub-channel 1
    1 space time stream to each STA3 and STA4 on sub-channel 2
    1 space time stream to STA5 on sub-channel 3
    1 space time stream to STA6 on sub-channel 4
  PSDU and HEW-LTF (HEW SIG-B also) are transmitted with same GI (G3 in Fig), except for the common HEW preamble field

## Slide 11: Part 1) TXVECTOR parameter NUM_STS Discussion on HEW PPDU Format
Second option for OFDM symbols alignment
  For example, AP transmits
    2 space time streams to each STA1 and STA2 on sub-channel 1
    1 space time stream to each STA3 and STA4 on sub-channel 2
    1 space time stream to STA5 on sub-channel 3
    1 space time stream to STA6 on sub-channel 4
  But, AP is equally transmitting 4 LTFs on all sub-channels

## Slide 12: Part 1) TXVECTOR parameter NUM_STS Discussion on HEW PPDU Format
Second option for OFDM symbols alignment
  AP is transmitting extra LTFs on a sub-channel if the required LTFs on the sub-channel is less than the largest one
    The total required LTFs on sub-channel 1 are 4 (i.e., no extra LTF)
    The total required LTFs on sub-channel 2 are 2 (i.e., 2 extra LTFs)
    The total required LTFs on sub-channel 3 is 1 (i.e., 3 extra LTFs)
    The total required LTFs on sub-channel 4 is 1 (i.e., 3 extra LTFs)
Extra LTFs

## Slide 13: Part 2) TXVECTOR parameter STBC Discussion on HEW PPDU Format
In 802.11ac Downlink MU-MIMO, STBC was not allowed.
In 802.11ax MIMO-OFDMA, STBC should be allowed.
But, we needs to discuss whether TXVECTOR parameter STBC is set to either
  a user-specific value or a common value.

## Slide 14: Part 2) TXVECTOR parameter STBC Discussion on HEW PPDU Format
First option for STBC: TXVECTOR parameter STBC on each sub-channels is common
  No STBC Transmission
  STBC Transmission
    TXTIME of HEW PSDUs are adjusted to have the same OFDM symbols
Note) Figures in this slide assumes the second option for OFDM symbols alignment as one of example. We are not biased to any specific option.

## Slide 15: Part 2) TXVECTOR parameter STBC Discussion on HEW PPDU Format
Second option for STBC: TXVECTOR parameter STBC on each sub-channels can be different
  For example, AP transmits
    4 space time stream with STBC on sub-channel 1 and 2
    1 space time stream without STBC on sub-channel 3 and 4
  TXTIME of HEW PSDUs are adjusted to have the same OFDM symbols
Note) Figures in this slide assumes the second option for OFDM symbols alignment as one of example. We are not biased to any specific option.

## Slide 16: Conclusion
Advanced MIMO technology of IEEE 802.11n/ac should be a base of IEEE 802.11ax new technology
Such new technologies should enhance the user experience by serving the heterogeneous users simultaneously
Also, to efficiently support heterogeneous users (having different link quality and different device capability), at least the following TXVECTOR parameters should be considered as user-specific values
  MCS, NUM_STS, FEC_CODING
And, STBC should be allowed as user-specific value or a common value