## Slide 1: Traffic Generator for OBSS Calibration Case
Date: 2014-09-14
Authors:

## Slide 2: Summary
MAC calibration for OBSS scenario was presented in July IEEE meeting
  11-14-0895-01-00ax-mac-calibration-obss-scenerio
  11-14-0972-01-00ax-mac-calibration-test-case-for-20-40-mhz-channel
The proposal was accepted and included in the
  11-14-0980-02-00ax-simulation-scenarios
The traffic generator for the 20MHz BSS traffic is based on the Weibull distribution
  2Mbps traffic, lamda = 695, k=0.8099
The concern is Weibull is too complicate to implement for the calibration scenario
Proposed to replace Weibull distribution with Poisson traffic distribution in the traffic generator

## Slide 3: Weibull vs. Poisson
Weibull
  Traffic is generated in a fixed interval
  The frame size varies based on video frame rate.
Poisson
  The inter-arrival time of frames is exponentially distributed with parameter “lambda”
  The frame size and the number of frame are fixed, for example one fixed size frame.
Poisson is more predictable and easier to implement

## Slide 4: Traffic Generator with Poisson Distribution
How to generate traffic with Poisson distribution
  MSDU length at 2000Bytes.
  Let lambda, for example, to be 100 ( in the unit of 1/second)
    The mean inter-arrival time is 1/100 second.
  The long time average data rate for the largest MSDU size is 2000*8/(1/100)=1.6Mbps
  1.6 Mbps is non-full buffer traffic since it is lower than the 20MHz BSS MCS0 rate

## Slide 5: Implementing Traffic Generator
Vendor specific implementation
  A Poisson distribution traffic generator
For NS -3
  Using On-off traffic generator
    On period: constant, say T_on
      send 1 packet
      The sum of “on” period is added to the simulation time
    Off time:
      Generating an exponentially distributed waiting time, say T_Total
      T_off = T_total-T_on

## Slide 6: Stability of the Average
How long should be the simulation time?
  Lambda is the “mean” of inter-arrival time
    How long it will take for the mean to be stabilized
How to determine the simulation time
  Each simulator calibrates its running time
    Step 1: Activate 20MHz BSS only and monitor how long it will take for the throughput of the 20MHz BSS to be stabilized.
      The throughput of the 20MHz BSS shall corresponding to the mean “inter arrival time” and record the time, t.
    Step 2: Run the OBSS MAC calibration case for at least time t.

## Slide 7: Straw Poll
Do you agree to revise the traffic generator to use Poisson traffic generator?
  Y
  N
  Abs

## Slide 8: Back Up

## Slide 9: Deferral test for network of different channel bandwidth
The set up and configuration is the same as test case 2a
  If packets collide, the both transmission fail
The first BSS operates in 40 MHz channel
The second BSS operates in a 20MHz channel which is the secondary channel of the first BSS
  With no channel model, the collision detection is determined by time domain information
    Any overlapping MPDU is considered a failure
  The secondary channel is consider free if there is no transmission on the secondary channel for PIFS
The 40MHz BSS is running full buffer.
The 20MHz BSS traffic is based on the Weibull distribution
  2Mbps traffic, lamda = 695, k=0.8099
The results other than throughput and PER of each BSS also include
  The percentage of time the 40MHz BSS running in 40 and 20 MHz mode.
AP1
AP2
STA2
STA1
BSS_2
BSS_1