## Slide 1: MAC Calibration Result
Date: 2014-09-07
Authors:

## Slide 2: Abstract
We have been doing MAC calibration and simulation using the ns-3 based platform.
This presentation describes MediaTek’s MAC calibration results based on DCN: 11-14-0967-01-00ax.

## Slide 3: Outline
Test 1a: MAC overhead without RTS/CTS
Test 1b: MAC overhead with RTS/CTS
Test 2a: Deferral Test 1
Test 2b: Deferral Test 2
Test 3: NAV deferral
Conclusions

## Slide 4: Test 1a: MAC overhead without RTS/CTS
Goal: This test case is designed to verify whether the simulator can correctly handle the basic frame exchange procedure, including DIFS+backoff procedure and A-MPDU+SIFS+BA sequence. Also to make sure the overheads are computed correctly.
Assumptions: PER is 0
Parameters:
  MSDU length:[500 : 1000 : 1500 : 2000 Bytes]
  2 MPDU limit
  RTS/CTS off
  MCS = [0 , 8]
STA 1
AP1

## Slide 5: Test 1a: MAC overhead without RTS/CTS Calibration Result
Aggregation (Number of MPDUs in A-MPDU) | Data Rate (MCS) | Application Packet Size (Bytes) | MSDU Size (Bytes) | MPDU Size (Including MPDU delimiter and padding) (Bytes) | A-MPDU Duration (Tcp2-Tcp1) (us) | SIFS (Tcp3-Tcp2) (us) | Block ACK Duration (Tcp4-Tcp3) (us) | Defer and Backoff Duration (Tcp5 –Tcp4) (AIFSN = 3, CW = 15) (us)
2 | 0 | 464 | 500 | 536 | 1364 | 16 | 68 | 110.5
2 | 0 | 964 | 1000 | 1036 | 2592 | 16 | 68 | 110.5
2 | 0 | 1464 | 1500 | 1536 | 3824 | 16 | 68 | 110.5
2 | 0 | 1964 | 2000 | 2036 | 5056 | 16 | 68 | 110.5
2 | 8 | 464 | 500 | 536 | 152 | 16 | 68 | 110.5
2 | 8 | 964 | 1000 | 1036 | 256 | 16 | 68 | 110.5
2 | 8 | 1464 | 1500 | 1536 | 356 | 16 | 68 | 110.5
2 | 8 | 1964 | 2000 | 2036 | 460 | 16 | 68 | 110.5

## Slide 6: Test 1a: MAC overhead without RTS/CTS Calibration Result
Average Time Waiting for Medium (AIFSN = 3, CW = 15) (us) | Aggregation (Number of MPDUs in A-MPDU) | Data Rate (MCS) | Application Packet Size (Bytes) | MSDU Size (Bytes) | MPDU Size (Including MPDU delimiter and padding) (Bytes) | Expected Application Throughput (Mbps) | Simulation Application Throughput (Mbps) | Expected MAC Throughput (Mbps) | Simulation MAC Throughput (Mbps)
110.5 | 2 | 0 | 464 | 500 | 536 | 4.77581 | 4.76175 | 5.14635 | 5.13120
110.5 | 2 | 0 | 964 | 1000 | 1036 | 5.53526 | 5.53028 | 5.74197 | 5.73680
110.5 | 2 | 0 | 1464 | 1500 | 1536 | 5.82904 | 5.82321 | 5.97238 | 5.9664
110.5 | 2 | 0 | 1964 | 2000 | 2036 | 5.98952 | 5.97842 | 6.09930 | 6.08800
110.5 | 2 | 8 | 464 | 500 | 536 | 21.67591 | 21.70555 | 23.35766 | 23.38960
110.5 | 2 | 8 | 964 | 1000 | 1036 | 34.54423 | 34.64847 | 35.83427 | 35.94240
110.5 | 2 | 8 | 1464 | 1500 | 1536 | 42.86185 | 42.70664 | 43.91583 | 43.75680
110.5 | 2 | 8 | 1964 | 2000 | 2036 | 48.30746 | 48.15100 | 49.19293 | 49.03360

## Slide 7: Test 1b: MAC overhead with RTS/CTS
Goal: This test case is designed to further verify whether the simulator can correctly handle the frame exchange procedure with RTS/CTS protection based on test1a. It also tests whether the correct overhead computation with RTS /CTS.
Assumptions: PER is 0
Parameters:
  MSDU length:[500 : 1000 : 1500 : 2000 Bytes]
  2 MPDU limit
  RTS/CTS on
  MCS = [0 , 8]
STA 1
AP1

## Slide 8: Test 1b: MAC overhead without RTS/CTS Calibration Result
Aggregation (Number of MPDUs in A-MPDU) | Data Rate (MCS) | Application Packet Size (Bytes) | MSDU Size (Bytes) | MPDU Size (Including MPDU delimiter and padding) (Bytes) | RTS Duration (Tcp2 - Tcp1) (us) | CTS Duration (Tcp4 - Tcp3) (us) | Frame Duration (Tcp6 - Tcp5) (us)
2 | 0 | 464 | 500 | 536 | 52 | 44 | 1364
2 | 0 | 964 | 1000 | 1036 | 52 | 44 | 2592
2 | 0 | 1464 | 1500 | 1536 | 52 | 44 | 3824
2 | 0 | 1964 | 2000 | 2036 | 52 | 44 | 5056
2 | 8 | 464 | 500 | 536 | 52 | 44 | 152
2 | 8 | 964 | 1000 | 1036 | 52 | 44 | 256
2 | 8 | 1464 | 1500 | 1536 | 52 | 44 | 356
2 | 8 | 1964 | 2000 | 2036 | 52 | 44 | 460

## Slide 9: Test 1b: MAC overhead with RTS/CTS Calibration Result
Average Time Waiting for Medium (AIFSN = 3, CW = 15) (us) | Aggregation (Number of MPDUs in A-MPDU) | Data Rate (MCS) | Application Packet Size (Bytes) | MSDU Size (Bytes) | MPDU Size (Including MPDU delimiter and padding) (Bytes) | Expected Application Throughput (Mbps) | Simulation Application Throughput (Mbps) | Expected MAC Throughput (Mbps) | Simulation MAC Throughput (Mbps)
110.5 | 2 | 0 | 464 | 500 | 536 | 4.41248 | 4.39909 | 4.75483 | 4.74040
110.5 | 2 | 0 | 964 | 1000 | 1036 | 5.29216 | 5.28735 | 5.48979 | 5.48480
110.5 | 2 | 0 | 1464 | 1500 | 1536 | 5.64910 | 5.64401 | 5.78801 | 5.78280
110.5 | 2 | 0 | 1964 | 2000 | 2036 | 5.87069 | 5.83701 | 5.95404 | 5.94400
110.5 | 2 | 8 | 464 | 500 | 536 | 15.77896 | 15.78565 | 17.00319 | 17.01040
110.5 | 2 | 8 | 964 | 1000 | 1036 | 26.84769 | 26.89637 | 27.85030 | 27.90080
110.5 | 2 | 8 | 1464 | 1500 | 1536 | 34.72795 | 34.61599 | 35.58191 | 35.46720
110.5 | 2 | 8 | 1964 | 2000 | 2036 | 40.36480 | 40.24157 | 41.10469 | 40.97920

## Slide 10: Test 2a: Deferral Test 1
Goal: This test case is designed to verify whether the simulator can correctly handle deferral procedure after collision happens without hidden nodes. It also checks whether deferral because of energy levels is happening correctly.
Assumptions: All devices are within energy detect range of each other. When AP1 and AP2 start to transmit on the same slot, both packets are lost (PER= 100%). Otherwise packets get through 100%. PER=0 %.
Parameters:
  MSDU length:[500 : 1000 : 1500 2000 Bytes]
  2 MPDU limit
  RTS/CTS [Off, On]
  MCS = [0]
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)

## Slide 11: Test 2a: Deferral Test 1 Calibration Result
RTS/CTS | Average Time Waiting for Medium (AIFSN = 3, CW = 15) (us) | Aggregation (Number of MPDUs in A-MPDU) | Data Rate (MCS) | Application Packet Size (Bytes) | MSDU Size (Bytes) | MPDU Size (Including MPDU delimiter and padding) (Bytes) | PER (%) | Simulation Application Throughput (Mbps) | Simulation MAC Throughput (Mbps)
Off | 110.5 | 2 | 0 | 464 | 500 | 536 | 11.07752 | 4.70931 | 5.07468
Off | 110.5 | 2 | 0 | 964 | 1000 | 1036 | 11.05631 | 5.48144 | 5.68614
Off | 110.5 | 2 | 0 | 1464 | 1500 | 1536 | 11.05517 | 5.77584 | 5.91787
Off | 110.5 | 2 | 0 | 1964 | 2000 | 2036 | 11.05883 | 5.93572 | 6.04452
On | 110.5 | 2 | 0 | 464 | 500 | 536 | 0 | 4.35062 | 4.68817
On | 110.5 | 2 | 0 | 964 | 1000 | 1036 | 0 | 5.24275 | 5.43854
On | 110.5 | 2 | 0 | 1464 | 1500 | 1536 | 0 | 5.61508 | 5.75315
On | 110.5 | 2 | 0 | 1964 | 2000 | 2036 | 0 | 5.81210 | 5.91863

## Slide 12: Test 2b: Deferral Test 2
Goal: This test case is designed to verify whether the simulator can correctly the handle deferral procedure after collision happens with the existing of hidden nodes.
Assumptions: AP1 and AP2 can not hear each other. (ever) If MPDUs from AP1 and AP2 overlap, they both fail with 100% probability. If an MPDU from AP1/AP2 is interference free, it succeeds with 100% probability.
Parameters:
  MSDU length:[1500 Bytes]
  2 MPDU limit
  RTS/CTS [Off]
  MCS = [0]
STA 1
AP 2
AP1
STA 2

## Slide 13: Test 2b: Deferral Test 2 Calibration Result
RTS/CTS | Average Time Waiting for Medium (AIFSN = 3, CW = 15) (us) | Aggregation (Number of MPDUs in A-MPDU) | Data Rate (MCS) | Application Packet Size (Bytes) | MSDU Size (Bytes) | MPDU Size (Including MPDU delimiter and padding) (Bytes) | PER (%) | Simulation Application Throughput (Mbps) | Simulation MAC Throughput (Mbps)
Off | 110.5 | 2 | 0 | 1464 | 1500 | 1536 | 99.37651 | 0.03631 | 0.03720

## Slide 14: Test 3: NAV Deferral
Goal: This test case is designed to verify whether the simulator can correctly the handle deferral procedure after collision happens with the existing of hidden nodes.
Assumptions: AP1 and AP2 can not hear each other. (ever) If MPDUs from AP1 and AP2 overlap, they both fail with 100% probability. If an MPDU from AP1/AP2 is interference free, it succeeds with 100% probability.
Parameters:
  MSDU length:[1500 Bytes]
  2 MPDU limit
  RTS/CTS [On]
  MCS = [0]
STA 1
AP 2
AP1
STA 2

## Slide 15: Test 3: NAV Deferral Calibration Result
RTS/CTS | Average Time Waiting for Medium (AIFSN = 3, CW = 15) (us) | Aggregation (Number of MPDUs in A-MPDU) | Data Rate (MCS) | Application Packet Size (Bytes) | MSDU Size (Bytes) | MPDU Size (Including MPDU delimiter and padding) (Bytes) | PER (%) | Simulation Application Throughput (Mbps) | Simulation MAC Throughput (Mbps)
On | 110.5 | 2 | 0 | 1464 | 1500 | 1536 | 0 | 5.63933 | 5.77800

## Slide 16: Conclusions
Variation of simulation result for Test case 1 comparing to expected result.
  Less than 0.6%.
In Test 2b, since both AP1 and AP2 can not hear each other and overlapped MPDUs from AP1 and AP2 are both fail. The PER is very high.
  PER = 99.35618%.
  Simulation parameters can be specified more precisely.