## Slide 1: Further Study of Time Varying Interference and PHY Abstraction
Date: 2014-11-02
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com
Jinjing Jiang |  |  |  | 
Bo Sun | ZTE |  |  | Sun.bo1@zte.com.cn
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Leif Wilhelmsson | Ericsson |  |  | leif.r.wilhelmsson@ericsson.com

## Slide 2: Introduction
Basic procedure of PHY abstraction in [1] is open to how to model time-varying interference.
Different models have been studied in [2], among which a block-wise PER model has been shown to be more accurate.
Some further studies on the time-varying interference are presented here.

## Slide 3: Concerns on Time Varying Interference Modeling
There have been concerns regarding the necessity of modeling time-varying interference.
  How often a MPDU sees time-varying interference?
  How large the interference level changes?
We collected the statistics of interference through integrated system level simulation.

## Slide 4: Simulation Assumptions
Residential (Scenario 1)
  4 STAs per apartment
  2.4GHz, each AP in an apartment uses a randomly selected 20MHz channel (out of 3 non-overlapping 20MHz channels).
  UL only
  Fixed MCS7
  CCA at -82dBm for the associated AP, and -82/-72/-62dBm for OBSS.
  Other simulation assumptions are based on [3]
Interference collection:
  A subframe sees many interference events (too many BSS’s around)
  Many of them do not matter (negligible interference levels change for far-away BSS)
  Only count interference change over 0.5dB.

## Slide 5: Interference Statistics
If a subframe sees an interference change:
  More than 50% of subframes under a 5dB interference rise, and 20% or more under a 10dB interference rise
  More than 30% of interference are less than 1/3 of subframe length.
As inter-BSS CCA threshold increases, stronger interference changes for a subframe

## Slide 6: Interference Statistics (2)
Inter-BSS CCA (dBm) | -82 | -72 | -62
2 interference levels in a subframe | 8.4% | 18.8% | 43.9%
2 or more interference levels in a subframe | 13.5% | 27.8% | 59.1%
5dB interference rise for less than 1/3 of subframe length | 2.7% | 5.6% | 10.2%
10dB interference rise for less than 1/3 of subframe length | 1.7% | 2.9% | 4.5%
Time varying interference experienced by a subframe is not negligible.
The issue becomes more significant if spatial reuse is under consideration.
It is important to handle the time-varying interference accurately.
[2] shows weakest link underestimate PER for a short and strong interference rise.

## Slide 7: Recap of Potential Solutions
Whole packet average
  T0=1, T=L
  Simulation shows it severely underestimate the PER under time varying interference.
Weakest link
  T0=argmin_t SINR(t), T=1
  PER estimation is improved but it still can overestimate PER for the short and strong interference rise.
Block-wise PHY abstraction
  For each event n, T0=Tk , T=1  PERk , k=1…K, and
  Most accurate and robust to time varying interference [2].
A simplified version of block-wise PHY abstraction to balance the performance and complexity.

## Slide 8: Proposed Text Change in [1]

## Slide 9: Conclusion
System level simulation shows interference change within a subframe is not negligible.
More significant interference change for spatial reuse.
An accurate PHY abstraction is needed to handle time-varying interference
  Block wise PHY abstraction or the simplified model
Proposed text change in [1] to complete the PHY abstraction procedure.

## Slide 10: Reference
[1] 11-14-0571-03-00ax-evaluation-methodology
[2] 11-14-1174-00-00ax-PHY-abstraction-for-time-varying-interference
[3] 11-14-0980-04-00ax-simulation-scenarios