## Slide 1: Protocol and signaling framework for OFDMA
Date:
Authors:

## Slide 2: Introduction
OFDMA is a promising candidate technology for increasing throughput in high-density networks
  Performance has been discussed in [1]
  More detailed technical proposals in [2-4]

## Slide 3: Protocol and signaling framework for OFDMA
OFDMA needs a protocol and signaling framework to operate in practice
  Which users to combine?
  Transmission parameters per user (#streams, MCS)
  …
IEEE 802.11-14/1210 : HEW PPDU Format for Supporting MIMO-OFDMA
  Flexibility per user (MCS, #streams, coding type)
  Discussion of preamble design
  Discussion of ACK mechanism

## Slide 4: Observation
For practical implementation of OFDMA, many of the necessary concepts already exist in MU-MIMO
  Grouping and group management
  Signaling through user position (instead of STA ID, …)
  Per-user parameter values (MCS, FEC, …)
  ACK procedures for multiple users
We should consider the MU-MIMO protocol and signaling as a basis for OFDMA
  Proven concepts
  Facilitate combined MU-MIMO/OFDMA systems

## Slide 5: Grouping
MU-MIMO groups users in semi-static groups
Group ID management frames establish and modify the members of the group and their positions within a group
For OFDMA:
  Define similar “OFDMA group” concept
  Define (or re-use) group management frame to select users and to assign users “their” frequency segment (“user position”)
  Example re-definition of “user position”:

## Slide 6: Per-user transmission parameters
In MU-MIMO:
  # streams and FEC type are signaled per user in VHT-SIG-A for up to 4 users
  MCS signaled per user in VHT-SIG-B
OFDMA:
  Almost complete re-use of parameters in VHT-SIG-A and VHT-SIG-B (or equivalent ax fields)
    No redefinition
    No additional bits/symbols in preamble
  VHT-SIG-B will contain different information per (20 MHz) frequency segment

## Slide 7: ACK mechanism
MU-MIMO
  one immediate ACK, followed by one or more BAR/ACK exchanges
OFDMA
  Similar mechanism applies
  More advanced ACK mechanism can be considered, but it is suggested to at least support the current mechanism for OFDMA

## Slide 8: Limitations
MU-MIMO
  Up to 4 users, Up to 8 total streams
OFDMA
  Maintain same limitations
  If the number of users or total number of streams is increased in 11ax, apply to both MU-MIMO and OFDMA

## Slide 9: Preamble considerations
Legacy preamble (incl. VHT-SIG-A) similar to 11ac
VHT-STF and VHT-LTF duplicated across the band
VHT-LTF
  Same number of VHT-LTF symbols for all users
  If not all users have the same number of streams, insert extra symbols
    Simple extension of current signal definition
    Actually improves channel estimation for users with lower # streams
VHT-SIG-B
  Possibly different content per 20 MHz

## Slide 10: Receiver consideration
Receiver typically processes legacy preamble (incl. VHT-SIG-A) on the primary 20 MHz channel
  All 20 MHz channels carry the same information
Parse VHT-SIG-A
  GROUP_ID identifies the packet as OFDMA
  GROUP_ID identifies the 20 MHz band for the receiving STA
  Max #streams across all users establishes # VHT-LTF symbols
After VHT-SIG-A, switch further processing to the appropriate 20 MHz channel
Process the remaining frame (incl. VHT-LTF, VHT-SIG-B, data) as a 20 MHz frame
  NOTE: discussion is given for 20 MHz channels. Extension to other cases is straightforward.

## Slide 11: Conclusion
The MU-MIMO protocol and signaling framework provides many of the elements that are needed for OFDMA
We should consider the existing framework as the basis for OFDMA. Specifically:
  Grouping/group ID
  Identify users by group and user position
  Per-user signaling in preamble fields (similar to 11ac)
  ACK mechanism using combination of immediate and BAR

## Slide 12: References
[1] IEEE 802.11-14/1227: “OFDMA Performance Analysis”
[2] IEEE 802.11-14/1208: “MAC considerations on 802.11ax OFDMA”
[3] IEEE 802.11-14/1210: “HEW PPDU Format for Supporting MIMO-OFDMA”
[4] IEEE 802.11-14/0839: “Discussion on OFDMA in IEEE 802.11ax”