## Slide 1: Considerations on DL OFDMA control mechanism
Date: 2014-11-04
Authors:

## Slide 2: Introduction
Numerically analysis of the gain of DL-OFDMA
Discussion on limitation of basic access and RTS/CTS for DL-OFDMA in dense OBSS environment, and necessity of additional coordination mechanism for DL-OFDMA
Analysis the effect of coordination overhead on AP and network throughput

## Slide 3: DL-UL asymmetry and DL OFDMA
DL-UL asymmetry
  Same prioritized contention of AP
    Same opportunity for accessing medium: 1/(N+1)[1]
  The starvation of AP gets severer as network gets denser
  Overall network performance degradation
DL OFDMA
  AP could deal with multiple STAs data at the same time
    Transmitting K STAs data -> mean contention period: 1/K
  Total access delay will be greatly reduced
  Overall MAC efficiency increases
    The duration of data increases while the duration of overhead remains the same
  Multi user diversity gain

## Slide 4: Access delay analysis of DL-OFDMA[2]
Every STA has data with the same size
Each STA is perfectly synchronized with each other
E[D] vs. 4E[D’]

## Slide 5: Other network settings
Only AP utilizes widerband
  UL transmission only through the primary 20MHz bandwidth
Bandwidth: 20, 40, 80, 160 MHz
  DL-OFDMA vs. 11ac widerband operation
  2 STAs DL data for 40MHz
  4 STAs DL data for 80MHz
  8 STAs DL data for 160MHz

## Slide 6: Transmission parameter
Guard interval: long
Data preamble: 11ac
Max retries: 10
Fixed MCS: MCS8 (78 Mbit/s)
RTS/CTS & BA
Cwmin: 15
PER: 0
MSDU length: 8000 bytes
Application data size: 7964 bytes
L4 – L3 header overhead: 36 bytes
SIFS: 16us, DIFS: 34us
MPDU size = (MSDU + MAC header + delimiter)*8 + padding + service + tail = (8000 + 30 + 4)*2*8 + 16 + 16 + 6 = 128582 bits
MPDU duration = ceil((FrameLength*8) /rate /OFDMsymbolduration) * OFDMsymbolduration + PHY Header = ceil(128582/6.5/4) * 4 + 40

## Slide 7: Comparison of mean access delay between 11ac widerband operation and DL-OFDMA
Contention periods dominates AP’s access delay and throughput
Contention isolation of DL-OFDMA reduces greatly the total access delay for multiple user DL data

## Slide 8: DL OFDMA in dense OBSS environment(1)
Considering a dense OBSS environment
  STAs might belong to the radio range of different OBSSs
  AP and STAs might see the busy/idle state of secondary channels differently
  AP could not guarantee that DL target STAs, allocated at secondary channel, will receive data successfully
DL OFDMA might not be utilized efficiently in dense OBSS environment

## Slide 9: DL OFDMA in dense OBSS environment(2)
Both basic access and RTS/CTS have no functionalities compensating unused secondary bands

## Slide 10: DL OFDMA in dense OBSS environment(3)
probability p: probability that a STA receives data successfully through each secondary channel independently from the AP
The throughput of DL OFDMA will decreases proportionally to p
Existence of p reduces the contention isolation gain of DL OFDMA
-26%
-52%

## Slide 11: Existing control mechanisms in DL OFDMA
AP cannot predict which STAs are able to respond RTS through secondary bands
  AP has no channel state information of STAs
Existing RTS/CTS mechanism is not suitable for DL-OFDMA
Further coordination might be necessary along with current RTS/CTS mechanism
  In order to achieve the contention isolation gain from DL OFDMA, it is required to increase the probability of successful CTS transmission of STAs (p)

## Slide 12: Simple examples of coordination for DL OFDMA
CH state feedback
RTS/CTS modification
Coordination could increase the probability p
tco: total additional overhead for DL-OFDMA
Coordination overhead (tco)
tco

## Slide 13: Trade off of coordination
Various solutions could be developed
Coordination will introduce additional overhead in time
Depending on the types of coordination, the coordination gain and overhead could vary
  Trade off between coordination gain and overhead

## Slide 14: Expected AP throughput enhancement
With proper coordination, AP throughput can be enhanced even with a large value of coordination overhead (tco=500 microsec)
+53% (n=5), +55% (n=50)
+33% (n=5), +52% (n=50)

## Slide 15: Network throughput comparison
How much the coordination overhead will affect the overall network throughput?
+7% (n=5), +28% (n=10)
-7% (n=5), +25% (n=10)

## Slide 16: Summary
Coordination for increasing the probability of transmitting CTS(p) will enhance the AP throughput
  helps to solve the DL-UL asymmetry problem
  Coordination schemes can be developed in various ways
  Trade off between the increment of p and coordination overhead
As network gets denser (chance of transmitting data decreases), the effect of overhead decreases in terms of both AP throughput and overall network throughput

## Slide 17: Conclusion
DL-OFDMA is a promising technique for contention isolation which could reduces DL-UL asymmetry problem
In dense OBSS environment, busy/idle state of secondary channels could be different by the location of STAs
Existing basic access or RTS/CTS mechanism is not a proper to control DL-OFDMA especially in dense OBSS environment
Additional coordination is required to fully utilize DL-OFDMA
The effect of coordination overhead on AP and network throughput is not severe as network gets denser
More in-depth discussions on DL-OFDMA coordination is necessary

## Slide 18: References
[1]11-13-1377-00-0hew-dl-efficiency-enhancement-in-high-dense-network
[2] Wang, Yunbo, Mehmet C. Vuran, and Steve Goddard. "Cross-layer analysis of the end-to-end delay distribution in wireless sensor networks." IEEE/ACM Transactions on Networking (TON) 20.1 (2012): 305-318.