## Slide 1: Empirical open-air VHT client scaling results for use in validating MAC simulators
Date: 2014-11-05
Authors:

## Slide 2: Abstract
Numerous MAC simulation results have been presented based on the Simulation Scenarios (SS). Vendors are cross-checking results.
SS2, SS3 and SS4 involve large numbers of co-located STAs, albeit with induced path loss due to walls, etc.
Aruba has a Very High Density (VHD) lab taking empirical data with late-model clients in open air
This contribution presents actual lab TCP data taken in open air with 50 STAs each of 1SS, 2SS and 3SS. Data is presented for VHT20, VHT40 and VHT80.
Our goal is to help vendors further validate the accuracy of their MAC & PHY simulators by sharing our data set.

## Slide 3: Our Box 5 Emulator

## Slide 4: Testbed Configuration
Clients:
  Smartphone, 11ac, 1SS, 100 stations
  Laptop, 11ac, 2SS, 100 stations
  Laptop, 11ac, 3SS, 100 stations
Controller & AP:
  7220-US controller running 6.4.0.3-HDMS public code.
  Aruba AP225 (11ac 3SS)
LAN:
  Jumbo frames enabled
Test Automation:
  IxChariot 8.1EA. Separate, dedicated machines for console and wired endpoint.
RF configuration:
  Channels - 100E (VHT80), 100+ (VHT40), 100 (VHT20).
  Exclusive use of 5490 - 5570MHz / swept daily.

## Slide 5: Aruba VHD Testbed Topology

## Slide 6: SSID Configuration
wlan ssid-profile "hdtest100-ssid"
essid "HDTest-5"
a-basic-rates 24
a-tx-rates 18 24 36 48 54
g-basic-rates 18
g-tx-rates 18 24 36 48 54
max-clients 255
wmm
wmm-vo-dscp "56"
wmm-vi-dscp "40"
g-beacon-rate 24
a-beacon-rate 24
!
wlan ht-ssid-profile "HDtest-htssid-profile"
max-tx-a-msdu-count-be 3
!
rf dot11a-radio-profile "hdtest100-11a-pf"
channel 100E
disable-arm-wids-functions Dynamic
!

## Slide 7: Known Issues
VHT80 - 3SS Laptop TCP Downstream
VHT80 – 1SS Phone TCP Bidirectional
VHT20 – 3SS Laptop TCP Upstream

## Slide 8: VHT80 - 1SS, 2SS & 3SS (Aggregate - Mbps)

## Slide 9: VHT80 - 1SS, 2SS & 3SS (Aggregate - %)
25% - 40% contention premium

## Slide 10: VHT80 - 1SS, 2SS & 3SS (Per-Client Avg)

## Slide 11: VHT40 - 1SS, 2SS & 3SS (Aggregate - Mbps)

## Slide 12: VHT40 - 1SS, 2SS & 3SS (Aggregate - %)
11% - 37% contention premium

## Slide 13: VHT40 - 1SS, 2SS & 3SS (Per-Client Avg)

## Slide 14: VHT20 - 1SS, 2SS & 3SS (Aggregate - Mbps)

## Slide 15: VHT20 - 1SS, 2SS & 3SS (Aggregate - %)
3% - 38% contention premium

## Slide 16: VHT20 - 1SS, 2SS & 3SS (Per Client Avg)

## Slide 17: Raw #s – VHT20 Aggregate
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
1SS Phone_VHT20_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 65.90 | 60.40 | 52.90 | 64.67 | 63.74 | 56.98 | 59.06 | 63.71 | 62.57 | 56.93 | 57.74 | 56.81 | 43.23 | 49.51 | 50.80
Run 2 | 65.65 | 58.81 | 52.97 | 65.14 | 64.08 | 60.30 | 63.98 | 63.84 | 60.53 | 55.74 | 55.40 | 55.76 | 41.25 | 53.26 | 52.97
Run 3 | 61.04 | 63.15 | 48.56 | 64.12 | 64.27 | 60.07 | 61.90 | 63.98 | 60.24 | 53.82 | 51.83 | 55.15 | 44.45 | 51.73 | 45.99
Average Throughput | 64.20 | 60.79 | 51.47 | 64.64 | 64.03 | 59.12 | 61.65 | 63.85 | 61.11 | 55.50 | 54.99 | 55.91 | 42.98 | 51.50 | 49.92
Total Pairs (Chariot) | 2 | 4 | 4 | 5 | 20 | 5 | 10 | 40 | 10 | 25 | 50 | 25 | 50 | 100 | 50
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
2SS Laptop_VHT20_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 138.43 | 137.36 | 142.46 | 125.58 | 136.06 | 136.94 | 120.14 | 138.42 | 132.07 | 111.47 | 132.80 | 127.12 | 96.99 | 109.79 | 98.73
Run 2 | 141.98 | 140.21 | 142.75 | 128.63 | 133.03 | 136.30 | 124.11 | 142.46 | 130.18 | 113.61 | 133.40 | 127.37 | 87.79 | 101.50 | 101.97
Run 3 | 142.03 | 138.05 | 143.26 | 123.99 | 137.28 | 136.00 | 120.62 | 139.29 | 129.23 | 113.07 | 128.63 | 128.00 | 87.66 | 100.77 | 97.22
Average Throughput | 140.81 | 138.54 | 142.82 | 126.07 | 135.45 | 136.41 | 121.62 | 140.06 | 130.49 | 112.72 | 131.61 | 127.50 | 90.81 | 104.02 | 99.31
Total Pairs (Chariot) | 10 | 20 | 10 | 20 | 40 | 20 | 80 | 160 | 80 | 100 | 200 | 100 | 100 | 200 | 100
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
3SS Laptop_VHT20_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 232.01 | 179.03 | 217.47 | 208.52 | 194.58 | 208.39 | 202.83 | 212.15 | 199.96 | 178.76 | 199.04 | 189.59 | 144.47 | 158.17 | 160.30
Run 2 | 228.86 | 186.08 | 214.18 | 208.22 | 196.20 | 200.60 | 202.61 | 210.80 | 195.15 | 177.59 | 198.26 | 188.82 | 150.10 | 156.84 | 155.82
Run 3 | 234.29 | 191.01 | 207.43 | 206.45 | 190.16 | 202.10 | 202.96 | 201.83 | 202.67 | 180.93 | 190.21 | 188.50 | 136.46 | 151.94 | 158.69
Average Throughput | 231.72 | 185.37 | 213.03 | 207.73 | 193.65 | 203.70 | 202.80 | 208.26 | 199.26 | 179.09 | 195.84 | 188.97 | 143.68 | 155.65 | 158.27
Total Pairs (Chariot) | 20 | 20 | 20 | 40 | 40 | 40 | 160 | 320 | 160 | 200 | 300 | 200 | 200 | 300 | 200

## Slide 18: Raw #s – VHT20 Per Client
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
1SS Phone_VHT20_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 65.90 | 60.40 | 52.90 | 12.93 | 12.75 | 11.40 | 5.91 | 6.37 | 6.26 | 2.28 | 2.31 | 2.27 | 0.86 | 0.99 | 1.02
Run 2 | 65.65 | 58.81 | 52.97 | 13.03 | 12.82 | 12.06 | 6.40 | 6.38 | 6.05 | 2.23 | 2.22 | 2.23 | 0.82 | 1.07 | 1.06
Run 3 | 61.04 | 63.15 | 48.56 | 12.82 | 12.85 | 12.01 | 6.19 | 6.40 | 6.02 | 2.15 | 2.07 | 2.21 | 0.89 | 1.03 | 0.92
Per Client Throughput | 64.20 | 60.79 | 51.47 | 12.93 | 12.81 | 11.82 | 6.16 | 6.38 | 6.11 | 2.22 | 2.20 | 2.24 | 0.86 | 1.03 | 1.00
Total Pairs (Chariot) | 2 | 4 | 4 | 5 | 20 | 5 | 10 | 40 | 10 | 25 | 50 | 25 | 50 | 100 | 50
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
2SS Laptop_VHT20_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 138.43 | 137.36 | 142.46 | 25.12 | 27.21 | 27.39 | 12.01 | 13.84 | 13.21 | 4.46 | 5.31 | 5.08 | 1.94 | 2.20 | 1.97
Run 2 | 141.98 | 140.21 | 142.75 | 25.73 | 26.61 | 27.26 | 12.41 | 14.25 | 13.02 | 4.54 | 5.34 | 5.09 | 1.76 | 2.03 | 2.04
Run 3 | 142.03 | 138.05 | 143.26 | 24.80 | 27.46 | 27.20 | 12.06 | 13.93 | 12.92 | 4.52 | 5.15 | 5.12 | 1.75 | 2.02 | 1.94
Per Client Throughput | 140.81 | 138.54 | 142.82 | 25.21 | 27.09 | 27.28 | 12.16 | 14.01 | 13.05 | 4.51 | 5.26 | 5.10 | 1.82 | 2.08 | 1.99
Total Pairs (Chariot) | 10 | 20 | 10 | 20 | 40 | 20 | 80 | 160 | 80 | 100 | 200 | 100 | 100 | 200 | 100
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
3SS Laptop_VHT20_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 232.01 | 179.03 | 217.47 | 41.70 | 38.92 | 41.68 | 20.28 | 21.22 | 20.00 | 7.15 | 7.96 | 7.58 | 2.89 | 3.16 | 3.21
Run 2 | 228.86 | 186.08 | 214.18 | 41.64 | 39.24 | 40.12 | 20.26 | 21.08 | 19.51 | 7.10 | 7.93 | 7.55 | 3.00 | 3.14 | 3.12
Run 3 | 234.29 | 191.01 | 207.43 | 41.29 | 38.03 | 40.42 | 20.30 | 20.18 | 20.27 | 7.24 | 7.61 | 7.54 | 2.73 | 3.04 | 3.17
Per Client Throughput | 231.72 | 185.37 | 213.03 | 41.55 | 38.73 | 40.74 | 20.28 | 20.83 | 19.93 | 7.16 | 7.83 | 7.56 | 2.87 | 3.11 | 3.17
Total Pairs (Chariot) | 20 | 20 | 20 | 40 | 40 | 40 | 160 | 320 | 160 | 200 | 300 | 200 | 200 | 300 | 200

## Slide 19: Raw #s – VHT40 Aggregate
 | 1 | Clients |  | 5 | Up |  | 10 | Up |  | 25 | Up |  | 50 | Up | 
1SS Phone_VHT40_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 132.94 | 129.35 | 107.51 | 134.52 | 140.37 | 118.17 | 125.15 | 138.05 | 116.06 | 105.12 | 120.03 | 117.77 | 102.12 | 99.75 | 92.35
Run 2 | 131.40 | 133.16 | 102.60 | 133.68 | 139.98 | 114.98 | 122.19 | 135.25 | 120.93 | 104.52 | 127.81 | 117.61 | 91.65 | 92.97 | 91.22
Run 3 | 134.63 | 133.37 | 102.97 | 134.06 | 139.30 | 115.75 | 125.21 | 137.27 | 123.07 | 99.47 | 127.83 | 117.98 | 101.56 | 91.90 | 91.49
Average Throughput | 132.99 | 131.96 | 104.36 | 134.09 | 139.88 | 116.30 | 124.19 | 136.85 | 120.02 | 103.04 | 125.22 | 117.79 | 98.45 | 94.88 | 91.69
Total Pairs (Chariot) | 2 | 4 | 1 | 5 | 20 | 5 | 10 | 40 | 10 | 25 | 100 | 25 | 50 | 100 | 50
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
2SS Laptop_VHT40_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 319.91 | 312.85 | 324.36 | 288.98 | 307.41 | 309.28 | 274.80 | 317.48 | 305.25 | 236.98 | 303.12 | 279.50 | 207.98 | 245.66 | 247.47
Run 2 | 320.97 | 313.33 | 322.23 | 289.47 | 304.95 | 301.76 | 281.19 | 312.43 | 303.41 | 232.62 | 311.34 | 280.50 | 219.38 | 240.89 | 248.30
Run 3 | 320.75 | 317.77 | 319.79 | 289.47 | 304.80 | 306.99 | 285.37 | 313.72 | 307.36 | 231.44 | 314.87 | 280.50 | 210.21 | 239.95 | 251.29
Average Throughput | 320.54 | 314.65 | 322.13 | 289.31 | 305.72 | 306.01 | 280.45 | 314.54 | 305.34 | 233.68 | 309.78 | 280.17 | 212.53 | 242.17 | 249.02
Total Pairs (Chariot) | 10 | 20 | 10 | 40 | 40 | 20 | 80 | 160 | 80 | 100 | 300 | 200 | 200 | 300 | 200
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
3SS Laptop_VHT40_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 467.26 | 480.71 | 481.21 | 426.20 | 470.29 | 465.58 | 413.80 | 485.90 | 449.88 | 373.68 | 469.74 | 410.38 | 294.86 | 387.55 | 375.61
Run 2 | 467.07 | 482.29 | 472.51 | 426.52 | 477.59 | 466.17 | 414.06 | 483.76 | 452.36 | 377.72 | 461.75 | 415.26 | 306.52 | 388.64 | 375.65
Run 3 | 467.17 | 478.34 | 470.72 | 426.24 | 468.50 | 466.54 | 417.00 | 478.91 | 452.96 | 376.63 | 464.69 | 414.42 | 307.66 | 393.39 | 380.34
Average Throughput | 467.17 | 480.45 | 474.81 | 426.32 | 472.12 | 466.09 | 414.95 | 482.86 | 451.73 | 376.01 | 465.39 | 413.35 | 303.01 | 389.86 | 377.20
Total Pairs (Chariot) | 20 | 20 | 10 | 40 | 80 | 40 | 160 | 320 | 160 | 200 | 500 | 200 | 300 | 500 | 200

## Slide 20: Raw #s – VHT40 Per Client
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
1SS Phone_VHT40_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 132.94 | 129.35 | 107.51 | 26.90 | 28.07 | 23.63 | 12.52 | 13.80 | 11.61 | 4.20 | 4.80 | 4.71 | 2.04 | 2.00 | 1.85
Run 2 | 131.40 | 133.16 | 102.60 | 26.74 | 28.00 | 23.00 | 12.22 | 13.52 | 12.09 | 4.18 | 5.11 | 4.70 | 1.83 | 1.86 | 1.82
Run 3 | 134.63 | 133.37 | 102.97 | 26.81 | 27.86 | 23.15 | 12.52 | 13.73 | 12.31 | 3.98 | 5.11 | 4.72 | 2.03 | 1.84 | 1.83
Per Client Throughput | 132.99 | 131.96 | 104.36 | 26.82 | 27.98 | 23.26 | 12.42 | 13.69 | 12.00 | 4.12 | 5.01 | 4.71 | 1.97 | 1.90 | 1.83
Total Pairs (Chariot) | 2 | 4 | 1 | 5 | 20 | 5 | 10 | 40 | 10 | 25 | 100 | 25 | 50 | 100 | 50
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
2SS Laptop_VHT40_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 319.91 | 312.85 | 324.36 | 57.80 | 61.48 | 61.86 | 27.48 | 31.75 | 30.52 | 9.48 | 12.12 | 11.18 | 4.16 | 4.91 | 4.95
Run 2 | 320.97 | 313.33 | 322.23 | 57.89 | 60.99 | 60.35 | 28.12 | 31.24 | 30.34 | 9.30 | 12.45 | 11.22 | 4.39 | 4.82 | 4.97
Run 3 | 320.75 | 317.77 | 319.79 | 57.89 | 60.96 | 61.40 | 28.54 | 31.37 | 30.74 | 9.26 | 12.59 | 11.22 | 4.20 | 4.80 | 5.03
Per Client Throughput | 320.54 | 314.65 | 322.13 | 57.86 | 61.14 | 61.20 | 28.05 | 31.45 | 30.53 | 9.35 | 12.39 | 11.21 | 4.25 | 4.84 | 4.98
Total Pairs (Chariot) | 10 | 20 | 10 | 40 | 40 | 20 | 80 | 160 | 80 | 100 | 300 | 200 | 200 | 300 | 200
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
3SS Laptop_VHT40_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 467.26 | 480.71 | 481.21 | 85.24 | 94.06 | 93.12 | 41.38 | 48.59 | 44.99 | 14.95 | 18.79 | 16.42 | 5.90 | 7.75 | 7.51
Run 2 | 467.07 | 482.29 | 472.51 | 85.30 | 95.52 | 93.23 | 41.41 | 48.38 | 45.24 | 15.11 | 18.47 | 16.61 | 6.13 | 7.77 | 7.51
Run 3 | 467.17 | 478.34 | 470.72 | 85.25 | 93.70 | 93.31 | 41.70 | 47.89 | 45.30 | 15.07 | 18.59 | 16.58 | 6.15 | 7.87 | 7.61
Per Client Throughput | 467.17 | 480.45 | 474.81 | 85.26 | 94.42 | 93.22 | 41.50 | 48.29 | 45.17 | 15.04 | 18.62 | 16.53 | 6.06 | 7.80 | 7.54
Total Pairs (Chariot) | 20 | 20 | 10 | 40 | 80 | 40 | 160 | 320 | 160 | 200 | 500 | 200 | 300 | 500 | 200

## Slide 21: Raw #s – VHT80 Aggregate
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
1SS Phone_VHT80_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 220.46 | 246.25 | 126.73 | 213.07 | 275.54 | 185.95 | 227.21 | 258.34 | 204.76 | 212.84 | 222.47 | 196.85 | 162.52 | 173.25 | 167.56
Run 2 | 216.36 | 241.43 | 134.03 | 213.39 | 270.75 | 183.26 | 227.08 | 245.50 | 210.13 | 207.86 | 223.16 | 197.37 | 161.81 | 163.91 | 172.42
Run 3 | 217.06 | 245.64 | 116.96 | 215.38 | 270.27 | 196.29 | 225.88 | 253.17 | 219.53 | 208.97 | 225.67 | 196.30 | 168.00 | 177.94 | 147.40
Average Throughput | 217.96 | 244.44 | 125.90 | 213.95 | 272.19 | 188.50 | 226.72 | 252.34 | 211.47 | 209.89 | 223.77 | 196.84 | 164.11 | 171.70 | 162.46
Total Pairs (Chariot) | 2 | 4 | 2 | 5 | 20 | 5 | 10 | 40 | 10 | 25 | 100 | 25 | 50 | 200 | 50
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
2SS Laptop_VHT80_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 603.43 | 645.31 | 638.99 | 571.41 | 625.50 | 629.20 | 534.85 | 620.51 | 597.08 | 430.53 | 551.49 | 515.60 | 362.78 | 462.09 | 436.90
Run 2 | 609.79 | 651.10 | 637.93 | 569.64 | 625.59 | 623.25 | 533.58 | 617.22 | 589.33 | 432.61 | 555.53 | 516.43 | 366.83 | 465.84 | 435.75
Run 3 | 605.97 | 647.66 | 638.31 | 568.74 | 626.44 | 628.82 | 535.48 | 618.95 | 596.11 | 431.29 | 550.55 | 519.93 | 364.56 | 463.24 | 437.95
Average Throughput | 606.40 | 648.02 | 638.41 | 569.93 | 625.84 | 627.09 | 534.64 | 618.89 | 594.17 | 431.48 | 552.52 | 517.32 | 364.72 | 463.72 | 436.87
Total Pairs (Chariot) | 10 | 20 | 10 | 40 | 40 | 20 | 120 | 160 | 80 | 200 | 300 | 200 | 300 | 300 | 200
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
3SS Laptop_VHT80_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 810.73 | 908.15 | 884.17 | 739.54 | 895.69 | 850.20 | 700.06 | 887.33 | 808.69 | 589.02 | 787.17 | 690.54 | 489.60 | 591.34 | 587.74
Run 2 | 809.78 | 912.09 | 891.06 | 738.70 | 899.57 | 853.93 | 705.84 | 881.02 | 801.76 | 599.64 | 779.39 | 695.41 | 507.39 | 594.88 | 591.53
Run 3 | 817.96 | 916.03 | 892.52 | 714.49 | 890.43 | 857.77 | 701.10 | 879.42 | 803.87 | 594.44 | 777.23 | 692.84 | 489.57 | 584.44 | 584.04
Average Throughput | 812.83 | 912.09 | 889.25 | 730.91 | 895.23 | 853.96 | 702.33 | 882.59 | 804.78 | 594.37 | 781.26 | 692.93 | 495.52 | 590.22 | 587.77
Total Pairs (Chariot) | 20 | 20 | 10 | 80 | 80 | 40 | 240 | 320 | 160 | 400 | 500 | 200 | 300 | 500 | 400

## Slide 22: Raw #s – VHT80 Per Client
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
1SS Phone_VHT80_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 220.46 | 246.25 | 126.73 | 42.61 | 55.11 | 37.19 | 22.72 | 25.83 | 20.48 | 8.51 | 8.90 | 7.87 | 3.25 | 3.47 | 3.35
Run 2 | 216.36 | 241.43 | 134.03 | 42.68 | 54.15 | 36.65 | 22.71 | 24.55 | 21.01 | 8.31 | 8.93 | 7.89 | 3.24 | 3.28 | 3.45
Run 3 | 217.06 | 245.64 | 116.96 | 43.08 | 54.05 | 39.26 | 22.59 | 25.32 | 21.95 | 8.36 | 9.03 | 7.85 | 3.36 | 3.56 | 2.95
Per Client Throughput | 217.96 | 244.44 | 125.90 | 42.79 | 54.44 | 37.70 | 22.67 | 25.23 | 21.15 | 8.40 | 8.95 | 7.87 | 3.28 | 3.43 | 3.25
Total Pairs (Chariot) | 2 | 4 | 2 | 5 | 20 | 5 | 10 | 40 | 10 | 25 | 100 | 25 | 50 | 200 | 50
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
2SS Laptop_VHT80_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 603.43 | 645.31 | 638.99 | 114.28 | 125.10 | 125.84 | 53.49 | 62.05 | 59.71 | 17.22 | 22.06 | 20.62 | 7.26 | 9.24 | 8.74
Run 2 | 609.79 | 651.10 | 637.93 | 113.93 | 125.12 | 124.65 | 53.36 | 61.72 | 58.93 | 17.30 | 22.22 | 20.66 | 7.34 | 9.32 | 8.72
Run 3 | 605.97 | 647.66 | 638.31 | 113.75 | 125.29 | 125.76 | 53.55 | 61.89 | 59.61 | 17.25 | 22.02 | 20.80 | 7.29 | 9.26 | 8.76
Per Client Throughput | 606.40 | 648.02 | 638.41 | 113.99 | 125.17 | 125.42 | 53.46 | 61.89 | 59.42 | 17.26 | 22.10 | 20.69 | 7.29 | 9.27 | 8.74
Total Pairs (Chariot) | 10 | 20 | 10 | 40 | 40 | 20 | 120 | 160 | 80 | 200 | 300 | 200 | 300 | 300 | 200
 | 1 | Clients |  | 5 | Clients |  | 10 | Clients |  | 25 | Clients |  | 50 | Clients | 
3SS Laptop_VHT80_TCP | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect | Down | Up | Bidirect
Run 1 | 810.73 | 908.15 | 884.17 | 147.91 | 179.14 | 170.04 | 70.01 | 88.73 | 80.87 | 23.56 | 31.49 | 27.62 | 9.79 | 11.83 | 11.75
Run 2 | 809.78 | 912.09 | 891.06 | 147.74 | 179.91 | 170.79 | 70.58 | 88.10 | 80.18 | 23.99 | 31.18 | 27.82 | 10.15 | 11.90 | 11.83
Run 3 | 817.96 | 916.03 | 892.52 | 142.90 | 178.09 | 171.55 | 70.11 | 87.94 | 80.39 | 23.78 | 31.09 | 27.71 | 9.79 | 11.69 | 11.68
Per Client Throughput | 812.83 | 912.09 | 889.25 | 146.18 | 179.05 | 170.79 | 70.23 | 88.26 | 80.48 | 23.77 | 31.25 | 27.72 | 9.91 | 11.80 | 11.76
Total Pairs (Chariot) | 20 | 20 | 10 | 80 | 80 | 40 | 240 | 320 | 160 | 400 | 500 | 200 | 300 | 500 | 400

## Slide 23: Call to Action
Adapt Box 3 simulators to create a special case of SS#2 that reflects our VHD lab setup and test sequence
Compare simulation results against empirical data
Results should be no worse than these numbers
Significantly higher numbers should be investigated
We are interested in your assessment of the mechanics of the contention premium.