## Slide 1: EPD for IEEE 802.11 5.9GHz Operations
Date: 2014-11-5
Authors:
Nov 2014
Date: 2014-11-5

## Slide 2: Abstract
Background
Rationale for switching from LLC Protocol Discrimination (LPD) to EtherType Protocol Discrimination (EPD) in the IEEE 802.11 5.9 GHz bands
Current status of implementations and support
Nov 2014

## Slide 3: Background
From their inception, 802.2 (LLC) and 802.3 (L/T aka Ethernet) have been and continue to be incompatible layer-2 (LLC-sublayer) protocols.
Somewhere between 1999 and 2007, IEEE 802.11 specifically designated LLC (as defined in 802.2) as the Logical Link Control sublayer protocol to be used in all 802.11 STAs.
Ethernet now dominates the LAN market (FDDI and Token Ring are disappearing)
Slide 3
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 3

## Slide 4: Background
IEEE 802.2 was withdrawn in 2011 and is no longer supported by IEEE (ISO maintains a “stabilized” version in ISO/IEC 8802-2:1998)
IEEE 802-2014 Overview and Architecture explicitly discourages the use of 802.2 LLC in the future.
  “New IEEE 802 standards shall support protocol discrimination in the LLC sublayer using EPD.”
Slide 4
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 4

## Slide 5: Background
The use of EtherTypes instead of DSAP/SSAP addresses as network layer protocol identifiers means LLC SNAP/RFC1042 has to be used (cf. IEEE 802.11)
As a consequence, six (6) octets of fixed content (and therefore useless) are transmitted in every over-the-air stream.
Slide 5
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 5

## Slide 6: Background
Slide 6
LLC-sublayer 802.2 (LPD) header format (LLC SNAP RFC1042)
Length/Type encoding (EPD) header format
Length < 1503 (0x05DF)
Ethertype > 1535 (0x05FF)
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 6

## Slide 7: Rationale
There are currently no commercial deployments of IEEE 802.11 5.9 GHz units/systems (only prototype units in trials); hence the 5.9 GHz MAC/PHY can be considered to be “new”.
Therefore, EPD should be used because it is:
  more efficient (6 bytes saved in every data frame)
  “compatible” with 802.3 ethernet LANs and 802.1Q bridges
  compatible with GLK (EPD) operation (when standardization is complete)
  IEEE 802-2014 mandates it!
Slide 7
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 7

## Slide 8: Current Implementations
4 vendors of 5.9 GHz (11p) radio units have made and successfully tested the change (< 2 man-hours of effort)
  Q-Free
  Commsignia
  Savari Networks
  Arada Systems
Slide 8
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 8

## Slide 9: Current Implementations
4 vendors of 5.9 GHz (11p) radio units have made and successfully tested the change (< 2 man-hours of effort)
  Q-Free
  Commsignia
  Savari Networks
  Arada Systems
Slide 9
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 9

## Slide 10: Current Implementations - LPD (before)
Slide 10
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 10

## Slide 11: Current Implementations - EPD (after)
Slide 11
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 11

## Slide 12: Current Support
Several other vendors have indicated support for the change
In October 2014, TC 204 passed the following resolution:
“Resolution 1072:
ISO/TC 204 resolves to support a change from LPD
to EPD in the 802.11 specifications for 5.9 GHz frequency bands.
APPROVED”
Slide 12
Nov 2014
Notes: doc.: IEEE 802.11-yy/0339r0
Month Year
John Doe, Some Company
Page 12