## Slide 1: Modeling components impacting throughput gain from CCAT adjustment
Date: 2015-01-11
Authors:

## Slide 2: Background
Some contributions show moderate gains from Clear Channel Assessment Threshold (CCAT) adjustment
  “DSC performance” [1] shows < 50% in both average and 5th percentile
Other contributions show much higher gains
  “Performance Gains from CCA Optimization” [2] indicates ~200% gain in average throughput
Question to answer:
  What are the important modelling components needed to get a more realistic estimation of the gain by adjusting CCAT?

## Slide 3: Background
Simplified traffic modeling used
  Full buffer DL only
Compare the effect of the following modeling components
Component | Simplified | Realistic
Spatial streams | 1 (SISO) | 1 to 2 (MIMO)
Link adaptation | “Ideal” | ACK-based
Preamble reception | Always received and decoded | In some cases not received or decoded

## Slide 4: Simulation scenario 2
“Enterprise Scenario” as defined in [3]
  8 offices, 64 cubicles per office, 2 STAs per cubicle
    (8 × 64 × 2) / 32 = 32 STA/AP
  4 × 80MHz channels (8 APs on the same channel)
    32 × 8 = 256 STAs on the same channel
  P2P links are not included in the simulation
DL full buffer traffic

## Slide 5: Simplified modelling components
SISO
‘Ideal’ link adaptation
  SINR@Receiver before transmission used to set MCS
Preamble Reception
  Ideal PLCP preamble decoding
    When two preambles arrive at the same time, both can be decoded
  802.11 OFDM signal always identified
    Even if PLCP has already been transmitted when the sensing starts
    In the simplified modeling CCA-SD (preamble detection) threshold is always used, although CCA-ED threshold should be used in case the preamble is not decoded
AP A
AP B
Payload
Preamble
Sensing
Payload
Preamble
AP A
AP B
Preamble
Payload

## Slide 6: More realistic modelling components
MIMO
Link adaptation
  Adaptive auto-rate fallback
Preamble Reception:
  PLCP preamble decoding
    When two preambles arrive at the same time, both can be decoded only if SINR is sufficiently high
  802.11 signal may not be identified
    If a preamble can not be detected, CCA-ED will be used
AP A
AP B
Payload
Preamble
Sensing
Payload
Preamble
AP A
AP B
Preamble
Payload

## Slide 7: Average throughput gain
Figure shows gain in average throughput for different CCAT compared to -82 dBm
Large gains with simplified modeling
Very small gains with more realistic modeling

## Slide 8: Modeling impact on throughput
-82 vs. -50 dBm CCAT: gain in average user throughput varies from 6% to 137%
Model analysis for gain from reduced CCAT:
  MIMO: high SINR with -82 dBm can not be fully utilized by SISO transmission,  higher user throughput @ -82 dBm
  LA: lower user throughput @ -50 dBm due to larger variations in interference
  PR: higher user throughput @ -82 dBm since the ED threshold (-62 dBm) is applied when an interferer’s preamble is not correctly decoded
Moving from simplified to more realistic modeling:
  Higher throughput @ -82 dBm and lower throughput @ -50 dBm
  The gain between -82 dBm and -50 dBm is reduced, compared to the simplified modeling gain
-82 dBm
-50 dBm
0
2
4
6
8
10
Average user throughput (Mb/s)
LA: link adaptation PR: preamble reception (detection & decoding)
MIMO
PR
LA
Ideal,SISO
Ideal,MIMO
Non-ideal LA,MIMO
Non-ideal PR,MIMO
Non-ideal LA+PR,MIMO

## Slide 9: Simplified models
Ideal LA & PR, SISO
Gain in average user throughput: 137%
  Gain in spatial reuse measured by AP transmitting time: 242%
  Loss in transmission rate: 21%
  Loss due to increased packet loss: 5%
-82 dBm
-70 dBm
-50 dBm
0
0.2
0.4
0.6
0.8
AP state ratio
Defer
Receive
Transmit
-82 dBm
-70 dBm
-50 dBm
0
2
4
6
8
Average MCS rate
(bits/symbol)
Relative value: 1 0.99487 0.79235

## Slide 10: More realistic models
Non-ideal LA & PR, MIMO
Gain in average user throughput: 6%
  Gain in spatial reuse measured by AP transmitting time: 178%
  Loss in transmission rate: 40%
  Loss due to increased packet loss : 40%
-82 dBm
-70 dBm
-50 dBm
0
0.2
0.4
0.6
0.8
AP state ratio
Defer
Receive
Transmit
-82 dBm
-70 dBm
-50 dBm
0
2
4
6
8
10
12
Average MCS rate
(bits/symbol)
Relative value: 1 0.95391 0.59807

## Slide 11: Summary
Factors limiting user throughput gain with CCAT adjustment are identified
With SISO and ideal modeling assumptions, high gain has been shown
The gain in average user throughput of adjusted CCAT is reduced significantly after adding:
  MIMO transmission (improves baseline)
  Adaptive auto rate fallback link adaptation
  Realistic preamble detection and decoding
Analysis was done for full buffer DL-only traffic, for realistic gain estimation realistic traffic model with mix of DL and UL traffic should be considered
Adjusted CCAT or DSC provides system improvements [1] but more realistic modeling is important to avoid overestimation of gains

## Slide 12: References
[1] 11-14/1427r2, “DSC Performance”
[2] 11-14/0889r3, “Performance Gains from CCA Optimization”
[3] 11-14/0980r5, “TGax Simulation Scenarios”