## Slide 1: Text Update on PHY Abstraction and SP
Date: 2015-01-12
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com
Jiyong Pang Jiayin Zhang | Huawei |  |  | 
Xiaofei WANG | InterDigital Communications, Inc. | 2 Huntington Quadrangle Melville, NY 11747 |  | xiaofei.wang@interdigital.com
Wookbong Lee | LG |  |  | 
Bo Sun Ke Yao | ZTE |  |  | 

## Slide 2: Discussion on Time-Varying Interference Modeling PHY Abstraction
Modeling of time-varying interference for PHY abstraction in SLS is open in [1] and has been discussed in [2,3,4]
  Different modeling methods have been proposed and evaluated.
  The simplified version of block-wise PHY abstraction has been agreed in offline discussions.
  Within this interference event, the desired signals and the interferences are assumed to be static. So channel generation and SINR calculation can be done over 1 OFDM symbol within this event.

## Slide 3: Further Discussions on Modeling of Non-overlapped OFDM Symbols
Since WiFi networks are asynchronous, signals may not be aligned on OFDM symbol boundaries.
  Some OFDM symbols are fully overlapped with this interference, the starting/end OFDM symbol are only partially overlapped.
Performance is dominated by the weakest link, or the most interfered part.
  Within the most interfered event, the fully overlapped OFDM symbols are then mostly interfered and the performance is dominated by those symbols.
For simplicity, propose to use 1 (e.g. the first) fully overlapped OFDM symbol for SINR calculation in each event.
  Assume signals are synchronous on OFDM symbol boundaries with in each event.
  Ignore the complicated modeling of ISI/ICI in the received interfering signals.

## Slide 4: Proposed Text Change in [1]
Propose the text change in [1] regarding the modeling of the time-varying and asynchronous interference.

## Slide 5: Conclusion
Proposed the simplified version of modeling of time-varying interference.
Proposed the modeling of asynchronous interference.
Proposed text change in [1] to complete the PHY abstraction procedure.

## Slide 6: Reference
[1] 11-14-0571-03-00ax-evaluation-methodology
[2] 11-14-1174-00-00ax-PHY-abstraction-for-time-varying-interference
[3] 11-14-1418-01-00ax-further-study-of-time-varying-interference-and-phy-abstraction
[4] 11-14-1388-01-00ax-consideration-on-per-prediction-for-phy-abstruction

## Slide 7: Straw Poll
Do you support to update the PHY abstraction procedure in 11/14/0571r6 to:

## Slide 8: Motion
Move to update the PHY abstraction procedure in 11-14/0571r6 Appendix 1 to: