## Slide 1: TGax SLS MAC Calibration Test 4 Results
Date: 2015-1-12
Authors:

## Slide 2: Background
MAC Calibration is ongoing as part of SLS [1].
4 total calibration tests are included in the MAC calibration spec [2].
Test 4 is designed for scenarios where two BSSs have different channel bandwidth [2][3].
  The first BSS operates in 40 MHz channel
  The second BSS operates in a 20MHz channel which is the secondary channel of the first BSS.
  The 40MHz BSS is running full buffer.
  The 20MHz BSS is generating Poisson traffic with lamda = 100.
  MSDU size 2000 bytes.

## Slide 3: Test Results
RTS/CTS | BSS2 channel | Backoff | Aggregation | MCS | MSDU size | MAC PER | Application Throughput | Channel Occupancy
OFF | 1 | ON | ON | MCS 0 | 2000 | N/A | 8.10664 | N/A
 |  |  |  |  |  | N/A | 1.52189 | N/A
ON | 1 | ON | ON | MCS 0 | 2000 | N/A | 7.76083 | N/A
 |  |  |  |  |  | N/A | 1.30356 | N/A

## Slide 4: Detailed Settings
Secondary channel CCA is assumed.
A-MPDU size - , (Number of MPDUs in AMPDU= 2)
Traffic category, BSS1: AC_BE, BSS2: AC_BE
  MAC header 30 bytes
  L4 header: 36 bytes
SIFS= 16us

## Slide 5: Test Objectives
Airtime sharing by two BSSs with different channel bandwidth
Throughput performance under this circumstance
PER performance under this circumstance
Calibrate with other companies/simulators

## Slide 6: Conclusion
Provide the test 4 results of SLS MAC calibration
To complete the missing part of the test very soon.

## Slide 7: Reference
  [1]. Doc. IEEE 802.11-14/0571r5 11ax evaluation methodology
  [2]. Doc. IEEE 802.11-14/0621r4 / Doc. IEEE 802.11-14/0980r4 ax Simulation scenarios
  [3]. Doc. IEEE 802.11-14/0895r1 Calibration of MAC simulator with OBSS Network Scenario