## Slide 1: Spatial Reuse AP Management
Date: 2015-01-11
Authors:

## Slide 2: Abstract
Multiple different versions of spatial reuse via variations in CCA rules have been proposed for 11ax. For purposes of this presentation, these variations include dynamic sensitivity control, and revised / variable / adaptive / dynamic CCA thresholds.
Without distinguishing between these, it is proposed that the final version should be parameterized, and the parameters should be configurable (to some extent) by the AP.

## Slide 3: Summary
Many different approaches to spatial reuse have been proposed, discussed, and evaluated for 11ax
  These include dynamic sensitivity control (DSC), and revised, adaptive, dynamic, signaled, and link-aware CCA threshold
  There are several subvariants with extra parameters to specify (‘margin’ and others)
Evaluations of achievable gains vary widely
  At the very least, it is clear that there is no “one-size-fits-all” approach that works well in all environments and for all devices, for any of these approaches
Enabling a degree of configurability benefits all approaches
  The principle of configurability is well established in 802.11, e.g., EDCA
  In any approach, standard could predefine permissible choices and conditions, with defaults
  Enables adaptation to highly varied deployments, managed v. unmanaged, etc.

## Slide 4: Spatial reuse / dynamic CCA taxonomy
Dynamic Sensitivity Control (DSC)
  Sensitivity modified based on RSSI modified by ‘Margin’ [3-6, 9, 12, 17-19, 24-26]
Revised / Variable / Dynamic / Signaled / Per-Link CCA *
  Revised CCA: CCA Threshold redefined for 11ax devices; with use of ‘BSS Color’
  Variable CCA: CCA Threshold variable for 11ax devices, centrally managed
  Dynamic CCA: CCA Threshold may change dynamically for 11ax devices
  Signaled CCA: CCA Threshold may be modified by transmitting device
  Per-Link CCA: CCA Threshold optimized on a per-link basis
    [1, 2, 7, 8, 10, 11, 13-16, 20-23, 26-28]
TGax has not yet standardized terminology;
these variations appear under different names

## Slide 5: Configurability
Commonalities
  All these algorithms have aspects in common
  CCA Threshold, and/or Receiver Sensitivity (and/or Transmit Power) are modified
  The remaining questions are how, when, and by whom
A common baseline
  Given the commonalities, it’s useful to consider SFD text that is applicable for each
  Each approach can benefit from reuse of established and well-proven principles of the underlying standard
  In particular it is useful to allow APs the ability and flexibility (within appropriate limits) to manage their BSSs and optimize for varying conditions:
    APs should have the ability to set spatial reuse parameters for the BSS
  Accepting this principle at the outset avoids extended debates between approaches that are in essence identical, and enables constructive progress

## Slide 6: Straw polls
Straw poll 1:
  Do you agree with adding the following text to the 11ax SFD?:
  “The 11ax amendment shall define a Spatial Reuse Parameters Set element to be included in beacon and probe responses, analogous to the EDCA Parameter Set element”
Straw poll 2:
  Do you agree with adding the following text to the 11ax SFD?:
  “The 11ax amendment shall define spatial reuse parameters carried in a Spatial Reuse parameters frame, analogous to the individually addressed quality-of-service management frame (IQMF [11ae])”

## Slide 7: References—I
“Improved Spatial Reuse Feasibility – Part I”, Ron Porat, Nihar Jindal (Broadcom), doc. IEEE 802.11-14/0082r0, January 2014.
“Improved Spatial Reuse Feasibility – Part II”, Ron Porat, Nihar Jindal (Broadcom), doc. IEEE 802.11-14/0083r0, January 2014.
“DSC Channel Selection and Legacy Sharing”, Graham Smith (DSP Group), doc. IEEE 802.11-14/0294, March 2014.
“Dynamic Sensitivity Control for HEW”, Graham Smith (DSP Group), doc. IEEE 802.11-13/1290r1, April 2014.
“Dynamic Sensitivity Control Implementation”, Graham Smith (DSP Group), doc. IEEE 802.11-14/0635r1, May 2014.
“DSC Practical Usage”, Graham Smith (DSP Group), doc. IEEE 802.11-14/0779r2, July 2014.
“Measurements on CCA Thresholds in OBSS Environment”, John (Ju-Hyun) Son, Jin Sam Kwak (WILUS Institute), Young Doo Kim, Hong Seok Shin (SK Telecom), doc. IEEE 802.11-14/0628r0, May 2014.
“Residential Scenario CCA/TPC Simulation Discussion”, Frank LaSita, Pengfei Xia, Joseph Lev (Interdigital), doc. IEEE 802.11-14/0578r0, May 2014.
“DSC and Legacy Coexistence,” Yuichi Morioka (Sony), et al., doc. IEEE 802.11-14/0854r0, July 2014.
“Evaluating Dynamic CCA/Receiver Sensitivity Algorithms”, Brian Hart (Cisco), et al., doc. IEEE 802.11-14/0856r0, July 2014.

## Slide 8: References—II
11. “A Protocol Framework for Dynamic CCA”, Sean Coffey (Realtek), et al., doc. IEEE 802.11-14/0872r0, July 2014.
12. “DSC Simulation Results for Scenario 3”, Masahito Mori (Sony) ,et al., doc. IEEE 802.11-14/1171r1, September 2014.
13. “CCA Study in Residential Scenario - Part 2”, Gwen Barriac (Qualcomm), et al., doc. IEEE 802.11-14/1199r1, September 2014.
14. “Link Aware CCA”, Brian Hart (Cisco), doc. IEEE 802.11-14/1224r0, September 2014.
15. “Considerations on CCA for OBSS Opearation in 802.11ax”, Jun Luo (Huawei), doc. IEEE 802.11-14/1225r0, September 2014.
16. “Adaptive CCA for 11ax”, Reza Hedayat, Young Hoon Kwon (Newracom), et al. doc. IEEE 802.11-14/1233r2, September 2014.
17. “Observed Protocol Violations Caused by DSC for Roaming STAs”, Chuck Lukaszewski (Aruba), doc. IEEE 802.11-14/1416r1, November 2014.
18. “DSC and Legacy Coexistence”, Gustav Wikstrom (Ericsson), et al., doc. IEEE 802.11-14/1426r2, November 2014.
19. “DSC Performance,” Gustav Wikstrom (Ericsson), et al., doc. IEEE 802.11-14/1427r0r2, November 2014.
20. “Considerations on OBSS Spatial Reuse”, Jianhan Liu (Mediatek), et al., doc. IEEE 802.11-14/1435r1, November 2014.

## Slide 9: References—III
21. “Adapting CCA and Receiver Sensitivity”, Esa Tuomaala (Nokia), et al., doc. IEEE 802.11-14/1443r0, November 2014.
22. “Considerations for Adaptive CCA”, Reza Hedayat (Newracom) ,et al., doc. IEEE 802.11-14/148r0, November 2014.
23. “Perspectives on Spatial Reuse in 11ax”, Reza Hedayat (Newracom), et al., doc. IEEE 802.11-14/1580r0, December 2014.
“DSC and Roaming”, Graham Smith (SRT), doc. IEEE 802.11-15/0025r0, January 2015.
“Simulation Based Evaluation DSC in residential scenario”, M. Shahwaiz Afaqui (UPC), et al. doc. IEEE 802.11-15/0027r0, January 2015.
“Performance Analysis of BSS Color and DSC”, Masahito Mori (Sony), doc. IEEE 802.11-15/0045r0, September 2014.
“Modeling components impacting throughput gain from CCAT adjustment”, Yu Wang (Ericsson), et al. doc. IEEE 802.11-15/0050r0, January 2015.
28. “Legacy Fairness Issues of Enhanced CCA”, John Son (WILUS), et al. doc. IEEE 802.11-15/0085r0, January 2015.