## Slide 1: Sleep States in IEEE 802.11ax Simulation Scenarios
Date: 2015-03-09
Authors:

## Slide 2: Contents of this Contribution
Motivation for sleep states definition
Need for refinement of current sleep state
Sleep state classification
Various sleep state illustrations
Comparison of power and latency requirements for sleep states

## Slide 3: Scenario of 802.11ax Densification
BSS 1
BSS 2
BSS 3
BSS 4
Communicating link
Interfering link
OBSS Interference
STA 1
STA 2
STA 3
STA 4
AP 1
AP 2
AP 3
AP 4
Reception of a BU at STA 1 from
AP 1 interfered by several UL
traffic from STAs 2, 3, and 4

## Slide 4: Motivation for Various Sleep States Definition
Simulation Scenarios document [1] of IEEE 802.11ax specifies the following common power model parameters for all simulation scenarios
  Sleep power state is defined as the state when the STA is in Doze state and receiver is off
Refinement of current sleep state to suit the network condition due to densification and low power operation
  We propose to define various sleep states where the receiver is partial or completely turned down
  We intend to include the proposed sleep states in the Simulation Scenarios document under Common Power Model Parameters for all simulation Scenarios [1]
Power State | Average Current Consumption [mA]
Transmit [mA] | 280
Receive [mA] | 100
Listen [mA] | 50
Sleep [mA] | 0.003 [2]

## Slide 5: Need for Refinement of Current Sleep State
Wi-Fi devices with various form factors
  Multitude of transmit power constraints
  Battery size requires different power consumption needs
General categorization of sleep state may not be sufficient
  Different power management or power save protocols allow distinct short or long sleep times
  Constrained on power efficiency due to activation requirements of RF and baseband processors
  Leads to trade-off between performance and energy efficient WLANs
Traffic models and latency requirements
  Sleep distribution based on disparate traffic models (bursty versus periodic, short or long packets, etc.)
  Multiple levels of sleep mode needed due to stringent (e.g., multimedia streaming, video conferencing) versus flexible (low duty cycle of UL or DL traffic) latency requirements

## Slide 6: Sleep State Classification
Micro sleep state – Decode the PHY Preamble and determine it is not a relevant packet and enter this sleep state for the duration of the PPDU; e.g., duration of a single UL or DL packet, spatial re-use in OBSS;
Shallow sleep state – Determine the protection duration from the first packet and enter this sleep state till end of that duration; e.g., TXOP duration
Deep sleep state – Sleep state over one or multiple beacon intervals
AP 1
STA 1
DL BU
Receive state
STA 2
Micro sleep state
ACK
UL Data
TXOP
Shallow sleep state
Deep sleep state
AP 2
Length of PPDU

## Slide 7: Comparison of Power and Latency Requirements Among Different Sleep States
Micro sleep state: MAC processor powered up, faster clock running, PLL ON, some leakage
  Power consumption around 5mW
  Latency to return to active state: 0-100us
  RF and modem OFF
Shallow sleep state: MAC processor in retention mode, slower clock running, PLL in low power mode, some leakage
  Power consumption around 1mW
  Latency to return to active state: < 500us
  RF and modem OFF
Deep sleep state: Wi-Fi power supply OFF
  Power consumption around 0-100uW
  Latency to return to active state: >3ms

## Slide 8: Proposal to Include Sleep States in IEEE 802.11ax Simulation Scenarios document
Sleep State Power and Latency Values |  | 
Sleep State | Power Consumption | Latency from sleep mode to active state
Micro Sleep | 5mW | 100us
Shallow Sleep | 1mW | 500us
Deep Sleep | 0.003mW [2] | 3ms
Propose to include the following Table for 3 sleep states under Common Power Model Parameters for all simulation Scenarios in Simulation Scenarios document doc. IEEE 802.11-14/0980r6 [1]

## Slide 9: Summary
We have presented the need for refinement of current sleep state for Wi-Fi devices in IEEE 802.11ax
We have proposed three sleep states based on the duration of sleep
  Micro sleep
  Shallow sleep
  Deep sleep
Finally, we have proposed to modify the Simulation Scenarios by including a table specifying the 3 sleep states for better power and latency modeling

## Slide 10: References
[1] IEEE 11-14/0980r6: TGax Simulation Scenarios
[2] IEEE 11-14/1444r2: Energy Efficiency Evaluation and Simulation Model

## Slide 11: Straw poll 1
Do you agree to define 3 sleep states defined in Slide 6 for the sleep state mentioned in the Simulation Scenarios document?

## Slide 12: Straw poll 2
Do you agree to include the table in Slide 8 under Common Power Model Parameters for all simulation Scenarios in the Simulation Scenarios document?