## Slide 1: Bandwidth granularity on UL-OFDMA data allocation
Date: 2015-03-11
Authors:

## Slide 2: Introduction
UL-OFDMA is included in Spec Framework Document for 11ax [1],[2]
  Key enabling technique to meet the requirement of throughput enhancement
  Unlike the conventional 802.11, simultaneous transmission of multiple STAs should be supported
  It is necessary to decide how to support multiple UL data for further developing UL-OFDMA procedure
Bandwidth granularity of multiple UL data allocation
  Considering wideband, larger FFT size
20MHz based or sub-channel based channel occupation

## Slide 3: UL-OFDMA procedure
Initiation (AP)
  UL-OFDMA procedure start indication
  Synchronization of UL-OFDMA procedure
  Channel availability indication of AP
  Duplicated for available channel from AP’s perspective
Scheduling (AP, STAs)
  STA
    Medium contention (Resource request)
    UL-data length and AC indication
    Channel availability indication of STAs
  AP
    Resource (Channel) allocation
  Explicit or implicit

## Slide 4: How do we develop UL-OFDMA procedure?
The very first step of designing UL-OFDMA
Procedural detail may vary depending on the target environment/situation/traffic/STA
Among these ingredients, we more focus on how many STAs can be allowed in a single UL-OFDMA session
  The granularity of bandwidth occupation will determine the number of tx-STA of UL-OFDMA

## Slide 5: Multiple STAs’ UL bandwidth occupation in UL-OFDMA
In conventional 802.11, minimum bandwidth occupation is 20MHz
  Only one tx-STA is allowed
  Control mechanism/signaling/frame structure have been designed based on 20MHz channel
DL-OFDMA of 11ax is considering to support finer granularity of bandwidth occupation [3], [4], [5], [6]
  Smaller minimum bandwidth occupation (1/2, 1/4, 1/8 of 20MHz )
Finer bandwidth occupation could also be considered for UL-OFDMA
  Multiple non-AP STAs to 1 AP
  It may requires new design or great modifications on current protocols
Two possible options for bandwidth occupation in UL-OFDMA
  20MHz based/sub-channel based bandwidth occupation

## Slide 6: 20MHz based UL-OFDMA
Only 1 STA per 20MHz channel
  The number of UL STAs is the same as available channel of AP
  The winner of contention at each channel will become UL STA
    Similar to conventional 802.11 medium contention
  Less complexity, little modification
  Relatively short scheduling duration per UL-OFDMA session
Assigned STA may exploit the control information in L/HE preamble exclusively
  Easier to design and implement

## Slide 7: 20MHz based UL-OFDMA –drawbacks (1)
Little contention isolation gain
  Contention isolation is the most powerful feature of OFDMA
  There isn’t much room for multiplexing UL data
  No contention isolation gain for single 20MHz channel
The smaller data size, the less spectral efficiency
  Spectral efficiency: Tdata/(Tdata +Toverhead)
  UL-OFDMA may introduce increased overhead (e.g., initiation, scheduling)
  Traffic measurement on packet size reveals that packet size is <66B with >75% chance for UL [7]
  The proportion of system overhead will increase with small-sized UL data

## Slide 8: 20MHz based UL-OFDMA –drawbacks (2)
Inflexible and inefficient resource allocation
  AP cannot transmit ACK while it receives UL data on different channels
  Every UL data must be timely aligned (e.g., zero padding, data repetition)
  The greater difference of UL data size, the less spectral efficiency

## Slide 9: Sub-channel based UL-OFDMA
Multiple UL STAs on a single channel
More contention isolation gain
  The ratio of contention and collision increases drastically as the network gets denser[8]
  The number of contention period could be reduced by the number of UL STAs
  Advantageous especially for denser network with more saturated traffic
More spectral efficiency
  The airtime of UL data will increase as the occupied bandwidth gets narrower
  The ratio of system overhead to data will decrease

## Slide 10: Sub-channel based UL-OFDMA
More flexibility in resource allocation
  Depending on the UL data size of each STA, different size of sub-channels can be assigned
  Less zero padding or data repetition is required for time alignment of data period
Sub-channel based UL-OFDMA seems more preferable in terms of Tput enhancement
There are some issues and concerns on implementing sub-channel based UL-OFDMA

## Slide 11: L-preamble transmission
L-preamble should be sent on 20MHz channel with 64 FFT size
  Designed for delivering common control information of a single transmitter
  Necessary to define how to deal with it for UL data transmission of multiple STAs
1. A chosen STA transmits L-preamble as a representative of the PPDU
  Synchronization might get trickier, as multiple STAs starts to transmit different points of time
2. Every STA sends identical L-preamble
  Different delay spread might degrade the decoding performance
  Common control information should be shared among UL STAs in advance

## Slide 12: HE preamble structure for sub-channel based UL-OFDMA
HE-SIG A, designed based on 20MHz with common control information ①
  HE-SIG A might be transmitted by one chosen or every UL STA
  TX-specific information should be contained in latter field of HE preamble
L preamble and HE-SIG A might be dropped for UL data transmission ②
  Unnecessary to retransmit information that is already shared among every participant
  With proper protection mechanism from legacy STAs
  Corresponding information must be negotiated before data transmission
HE-SIG A might be designed with the minimum size of channel occupation ③
  TX-specific information might be included for every STA
  HE-SIG A for STA with multiple sub-channel might be duplicated on every assigned sub-channel
①
②
③

## Slide 13: Conclusion
UL-OFDMA is likely to become one of the most important feature of 11ax in terms of throughput enhancement
Making decision of granularity of bandwidth occupation might be the starting point for designing procedural detail of UL-OFDMA
We have discussed and compared 20MHz based / sub-channel based bandwidth occupation
In terms of Tput enhancement, sub-channel based UL-OFDMA seems more preferable
  Adjustment for sub-channel based operation should be followed

## Slide 14: References
[1][14/1453/r2] Spec Framework Proposal
[2][14/1447/r1] Proposed Spec Framework Document for 11ax considering potential tech features
[3] [14/1452/r0] Frequency selective scheduling in OFDMA
[4] [15/0082/r1] Considerations on 11ax OFDMA Frequency Granularity
[5] [15/0305/r0] Effective Subcarrier Assignment for DL-OFDMA
[6] [15/0092/r1] DL-OFDMA Procedure in IEEE 802.11ax
[7] [14/1232/r1] On Multi-STA Aggregation Mechanisms in 11axOn Multi-STA Aggregation Mechanisms in 11ax
[8] Sakurai, Taka, and Hai L. Vu. "MAC access delay of IEEE 802.11 DCF."Wireless Communications, IEEE Transactions on 6.5 (2007): 1702-1710.

## Slide 15: Strawpoll
Do you agree to add to the TG Specification Frame work document?
x.y.z. HE-PPDU for UL-OFDMA shall support UL data transmission below 20MHz for an HE STA
Y/N/A